INTERNATIONAL ORGANISATION FOR STANDARDISATION

ORGANISATION INTERNATIONALE DE NORMALISATION

ISO/IEC JTC 1/SC 29/WG 11

CODING OF MOVING PICTURES AND AUDIO

ISO/IEC JTC 1/SC 29/WG 11 N15906

San Diego, CA, US – February 2016

| Source: | Leonardo Chiariglione |
| --- | --- |
| Title: | Report of 114th meeting |
| Status |  |

Report of 114th meeting

Annex A – Attendance list	2

Annex B – Agenda	3

Annex C – Input contributions	4

Annex D – Output documents	5

Annex E – Requirements report	6

Annex F – Systems report	7

Annex G – Video report	8

Annex H – JCT-VC report	9

Annex I – JCT-3V report	10

Annex J – Audio report	11

Annex K – 3DG report	12

# Opening

The 114th MPEG meeting was held in San Diego, CA, USA, 2016/02/22T09:00-26T20:00

# Roll call of participants

This is given in Annex 1

# Approval of agenda

Tha approved agenda is given in Annex 2

# Allocation of contributions

This is given in Annex 3

# Communications from Convenor

There was no communication

# Report of previous meetings

The following document was approved

| 15623 | Report of 113th meeting |
| --- | --- |

# Workplan management

### Media coding

### Profiles, Levels and Downmixing Method for 22.2 Channel Programs

The following document was approved

| 15999 | ISO/IEC 14496-3:2009/DAM 6, Profiles, Levels and Downmixing Method for 22.2 Channel Programs |
| --- | --- |

### Additional Levels and Supplemental Enhancement Information

The following documents were approved

| 16030 | Disposition of Comments on ISO/IEC 14496-10:2014/DAM2 |
| --- | --- |
| 16031 | Text of ISO/IEC 14496-10:2014/FDAM2 Additional Levels and Supplemental Enhancement Information |

### Progressive High 10 Profile

The following documents were approved

| 16032 | Request for ISO/IEC 14496-10:2014/Amd.4 |
| --- | --- |
| 16033 | Text of ISO/IEC 14496-10:2014/PDAM4 Progressive High 10 Profile, additional VUI code points and SEI messages |

### Printing material and 3D graphics coding for browsers

The following document was approved

| 16037 | Core Experiments Description for 3DG |
| --- | --- |

### Updated text layout features and implementations

The following documents were approved

| 15930 | Request for ISO/IEC 14496-22:2015 AMD 2 Updated text layout features and implementations |
| --- | --- |
| 15931 | Text of ISO/IEC 14496-22:2015 PDAM 2 Updated text layout features and implementations |

### Video Coding for Browsers

The Convenor recalled the ITTF letter giving instructions on handling Type 3 declaration that he had distributed on the livelink email system.

The most welcome clarification mandated that VCB activities should be stopped.

He also recalled that the Secretary had incredibly omitted to send the Convenor the Type 3 declaration that ITTF had sent to the Secretariat.

The Convenor also responded orally at the meeting and then in writing (m38221) to the FINB document (m38044).

### Internet Video Coding

The following documents were approved

| 16034 | Study Text of ISO/IEC DIS 14496-33 Internet Video Coding |
| --- | --- |
| 16035 | Internet Video Coding Test Model (ITM) v 14.1 |
| 16036 | Description of IVC Exploration Experiments |
| 16038 | Draft verification test plan for Internet Video Coding |

### MVCO Extensions on Time Segments and Multi-Track Audio

The following document was approved

| 15936 | WD of ISO/IEC 21000-19:2010 AMD 1 Extensions on Time Segments and Multi-Track Audio |
| --- | --- |

### Contract Expression Language

The following documents were approved

| 15937 | DoC on ISO/IEC DIS 21000-20 2nd edition Contract Expression Language |
| --- | --- |
| 15994 | Text of ISO/IEC IS 21000-20 2nd edition Contract Expression Language |

### Media Contract Ontology

The following documents were approved

| 15939 | DoC on ISO/IEC DIS 21000-21 2nd Media Contract Ontology |
| --- | --- |
| 15940 | Text of ISO/IEC IS 21000-21 2nd Media Contract Ontology |

### User Description

The following documents were approved

| 15941 | DoC on ISO/IEC DIS 21000-22 User Description |
| --- | --- |
| 15942 | Text of ISO/IEC IS 21000-22 User Description |

### FU and FN extensions for Parser Instantiation

The following documents were approved

| 16041 | Disposition of Comments on ISO/IEC 23002-4:2014/PDAM3 |
| --- | --- |
| 16042 | Text of ISO/IEC 23002-4:2014/DAM3 FU and FN descriptions for parser instantiation from BSD |

### Spatial Audio Object Coding

The following document was approved

| 16079 | Draft of ISO/IEC 23003-2:2010 SAOC, Second Edition |
| --- | --- |

### MPEG Surround Extensions for 3D Audio

The following document was approved

| 15934 | Study on ISO/IEC 23003-1:2007/DAM 3 MPEG Surround Extensions for 3D Audio |
| --- | --- |

### Support for MPEG-D DRC

The following documents were approved

| 16082 | DoC on ISO/IEC 23003-3:2012/DAM 3 Support of MPEG-D DRC, Audio Pre-Roll and IPF |
| --- | --- |
| 16083 | Text of ISO/IEC 23003-3:2012/FDAM 3 Support of MPEG-D DRC, Audio Pre-Roll and IPF |

### Parametric DRC, Gain Mapping and Equalization Tools

The following documents were approved

| 16085 | DoC on ISO/IEC 23003-4:2015 PDAM 1, Parametric DRC, Gain Mapping and Equalization Tools |
| --- | --- |
| 16086 | Text of ISO/IEC 23003-4:2015 DAM 1, Parametric DRC, Gain Mapping and Equalization Tools |

### Media Context and Control – Control Information

The following documents were approved

| 16109 | Request for ISO/IEC 23005-2 4th Edition Control Information |
| --- | --- |
| 16110 | Text of ISO/IEC CD 23005-2 4th Edition Control Information |

### Media Context and Control – Sensory Information

The following documents were approved

| 16111 | Request for ISO/IEC 23005-3 4th Edition Sensory Information |
| --- | --- |
| 16112 | Text of ISO/IEC CD 23005-3 4th Edition Sensory Information |

### Media Context and Control – Virtual World Object Characteristics

The following documents were approved

| 16113 | Request for ISO/IEC 23005-4 4th Edition Virtual world object characteristics |
| --- | --- |
| 16114 | Text of ISO/IEC CD 23005-4 4th Edition Virtual world object characteristics |

### Media Context and Control – Data Formats for Interaction Devices

The following documents were approved

| 16115 | Request for ISO/IEC 23005-5 4th Edition Data Formats for Interaction Devices |
| --- | --- |
| 16116 | Text of ISO/IEC CD 23005-5 4th Edition Data Formats for Interaction Devices |

### Media Context and Control – Common Types and Tools

The following documents were approved

| 16117 | Request for ISO/IEC 23005-6 4th Edition Common types and tools |
| --- | --- |
| 16118 | Text of ISO/IEC CD 23005-6 4th Edition Common types and tools |

### HEVC

The following documents were approved

| 16045 | Disposition of Comments on DIS ISO/IEC 23008-2:201x |
| --- | --- |
| 16046 | Text of ISO/IEC FDIS 23008-2:201x High Efficiency Video Coding [3rd ed.] |
| 16048 | High Efficiency Video Coding (HEVC) Test Model 16 (HM16) Improved Encoder Description Update 5 |
| 16049 | HEVC Screen Content Coding Test Model 7 (SCM 7) |
| 16050 | MV-HEVC verification test report |
| 16051 | SHVC verification test report |
| 16052 | Verification test plan for HDR/WCG coding using HEVC Main 10 Profile |

### Conversion and coding practices for HDR/WCG video

The following document was approved

| 16063 | WD of ISO/IEC TR 23008-14 Conversion and coding practices for HDR/WCG video |
| --- | --- |

### Additional colour description indicators

The following document was approved

| 16047 | WD of ISO/IEC 23008-2:201x/Amd.1 Additional colour description indicators |
| --- | --- |

### MPEG-H 3D Audio File Format Support

The following documents were approved

| 16090 | DoC on ISO/IEC 23008-3:2015/DAM 2, MPEG-H 3D Audio File Format Support |
| --- | --- |
| 16091 | Text of ISO/IEC 23008-3:2015/FDAM 2, MPEG-H 3D Audio File Format Support |

### MPEG-H 3D Audio Phase 2

The following document was approved

| 16092 | Study on ISO/IEC 23008-3:2015/DAM 3, MPEG-H 3D Audio Phase 2 |
| --- | --- |

### Carriage of Systems Metadata in MPEG-H 3D Audio

The following document was approved

| 16093 | Study on ISO/IEC 23008-3:2015/DAM 4, Carriage of Systems Metadata |
| --- | --- |

### 3D Audio Profiles

The following document was approved

| 16094 | WD on New Profiles for 3D Audio |
| --- | --- |

### Point Cloud Compression

The following documents were approved

| 16121 | Current status on Point Cloud Compression (PCC) |
| --- | --- |
| 16122 | Description of PCC Software implementation |

### Free Viewpoint Television

The following documents were approved

| 16128 | Results of the Call for Evidence on Free-Viewpoint Television: Super-Multiview and Free Navigation |
| --- | --- |
| 16129 | Description of 360 3D video application Exploration Experiments on Divergent multi-view video |
| 16130 | Use Cases and Requirements on Free-viewpoint Television (FTV) v.3 |

### Future Video Coding

The following documents were approved

| 16138 | Requirements for a Future Video Coding Standard v2 |
| --- | --- |
| 16125 | Presentations of the Workshop on 5G and beyond UHD Media |
| 16066 | Algorithm description of Joint Exploration Test Model 2 (JEM2) |
| 16067 | Description of Exploration Experiments on coding tools |
| 16068 | Call for test materials for future video coding standardization |

### Digital representations of light fields

The following documents were approved

| 16149 | Summary notes of technologies relevant to digital representations of light fields |
| --- | --- |
| 16150 | Draft report of the Joint Ad hoc Group on digital representations of light/sound fields for immersive media applications |

### Genome Compression

The following documents were approved

| 16134 | Requirements on Genome Compression and Storage |
| --- | --- |
| 16135 | Lossy compression framework for Genome Data |
| 16136 | Draft Call for Proposal for Genomic Information Compression and Storage |
| 16137 | Presentations of the MPEG Seminar on Genome Compression Standardization |
| 16146 | Evaluation Procedure for the Draft Call for Proposals on Genomic Information Representation and Compression |
| 16145 | Database for Evaluation of Genomic Information Compression and Storage |
| 16147 | Results of the Evaluation of the CfE on Genomic Information Compression and Storage |

## Composition coding

### MPEG-H Composition Information

The following document was approved

| 15970 | Technology under Consideration for ISO/IEC 23008-11 AMD 1 |
| --- | --- |

## Description coding

### Compact Descriptors for Video Analysis

The following documents were approved

| 15938 | Results of the Call for Proposals on CDVA |
| --- | --- |
| 16064 | CDVA Experimentation Model (CXM) 0.1 |
| 16065 | Description of Core Experiments in CDVA |

## Systems support

### Coding-independent codepoints

The following documents were approved

| 16039 | Request for ISO/IEC 23001-8:201x/Amd.1 |
| --- | --- |
| 16040 | Text of ISO/IEC 23001-8:201x/PDAM1 Additional code points for colour description |

### Media orchestration

The following documents were approved

| 16131 | Context and Objectives for Media Orchestration v.3 |
| --- | --- |
| 16132 | Requirements for Media Orchestration v.3 |
| 16133 | Call for Proposals on Media Orchestration Technologies |

## Transport and File formats

### Carriage of MPEG-H 3D audio over MPEG-2 Systems

The following documents were approved

| 15912 | DoC on ISO/IEC 13818-1:2015 DAM 5 Carriage of MPEG-H 3D audio over MPEG-2 Systems |
| --- | --- |
| 15913 | Text of ISO/IEC 13818-1:2015 FDAM 5 Carriage of MPEG-H 3D audio over MPEG-2 Systems |

### Carriage of Quality Metadata in MPEG-2 Systems

The following document was approved

| 15914 | Text of ISO/IEC 13818-1:2015 AMD 6 Carriage of Quality Metadata in MPEG-2 Systems |
| --- | --- |

### Virtual segments

The following documents were approved

| 15915 | DoC on ISO/IEC 13818-1:2015 PDAM 7 Virtual Segment |
| --- | --- |
| 15916 | Text of ISO/IEC 13818-1:2015 DAM 7 Virtual Segment |

### Signaling of carriage of HDR/WCG video in MPEG-2 Systems

The following documents were approved

| 15917 | Request for ISO/IEC 13818-1:2015 AMD 8 Signaling of carriage of HDR/WCG video in MPEG-2 Systems |
| --- | --- |
| 15918 | Text of ISO/IEC 13818-1:2015 PDAM 8 Signaling of carriage of HDR/WCG video in MPEG-2 Systems |

### DRC file format extensions

The following documents were approved

| 15922 | DoC on ISO/IEC 14496-12:2015 PDAM 1 DRC Extensions |
| --- | --- |
| 15923 | Text of ISO/IEC 14496-12:2015 DAM 1 DRC Extensions |

### Enhancements to the ISO Base Media File Format

The following document was approved

| 15925 | WD of ISO/IEC 14496-12:2015 AMD 2 |
| --- | --- |

### Carriage of NAL unit structured video in the ISO Base Media File Format

The following documents were approved

| 15927 | Draft DoC on ISO/IEC DIS 14496-15 4th edition |
| --- | --- |
| 15928 | Draft text of ISO/IEC FDIS 14496-15 4th edition |

### MMT

The following documents were approved

| 15963 | Description of Core Experiments on MPEG Media Transport |
| --- | --- |
| 15964 | Revised text of ISO/IEC 23008-1:201x 2nd edition MMT |

### Use of MMT Data in MPEG-H 3D Audio

The following documents were approved

| 15958 | DoC on ISO/IEC 23008-1:201x PDAM 1 Use of MMT Data in MPEG-H 3D Audio |
| --- | --- |
| 15959 | Text of ISO/IEC 23008-1:201x DAM 1 Use of MMT Data in MPEG-H 3D Audio |

### MMT Enhancements for Mobile Environments

The following documents were approved

| 15995 | Request for ISO/IEC 23008-1:201x AMD 2 Enhancements for Mobile Environments |
| --- | --- |
| 15960 | Text of ISO/IEC 23008-1:201x PDAM 2 Enhancements for Mobile Environments |

The following document was approved

| 15961 | WD of ISO/IEC 23008-1:201x AMD 3 |
| --- | --- |

### Carriage of Green Metadata in an HEVC SEI Message

The following documents were approved

| 15948 | DoC on ISO/IEC 23001-11:201x/DAM 1 Carriage of Green Metadata in an HEVC SEI Message |
| --- | --- |
| 15949 | Text of ISO/IEC 23001-11:201x/FDAM 1 Carriage of Green Metadata in an HEVC SEI Message |

### Support for AVC, JPEG and layered coding of images

The following documents were approved

| 15972 | Request for ISO/IEC 23008-12 AMD 1 |
| --- | --- |
| 15973 | Text of ISO/IEC 23008-12 PDAM 1 Support for AVC, JPEG and layered coding of images |

### MPEG Media Transport Implementation Guidelines

The following documents were approved

| 15976 | DoC for ISO/IEC PDTR 23008-13 2nd edition MPEG Media Transport Implementation Guidelines |
| --- | --- |
| 15977 | Text of ISO/IEC DTR 23008-13 2nd edition MPEG Media Transport Implementation Guidelines |
| 15978 | WD of ISO/IEC 23008-13 3rd edition MPEG Media Transport Implementation Guidelines |

### DASH

The following documents were approved

| 15985 | Technologies under Consideration for DASH |
| --- | --- |
| 15986 | Descriptions of Core Experiments on DASH amendment |
| 15987 | Draft Text of ISO/IEC 23009-1 3rd edition |

### Authentication, Access Control and Multiple MPDs

The following documents were approved

| 15979 | DoC on ISO/IEC 23009-1:2014 DAM 3 Authentication, Access Control and multiple MPDs |
| --- | --- |
| 15980 | Text of ISO/IEC 23009-1:2014 FDAM 3 Authentication, Access Control and multiple MPDs |

### Segment Independent SAP Signalling, MPD chaining and other extensions

The following documents were approved

DoC on ISO/IEC 23009-1:2014 PDAM 4 Segment Independent SAP Signalling (SISSI), MPD chaining, MPD reset and other extensions

Text of ISO/IEC 23009-1:2014 DAM 4 Segment Independent SAP Signalling (SISSI), MPD chaining, MPD reset and other extensions

### MPEG-DASH Implementation Guidelines

The following document was approved

| 15990 | WD of ISO/IEC 23009-3 2nd edition AMD 1 DASH Implementation Guidelines |
| --- | --- |

### Server and Network Assisted DASH

The following document was approved

| 15991 | Study of ISO/IEC DIS 23009-5 Server and Network Assisted DASH |
| --- | --- |

### DASH with Server Push and WebSockets

The following documents were approved

| 15992 | Request for subdivision of ISO/IEC 23009-6 DASH with Server Push and WebSockets |
| --- | --- |
| 15993 | Text of ISO/IEC CD 23009-6 DASH with Server Push and WebSockets |

## Multimedia architecture

### MPEG-M Architecture

The following documents were approved

| 15952 | DoC on ISO/IEC CD 23006-1 3rd edition Architecture |
| --- | --- |
| 15953 | Text of ISO/IEC DIS 23006-1 3rd edition Architecture |

### MPEG extensible middleware (MXM) API

The following document was approved

| 15954 | Text of ISO/IEC IS 23006-2 3rd edition MXM API |
| --- | --- |

### MPEG-V Architecture

The following documents were approved

| 16106 | Technology under consideration |
| --- | --- |
| 16107 | Request for ISO/IEC 23005-1 4th Edition Architecture |
| 16108 | Text of ISO/IEC CD 23005-1 4th Edition Architecture |

### Mixed and Augmented Reality Reference Model

The following document was approved

| 16119 | Text of ISO/IEC 2nd CD 18039 Mixed and Augmented Reality Reference Model |
| --- | --- |

### Media-centric Internet of Things and Wearables

The following documents were approved

| 16140 | Overview, context and objectives of Media-centric IoTs and Wearables |
| --- | --- |
| 16141 | Conceptual model, architecture and use cases for Media-centric IoTs and Wearables |
| 16139 | Draft Requirements for Media-centric IoTs and Wearables |
| 16120 | State of discussions related to MIoTW technologies |

### Big Media

The following document was approved

| 16151 | Thoughts and Use Cases on Big Media |
| --- | --- |

## Application formats

### Augmented Reality Application Format

The following document was approved

| 16103 | Text of ISO/IEC FDIS 23000-13 2nd Edition Augmented Reality Application Format |
| --- | --- |

### Publish/Subscribe Application Format

The following documents were approved

| 15944 | DoC on ISO/IEC DIS 23000-16 Publish/Subscribe Application Format |
| --- | --- |
| 15945 | Text of ISO/IEC FDIS 23000-16 Publish/Subscribe Application Format |

### Multisensorial Effects Application Format

The following documents were approved

| 16104 | DoC for ISO/IEC 23000-17:201x CD Multiple Sensorial Media Application Format |
| --- | --- |
| 16105 | Text of ISO/IEC 23000-17:201x DIS Multiple Sensorial Media Application Format |

### Omnidirectional Media Application Format

The following documents were approved

| 16143 | Requirements for OMAF |
| --- | --- |
| 15946 | Technologies under Considerations for Omnidirectional Media Application Format |

### Common Media Application Format

The following documents were approved

| 16144 | Requirements for the Common Media Application Format |
| --- | --- |
| 15947 | WD v.1 of Common Media Application Format |

### Visual Identiy Management Application Format

The following document was approved

| 16142 | Use cases and requirements on Visual Identiy Management AF |
| --- | --- |

## Reference implementation

### Reference Software for Internet Video Coding

The following documents were approved

| 16026 | Disposition of Comments on ISO/IEC 14496-5:2001/PDAM41 |
| --- | --- |
| 16027 | Text of ISO/IEC 14496-1:2001/DAM41 Reference Software for Internet Video Coding |

### Reference Software for Alternative Depth Information SEI message

The following documents were approved

| 16028 | Disposition of Comments on ISO/IEC 14496-5:2001/PDAM42 |
| --- | --- |
| 16029 | Text of ISO/IEC 14496-1:2001/DAM42 Reference Software for Alternative Depth Information SEI message |

### Reference Software for File Format

The following document was approved

| 15935 | WD of ISO/IEC 14496-32 Reference Software and Conformance for File Format |
| --- | --- |

### Reference Software and Implementation Guidelines of User Description

The following documents were approved

| 15921 | Request for ISO/IEC 21000-22 AMD 1 Reference Software and Implementation Guidelines of User Description |
| --- | --- |
| 15943 | Text of ISO/IEC 21000-22 PDAM 1 Reference Software and Implementation Guidelines of User Description |

### Reference Software for Green Metadata

The following documents were approved

| 15950 | Request for ISO/IEC 23001-11 AMD 2 Conformance and Reference Software |
| --- | --- |
| 15951 | Text of ISO/IEC 23001-11 PDAM 2 Conformance and Reference Software |

### Reference Software for Media Tool Library

The following documents were approved

| 16043 | Disposition of Comments on ISO/IEC 23002-5:2013/PDAM3 |
| --- | --- |
| 16044 | Text of ISO/IEC 23002-5:2013/DAM3 Reference software for parser instantiation from BSD |

### SAOC and SAOC Dialogue Reference Software

The following document was approved

| 16078 | Study on ISO/IEC 23003-2:2010/DAM 5, SAOC Reference Software |
| --- | --- |

### Reference Software for DRC

The following documents were approved

| 16087 | Request for Amendment ISO/IEC 23003-4:2015/AMD 2, DRC Reference Software |
| --- | --- |
| 16088 | ISO/IEC 23003-4:2015/PDAM 2, DRC Reference Software |

### Reference Software for MPEG-M

The following document was approved

| 15955 | Text of ISO/IEC IS 23006-3 3rd edition MXM Reference Software and Conformance |
| --- | --- |

### MMT Reference Software

The following documents were approved

| 15965 | Text of ISO/IEC IS 23008-4 MMT Reference Software |
| --- | --- |
| 15966 | Request for ISO/IEC 23008-4 AMD 1 MMT Reference Software with Network Capabilities |
| 15967 | Text of ISO/IEC 23008-4 PDAM 1 MMT Reference Software with Network Capabilities |

### HEVC Reference Software`

The following documents were approved

| 16053 | Disposition of Comments on ISO/IEC 23008-5:2015/DAM3 |
| --- | --- |
| 16054 | Disposition of Comments on ISO/IEC 23008-5:2015/DAM4 |
| 16055 | Text of ISO/IEC FDIS 23008-5:201x Reference Software for High Efficiency Video Coding [2nd ed.] |
| 16056 | Request for ISO/IEC 23008-5:201x/Amd.1 |
| 16057 | Text of ISO/IEC 23008-5:201x/PDAM1 Reference Software for Screen Content Coding Profiles |

### 3D Audio Reference Software

The following documents were approved

| 16095 | 3D Audio Reference Software RM6 |
| --- | --- |
| 16096 | Workplan on 3D Audio Reference Software RM7 |

### MPEG-DASH Reference Software

The following document was approved

| 15989 | Work plan for development of DASH Conformance and reference software and sample clients |
| --- | --- |

## Conformance

### Internet Video Coding Conformance

The following documents were approved

| 16024 | Disposition of Comments on ISO/IEC 14496-4:2004/PDAM46 |
| --- | --- |
| 16025 | Text of ISO/IEC 14496-4:2004/DAM46 Conformance Testing for Internet Video Coding |

### Conformance of File Format

The following document was approved

| 15935 | WD of ISO/IEC 14496-32 Reference Software and Conformance for File Format |
| --- | --- |

### Media Tool Library Conformance

The following documents were approved

| 16043 | Disposition of Comments on ISO/IEC 23002-5:2013/PDAM3 |
| --- | --- |
| 16044 | Text of ISO/IEC 23002-5:2013/DAM3 Reference software for parser instantiation from BSD |

### Conformance for Green Metadata

The following documents were approved

| 15950 | Request for ISO/IEC 23001-11 AMD 2 Conformance and Reference Software |
| --- | --- |
| 15951 | Text of ISO/IEC 23001-11 PDAM 2 Conformance and Reference Software |

### SAOC and SAOC Dialogue Enhancement Conformance

The following document was approved

| 16077 | Study on ISO/IEC 23003-2:2010/DAM 4, SAOC Conformance |
| --- | --- |

### MPEG-V – Conformance

### Conformance of MPEG-M

The following document was approved

| 15955 | Text of ISO/IEC IS 23006-3 3rd edition MXM Reference Software and Conformance |
| --- | --- |

### MMT Conformance

The following document was approved

| 15968 | Workplan of MMT Conformance |
| --- | --- |

### HEVC Conformance

The following documents were approved

| 16058 | Disposition of Comments on ISO/IEC 23008-8:2015/DAM1 |
| --- | --- |
| 16059 | Disposition of Comments on ISO/IEC 23008-8:2015/DAM2 |
| 16060 | Disposition of Comments on ISO/IEC 23008-8:2015/DAM3 |
| 16061 | Text of ISO/IEC FDIS 23008-8:201x HEVC Conformance Testing [2nd edition] |
| 16062 | Working Draft of ISO/IEC 23008-8:201x/Amd.1 Conformance Testing for Screen Content Coding Profiles |

## Maintenance

### Systems coding standards

The following documents were approved

| 15910 | DoC on ISO/IEC 13818-1:2015 AMD 1/DCOR 2 |
| --- | --- |
| 15911 | Text of ISO/IEC 13818-1:2015 AMD 1/COR 2 |
| 15919 | Text of ISO/IEC 13818-1:2015 DCOR 2 |
| 15920 | Defect Report of ISO/IEC 14496-12 |
| 15926 | Text of ISO/IEC 14496-14 COR 2 |
| 15929 | Defect Report of ISO/IEC 14496-15 |
| 15932 | DoC on ISO/IEC 14496-30:2014 DCOR 2 |
| 15933 | Text of ISO/IEC 14496-30:2014 COR 2 |
| 15956 | DoC on ISO/IEC 23008-1:2014 DCOR 2 |
| 15957 | Text of ISO/IEC 23008-1:2014 COR 2 |
| 15962 | Defects under investigation in ISO/IEC 23008-1 |
| 15969 | Text of ISO/IEC 23008-11 DCOR 1 |
| 15974 | DoC on ISO/IEC 23008-12 DCOR 1 |
| 15975 | Text of ISO/IEC 23008-12 COR 1 |
| 15974 | DoC on ISO/IEC 23008-12 DCOR 1 |
| 15975 | Text of ISO/IEC 23008-12 COR 1 |
| 15983 | Text of ISO/IEC 23009-1:2014 DCOR 3 |
| 15984 | Defects under investigation in ISO/IEC 23009-1 |

### Audio coding standards

The following documents were approved

| 15998 | Text of ISO/IEC 14496-3:2009/AMD 3:2012/COR 1, Downscaled (E)LD |
| --- | --- |
| 15924 | Text of ISO/IEC 14496-5:2001/AMD 24:2009/DCOR 3, Downscaled (E)LD |
| 16076 | ISO/IEC 23003-2:2010/DCOR 3 SAOC, SAOC Corrections |
| 16080 | DoC on ISO/IEC 23003-3:2012/Amd.1:2014/DCOR 2 |
| 16081 | Text of ISO/IEC 23003-3:2012/Amd.1:2014/COR 2 |
| 16084 | Defect Report on MPEG-D DRC |
| 16089 | ISO/IEC 23008-3:2015/DCOR 1 Multiple corrections |

# Organisation of this meeting

## Tasks for subgroups

The following tasks were assigned

| Group | Std | Pt | E/A | Title |
| --- | --- | --- | --- | --- |
| Requirements | 7 |  |  | Compact Descriptors for Video Analysis |
|  | A |  |  | CMAF |
|  | V |  |  | MioT – MPEG wearable |
|  | Exp |  |  | FTV |
|  | Exp |  |  | Future video coding |
|  | Exp |  |  | Media orchestration |
|  | Exp |  |  | Genome compression |
|  | Exp |  |  | Everything 3D |
| Systems | 2 | 1 | A4 | Carriage of additional Audio P&L |
|  |  | 1 | A5 | Carriage of 3D Audio |
|  |  | 1 | A6 | Carriage of quality metadata |
|  |  | 1 | A7 | Virtual segments |
|  | 4 | 15 | E4 | Carriage of layered HEVC |
|  |  |  | A2 | Carriage of AVC-based 3D excluding MVC |
|  |  | 22 | E3 | Open Font Format |
|  |  | 32 | E1 | FF RS (including SVC FF RS) |
|  | 21 | 22 | E1 | User description |
|  | A | 15 | E1 | MPAF |
|  |  | 16 | E1 | PSAF |
|  |  | 17 | E1 | Multisensorial AF |
|  |  | 18 | E1 | MLAF |
|  |  | 19 | E1 | Screen Sharing AF |
|  |  | 20 | E1 | Omnidirectional Media AF |
|  |  | 21 | E1 | CMAF |
|  |  | 22 | E1 | Identity management AF |
|  | B | 8 | A1 | CICP |
|  |  | 10 | A1 | ROI coordinates |
|  | DA | 1 | A3 | Authentication access control and multiple MPD |
|  |  | 2 | E2 | DASH C&RS |
|  |  | 3 | E3 | Implementation guidelines |
|  |  | 5 | E1 | SAND |
|  |  | 6 | E1 | FDH |
|  | H | 1 | A1 | MMT data carriage in 3D Audio |
|  |  |  | A2 | Mobile MMT |
|  |  | 4 | E1 | MMT Reference Software |
|  |  | 7 | E1 | MMT Conformance |
|  |  | 12 | E1 | Storage of image sequences in ISOBMFF |
|  |  | 13 | E2 | MMT implementation guidelines |
|  | M | 1 | E3 | Architecture |
|  |  | 2 | E3 | MXM Engines and API |
|  |  | 3 | E3 | Reference software |
|  | Exp |  |  | Media orchestration |
| Video | 4 | 10 | A2 | Additional levels and SEI |
|  |  |  | A4 | Progressive High 10 Profile |
|  |  | 33 | E1 | Internet Video Coding |
|  | 7 | 6 | E2 | Reference software |
|  |  | 14 | E1 | CDVS RS&C |
|  |  | 15 | E1 | CDVA |
|  | B | 4 | E4 | Parser instantiation from BSD |
|  |  | 8 | A1 | CICP |
|  | C | 4 | A2 | VTL extensions (HEVC) |
|  | Exp |  |  | Future Video Coding |
| VC | H | 2 | E3 | SCC |
|  |  | 5 | A1 | RExt Reference Software |
|  |  |  | A3 | SHVC Reference Software |
|  |  | 8 | A2 | RExt Conformance |
|  |  |  | A3 | SHVC conformance |
|  |  | 14 | E1 | HDR best practices |
| 3V | 4 | 4 | A45 | MFC+depth conformance |
|  |  | 5 | A39 | MFC+depth RS |
|  |  | 10 | A3 | Additional SEI |
|  | H | 5 | A2 | MV-HEVC RS |
|  |  |  | A4 | 3D RS |
|  |  | 8 | A1 | MV + 3D Conformance |
| Audio | 4 | 3 | A6 | Levels for 22 channel programs |
|  | D | 4 | A1 | Decoder generated DRC sets |
|  |  |  | A2 | DRC C |
|  |  |  | A3 | DRC RS |
|  | H | 3 | E2 | 3D Audio phase 2 |
|  |  |  | A2 | FF support for 3D Audio |
|  |  | 6 | E1 | 3D Audio RS |
|  |  | 9 | E1 | 3D Audio C |
| 3DG | 4 | 5 | A40 | Web3D coding RS |
|  |  | 11 | E2 | Protos for ARAF in BIFS |
|  |  | 25 | E3 | Web 3DG coding |
|  |  | 27 | A4 | Web3D coding C |
|  | A | 13 | E2 | ARAF |
|  |  | 17 | E1 | Multisensory MAF |
|  | M | 2 | E3 | MPEG-V engines |
|  | MAR |  | E1 | MAR RM |
|  | V | 1 | E3 | Architecture |
|  |  | 2 | E3 | Control Information |
|  |  | 3 | E3 | Sensory information |
|  |  | 4 | E3 | Virtual world object characteristics |
|  |  | 5 | E3 | Data representation for interaction devices |
|  |  | 6 | E3 | Common types and tools |
|  |  | 7 | E3 | Conformance and reference software |
| Communication | White Paper |  |  | Animation Framework eXtension (AFX) Compact descriptors for visual search Image File Format CEL & MCO ARAF |
|  | Video |  |  | 3D Audio |
|  | Introduction |  |  | Make a good introduction for ARAF, UD |
|  | Column |  |  | Open font format Dynamic Range Control HEVC/SCC 3D Audio CDVS User Description ARAF PSAF |

## Joint meetings

The following joint meetings were held

| Groups | What | Day | Time1 | Time2 | Where |
| --- | --- | --- | --- | --- | --- |
| R, V | HDR | Mon | 15:30 | 16:30 | V |
| R, V, VC, VCEG | HDR, SCC | Mon | 16:30 | 18:00 | VC |
| R, V, VCEG | AVC | Mon | 18:00 | 18:30 | VC |
| S, A | System carriage | Tue | 09:00 | 10:00 | A |
| R, V | CDVA | Tue | 09:00 | 10:00 | R |
| R, V, 3 | Everything 3D | Tue | 10:00 | 11:00 | R |
| S, R | CMF, OMAF | Tue | 12:00 | 13:00 | R |
| All | MPEG Vision | Wed | 11:30 | 13:00 | A |
| R, V, VCEG, VC | HDR | Wed | 11:00 | 12:00 | Salon D-E |
| JPEG-MPEG | Joint standards | Thu | 09:00 | 10:00 | JPEG |
| A, 3 | 3D Audio in VR/AR | Thu | 10:00 | 11:00 | A |
| R, A | 3D Audio profiles | Thu | 11:00 | 12:00 | A |
| R, 3 | MIoTW | Thu | 14:00 | 15:00 | 3 |
| All | Communication | Thu | 16:00 | 17:00 | MIssion Beach |
| All | MPEG Vision | Thu | 16:00 | 18:00 |  |

# WG management

## Terms of reference

The following document was approved

| 16000 | Terms of Reference |
| --- | --- |

## Liaisons

### Input liaisons

The following input liaisons were received

| # | Title | Source | Disposition |  |
| --- | --- | --- | --- | --- |
| 37576 | Liaison statement | JTC 1/ WG 10 | IoT | 3 |
| 37577 | Liaison statement | SC 37 | Biometric presentation attack detection | R |
| 37578 | ITU-T SG | ITU-T SG 16 | 16 on video coding collaboration | V |
| 37579 | ITU-T SG 16 | ITU-T SG 16 | on discontinued IPTV multimedia application frameworks to include the definition of IPTV in N13952 | S |
| 37580 | ITU-R SG 6 | ITU-R SG 6 | on ITU-R BS.1196-5Audio coding for digital broadcasting | A |
| 37581 | JTC 1/WG 10 | JTC 1/ WG 10 | Invitation to the 4th JTC 1/WG 10 Meeting, 18th-22nd Jan. 2016 | 3 |
| 37582 | JTC 1/WG 10 on | JTC 1/ WG 10 | Logistical information for the 4th JTC 1/WG 10 Meeting | 3 |
| 37583 | Liaison statement | ITU-T SG 20 | a new Study Group, IoT and its applications including smart cities and communities (SC&C) | 3 |
| 37584 | Liaison statement | JTC 1/ WG 10 | collection of Data related to the Internet of Things | 3 |
| 37585 | Liaison statement | IETF | URI Signing | S |
| 37653 | Liaison statement | ITU-T SG 9 | Specification of IP-VOD DRM for cable television multiscreen system in Multi-DRM environment | S |
| 37654 | HDR | DVB |  | V |
| 37655 | MPEG-H Audio | DVB |  | A |
| 37656 | Liaison statement | 3GPP | DASH | S |
| 37787 | Liaison statement | DVB | TEMI | S |
| 37788 | Liaison statement | ITU-T SG 16 | HDR | V |
| 37899 | MPEG-DASH (N15699) | DASH IF |  | S |
| 38016 | Liaison statement | ETSI ISG CCM | HDR | V |
| 38040 | Liaison statement | HbbTV | TEMI | S |
| 38041 | Revised WD of ISO/IEC 30141 | JTC 1/ WG 10 | Internet of Things Reference Architecture (IoT RA) | 3 |
| 38042 |  | JTC 1/ WG 10 | Request contributions on IoT use cases | 3 |
| 38082 | HDR | SMPTE |  | V |
| 38095 | Liaison statement | VSF | higher resolution JPEG 2000 video in MPEG-2 TS | S |
| 37658 | IEC CD 60728-13-1 Ed. 2.0 | IEC TC 100 | Cable networks for television signals, sound signals and interactive services |  |
| 37589 | IEC CD 61937-13 and 61937-14 | IEC TC 100 | Digital audio - Interface for non-linear PCM encoded audio bitstreams |  |
| 37590 | IEC CD 61937-2 Ed. 2.0/Amd.2 | IEC TC 100 | Digital audio - Interface for non-linear PCM encoded audio bitstreams |  |
| 37686 | IEC CD 62608-2 Ed.1.0 | IEC TC 100 | Multimedia home network configuration - Basic reference model |  |
| 37591 | IEC CD 63029 [IEC 100/2627/CD] | IEC TC 100 | Multimedia e-publishing and e-book technologies - Raster-graphics image-based e-books |  |
| 37592 | IEC CD 63029 [IEC 100/2627A/CD] | IEC TC 100 | Multimedia e-publishing and e-book technologies - Raster-graphics image-based e-books (Titre) : Introductory note |  |
| 37650 | IEC CDV 62394/Ed.3 | IEC TC 100 | Service diagnostic interface for consumer electronics products and networks |  |
| 37595 | IEC CDV 62680-1-3, 62680-3-1 and 62943 | IEC TC 100 | Universal Serial Bus Type-CTM Cable and Connector Specification, Revision 1.1 |  |
| 37586 | IEC CDV 62766-4-1, 62766-4-2, 62766-5-1, 62766-5-2, 62766-6, 62766-7 and 62766-8 | IEC TC 100 | Open IPTV Forum (OIPF) consumer terminal function and network interfaces for access to IPTV and open Internet multimedia services |  |
| 37657 | IEC CDV 62827-3 Ed. 1.0 | IEC TC 100 | Wireless Power Transfer - Management |  |
| 37659 | IEC CDV 62943/Ed. 1.0 | IEC TC 100 | Visible light beacon system for multimedia applications |  |
| 37598 | IEC CDV 63002 Ed. 1.0 | IEC TC 100 | Identification and communication interoperability method for external power supplies used with portable computing devices |  |
| 37660 | IEC CDV 63002 Ed.1.0 | IEC TC 100 | Identification and communication interoperability method for external power supplies used with portable computing devices |  |
| 37588 | IEC CDV 63028 Ed. 1.0 | IEC TC 100 | Wireless Power Transfer - Magnetic Resonance Interoperability |  |
| 37596 | IEC CDV | IEC TC 100 | MIDI (MUSICAL INSTRUMENT DIGITAL INTERFACE) SPECIFICATION 1.0 (ABRIDGED EDITION, 2015)MIDI (MUSICAL INSTRUMENT DIGITAL INTERFACE) SPECIFICATION 1.0 |  |
| 37587 | IEC DTR 62921 Ed. 2.0 | IEC TC 100 | QUANTIFICATION METHODOLOGY FOR GREENHOUSE GAS EMISSIONS FOR COMPUTERS AND MONITORS |  |
| 37651 | IEC | IEC TC 100 | NP Microspeakers |  |
| 37597 | IEC | IEC TC 100 | NP MIDI (MUSICAL INSTRUMENT DIGITAL INTERFACE) SPECIFICATION 1.0 (ABRIDGED EDITION, 2015) |  |
| 37652 | IEC | IEC TC 100 | NP Multimedia Vibration Audio Systems - Method of measurement for audio characteristics of audio actuator by pinna-conduction |  |
| 37593 | IEC | IEC TC 100 | NP: Universal Serial Bus interfaces for data and power - Part 3-1 |  |
| 37594 | IEC | IEC TC 100 | NP: Universal Serial Bus interfaces for data and power - Part 1-3 |  |
| 37661 | IEC TR 62935 Ed1.0 | IEC TC 100 | TECHNICAL REPORT OF MEASUREMENT METHODS – High Dynamic Range Video |  |
| 37685 | IEC TS 63033-1 | IEC TC 100 | CAR MULTIMEDIA SYSTEMS AND EQUIPMENT – DRIVE MONITOR SYSTEM |  |

### Output liaisons

The following output liaisons were sent

| 16148 | Liaison with TC 276 |
| --- | --- |
| 16126 | Liaison to JTC 1/WG 9 |
| 16015 | Liaison Statement to IETF on URI signing |
| 16016 | Liaison Statement template on DASH with Server Push and WebSockets |
| 16017 | Liaison Statement to 3GPP on DASH |
| 16018 | Liaison Statement to DASH-IF on DASH |
| 16019 | Liaison Statement to DVB on TEMI |
| 16020 | Liaison Statement to HbbTV on TEMI |
| 16021 | Liaison Statement template on Common Media Application Format |
| 16022 | Liaison Statement template on HEVC sync samples in ISO/IEC 14496-15 |
| 16023 | Liaison Statement to SCTE on Virtual Segments and DASH |
| 16069 | Liaison statement to ITU-T SG 16 on video coding collaboration |
| 16070 | Liaison statement to DVB on HDR |
| 16071 | Liaison statement to ATSC on HDR/WCG |
| 16072 | Liaison statement to ITU-R WP6C on HDR |
| 16073 | Liaison statement to ETSI ISG CCM on HDR |
| 16074 | Liaison statement to SMPTE on HDR/WCG |
| 16097 | Liaison Statement to DVB on MPEG-H 3D Audio |
| 16098 | Liaison Statement Template on MPEG-H 3D Audio |
| 16099 | Liaison Statement to ITU-R Study Group 6 on BS.1196-5 |
| 16100 | Liaison Statement to IEC TC 100 |
| 16101 | Liaison Statement to IEC TC 100 TA 4 |
| 16102 | Liaison Statement to IEC TC 100 TA 5 |
| 16123 | Liaison Statement to JTC1 WG10 related to MIoT |
| 16124 | Liaison Statement to ITU-T SG20 related to MIoT |

### Statement of benefits

The following document was approved

| 16075 | Statement of benefit for establishing a liaison with DICOM |
| --- | --- |

### Organisations in liaison

The following document was approved

| 16011 | List of organisations in liaison with MPEG |
| --- | --- |

## Ad hoc groups

The following document was approved

| 15905 | List of AHGs Established at the 114th Meeting |
| --- | --- |

## Asset management

The following documents were approved

| 16005 | Schemas |
| --- | --- |
| 16006 | Reference software |
| 16007 | Conformance |
| 16008 | Content |
| 16009 | URIs |

## IPR management

The following document was approved

| 16010 | Call for patent statements on standards under development |
| --- | --- |

## Work plan and time line

The following documents were approved

| 16001 | MPEG Standards |
| --- | --- |
| 16002 | Table of unpublished FDIS |
| 16003 | MPEG Work plan |
| 16004 | MPEG time line |
| 16013 | Complete list of all MPEG standards |
| 15971 | MPEG Strategic Standardisation Roadmap |

# Administrative matters

## Schedule of future MPEG meetings

The following meeting schedule was approved

| # | City | Country | yy | mm-mm | dd-dd |
| --- | --- | --- | --- | --- | --- |
| 115 | Geneva | CH | 16 | 05-06 | 30-03 |
| 116 | Chengdu | CN | 16 | 10 | 17-21 |
| 117 | Geneva | CH | 17 | 01 | 16-20 |
| 118 | Hobart | AU | 17 | 04 | 03-07 |
| 119 | Torino | IT | 17 | 07 | 17-21 |
| 120 | ?? | ?? | 17 | 10 | 23-27 |
| 121 | ?? | ?? | 18 | 01 | 22-26 |
| 122 | ?? | ?? | 18 | 04 | 16-20 |

## Promotional activities

The following documents were approved

| 15996 | White Paper on MPEG-21 Contract Expression Language (CEL) and MPEG-21 Media Contract Ontology (MCO) |
| --- | --- |
| 15997 | White Paper on the 2nd edition of ARAF |
| 15907 | Press Release of the 114th Meeting |

# Resolutions of this meeting

These were approved

# A.O.B.

There was no other business

# Closing

Meeting closed at 2016/02/26T20:00

– Attendance list

| LastName | FirstName | Organization | Country |
| --- | --- | --- | --- |
| Brown | Gregg | Microsoft | United States |
| Chon | Jaehong | Qualcomm | United States |
| Chong | In suk | Qualcomm | United States |
| El-Maleh | khaled | Qualcomm | United States |
| Hach | Faraz | Simon Fraser University | Canada |
| Harvey | Ian | 20th Century Fox | United States |
| Kempf | James | Ericsson | United States |
| Koizumi | Mariko | Kyoto Seika University | Japan |
| Lee | Gwo Giun | National Cheng Kung University | China |
| Li | Zhu | University of Missouri, Kansas City | United States |
| Lo | Charles | Qualcomm Technologies Incorporated | United States |
| Nandhakumar | Nandhu | LG Electronics | United States |
| Pazos | Marcelo | Qualcomm Inc. | United States |
| Sedlik | Jeffrey | PLUS Coalition | United States |
| Zhong | Xin | QUALCOMM | United States |
| Zhou | Wensheng | SIP UCLA ITA | United States |
| Aaron | Anne | Netflix | United States |
| Abbas | Adeel | GoPro | United States |
| Agnelli | Matteo | Fraunhofer IIS | Germany |
| Agostinelli | Massimiliano | Trellis Management Ltd | United Kingdom |
| Ahn | Yong-Jo | Kwangwoon University (KWU) | Korea |
| Alberti | Claudio | EPFL | Switzerland |
| Alpaslan | Zahir | Ostendo Technologies, Inc. | United States |
| Alshina | Elena | Samsung Electronics | Korea |
| Alvarez | Jose Roberto | Huawei Technologies | United States |
| Amon | Peter | Siemens AG | Germany |
| Andersson | Kenneth | Ericsson | Sweden |
| Andriani | Stefano | ARRI Cinetechnik GmbH | Germany |
| Aoki | Shuichi | NHK | Japan |
| Artusi | Alessandro | Trellis | United Kingdom |
| Azimi | Maryam | University of British Columbia | Canada |
| Bae | HyoChul | Konkuk University | Korea |
| Bailer | Werner | JOANNEUM RESEARCH | Austria |
| Balestri | Massimo | Telecom Italia S.p.A. | Italy |
| Ballocca | Giovanni | Sisvel Technology srl | Italy |
| Bandoh | Yukihiro | NTT | Japan |
| Bang | Gun | ETRI | Korea |
| Baroncini | Vittorio | GBTech | Italy |
| Barroux | Guillaume | Fujitsu Laboratories Ltd. | Japan |
| Baumgarte | Frank | Apple Inc. | United States |
| Baylon | David | ARRIS | United States |
| Beack | Seungkwon | ETRI | Korea |
| Benjelloun Touimi | Abdellatif | Huawei Technologies (UK) Co., Ltd. | United Kingdom |
| bergeron | cyril | Thales | France |
| Bivolarsky | Lazar | Tata Communnications | United States |
| Bober | Miroslaw | Surrey University | United Kingdom |
| Boitard | Ronan | University of British Columbia | Canada |
| Bouazizi | Imed | Samsung Research America | United States |
| Boyce | Jill | Intel | United States |
| brondijk | robert | Philips | Netherlands |
| Bross | Benjamin | Fraunhofer HHI | Germany |
| Bruylants | Tim | Vrije Universiteit Brussel - iMinds | Belgium |
| Budagavi | Madhukar | Samsung Research America | United States |
| Bugdayci Sansli | Done | Qualcomm | Finland |
| Byun | Hyung Gi | Kangwon National University | Korea |
| Carballeira | Pablo | Universidad Politecnica de Madrid | Spain |
| Ceulemans | Beerend | iMinds - ETRO - VUB | Belgium |
| Chai | Chi | Real Communications | United States |
| Chalmers | Alan | University of Warwick | United Kingdom |
| Champel | Mary-Luc | Technicolor | France |
| Chandramouli | Krishna | Queen Mary, University of London | United Kingdom |
| Chang | Mike | Huawei Devices | United States |
| CHANG | SUNG JUNE | ETRI | Korea |
| CHANG | YAO JEN | ITRI International | China |
| Chen | Chun-Chi | InterDigital | United States |
| Chen | Hao | Shanghai Jiao Tong University | China |
| Chen | Jianle | Qualcomm Inc. | United States |
| Chen | Jie | Peking University | China |
| Chen | Junhua | Huawei Technologies Co., Ltd. | China |
| Chen | Peisong | Broadcom Corporation | United States |
| Chen | Weizhong | Huawei technologies CO.,LTD | China |
| Chiariglione | Leonardo | CEDEO | Italy |
| Chien | Wei-Jung | Qualcomm Inc. | United States |
| Chinen | Toru | Sony Corporation | Japan |
| Chiu | Yi-Jen | Intel Corp. | United States |
| Cho | Minju | Seoul Women's University | Korea |
| Choe | Yoonsik | Yonsei University | Korea |
| Choi | Byeongdoo | Samsung Electronics | Korea |
| Choi | Hae Chul | Hanbat National University | Korea |
| Choi | JangSik | Kangwon national university | Korea |
| Choi | Jangwon | LG Electronics | Korea |
| Choi | Kiho | Samsung Electronics | Korea |
| Choi | Miran | ETRI | Korea |
| CHOI | SEUNGCHEOL | Sejong University | Korea |
| Chon | Sang Bae | Samsung Electronics | Korea |
| Chono | Keiichi | NEC Corp. | Japan |
| Chujoh | Takeshi | Toshiba corporation | Japan |
| Chun | Sungmoon | Insignal | Korea |
| clare | gordon | orange labs | France |
| Concolato | Cyril | Telecom ParisTech | France |
| DA YOUNG | JUNG | Konkuk University | Korea |
| Dang | Niem | SCTE | United States |
| Daniels | David | Sky | United Kingdom |
| Daniels | Noah | MIT | United States |
| de Bruijn | Werner | Philips | Netherlands |
| De Cock | Jan | Netflix | United States |
| de Haan | Wiebe | Philips | Netherlands |
| DEROUINEAU | Nicolas | VITEC | France |
| Descampe | Antonin | intoPIX | Belgium |
| Dias | Andre | BBC | United Kingdom |
| Doherty | Richard | Dolby Labs | United States |
| Dolan | Michael | TBT | United States |
| Domanski | Marek | Poznan University of Technology | Poland |
| doyen | didier | technicolor | France |
| Ducloux | Xavier | B<>com | France |
| Duenas | Alberto | NGCodec Inc | United States |
| Dufourd | Jean-Claude | Institut Mines Telecom | France |
| Ebrahimi | Touradj | EPFL | Switzerland |
| Ehara | Hiroyuki | Panasonic Corporation | Japan |
| fautier | thierry | harmonic | United States |
| Feng | Jie | Vixs System Inc | Canada |
| Fersch | Christof | Dolby Laboratories | Germany |
| Filippov | Alexey | Huawei Technologies | Russia |
| Filos | Jason | Qualcomm | United States |
| Foessel | Siegfried | Fraunhofer IIS | Germany |
| Fogg | Chad | MovieLabs | United States |
| Francois | Edouard | Technicolor | France |
| Fröjdh | Per | Ericsson | Sweden |
| Fuchs | Harald | Fraunhofer IIS | Germany |
| Gao | Wen | Harmonic Inc | United States |
| Gendron | Patrick | Thomson Video Networks | France |
| Gérard | MADEC | B-COM | France |
| Gibbs | Jon | Huawei Technologies Co Ltd | United Kingdom |
| Gibellino | Diego | Telecom Italia SPA | Italy |
| GISQUET | Christophe | CANON Research France | France |
| Grange | Adrian | Google | United States |
| Grant | Catherine | Nine Tiles | United Kingdom |
| Graziosi | Danillo | Ostendo Technologies Inc. | United States |
| Grois | Dan | Fraunhofer HHI | Germany |
| Grüneberg | Karsten | Fraunhofer HHI | Germany |
| Gu | Zhouye | Arris Group Inc. | United States |
| GUEZ VUCHER | Marc | SCPP | France |
| Hagqvist | Jari | Nokia Technologies | Finland |
| Hamidouche | Wassim | INSA de Rennes / IETR | France |
| Hannuksela | Miska | Nokia | Finland |
| Hara | Junichi | Ricoh company, ltd. | Japan |
| HARA | KAZUHIRO | NHK | Japan |
| HASHIMOTO | Ryoji | Renesas Electoronics | Japan |
| HATTORI | SALLY | Twentieth Century Fox | United States |
| He | Dake | BlackBerry | Canada |
| He | Yun | Tsinghua Univ. | China |
| He | Yuwen | InterDigital Communications | United States |
| Hearty | Paul | Sony Electronics, Inc. | United States |
| Hendry | FNU | Qualcomm | United States |
| HEO | JIN | LG Electronics | Korea |
| Hernaez | Mikel | Stanford University | United States |
| Herre | Juergen | Fraunhofer IIS | Germany |
| Hinds | Arianne | Cable Television Laboratories | United States |
| Hipple | Aaron | Netflix | United States |
| Hirabayashi | Mitsuhiro | SONY Corp. | Japan |
| HO | YO-SUNG | GIST | Korea |
| Hoang | Dzung | NXP Semiconductor | United States |
| Hofmann | Ingo | Fraunhofer IIS | Germany |
| Holland | James | Intel Corporation | United States |
| Hong | Seungwook | Arris | United States |
| Hsieh | Ted | Qualcomm | United States |
| Huang | Cheng | Nanjing Zhongxingxin Software Co.Ltd | China |
| Huang | Qi | Dolby | China |
| Huang | Tiejun | Peking University | China |
| Huang | Wei | Shanghai Jiao Tong University | China |
| Huang | Yu-Wen | MediaTek Inc. | China |
| Hughes | Kilroy | Microsoft | United States |
| Iacoviello | Roberto | RAI | Italy |
| Ichigaya | Atsuro | NHK | Japan |
| Ikai | Tomohiro | Sharp corporation | Japan |
| Ikeda | Masaru | Sony Electronics Inc. | United States |
| IMANAKA | Hideo | NTT | Japan |
| Ishikawa | Takaaki | Waseda University | Japan |
| Iwamura | Shunsuke | NHK | Japan |
| JANG | DALWON | Korea Electronics Technology Institute | Korea |
| Jang | EueeSeon | HanyangUniversity | Korea |
| Jang | In-su | ETRI | Korea |
| Jang | Si-Hwan | ETRI | Korea |
| Jang | Wonkap | Vidyo Inc. | United States |
| Januszkiewicz | Łukasz | Zylia Sp. z o.o. | Poland |
| Jasiński | Marcin | Imagination Ltd. | Poland |
| Jeon | Seungsu | SungKyunKwan Univ. | Korea |
| JEONG | JINHO | GreenCloud co.ltd. | Korea |
| Jeong | Min Hyuk | Myongji University | Korea |
| jiang | minqiang | santa clara university | United States |
| Jin | Guoxin | Qualcomm | United States |
| Jo | Bokyun | Kyunghee University | Korea |
| Jo | Bokyun | Kyunghee University | Korea |
| Jongmin | Lee | SK Telecom | Korea |
| Joo | Sanghyun | ETRI | Korea |
| Joshi | Rajan | Qualcomm | United States |
| Joveski | Bojan | USTARTAPP | France |
| JU | HYUNHO | Korea Electronics Technology Institute | Korea |
| JUN | DONGSAN | ETRI | Korea |
| Jung | Cheolkon | Xidian University | China |
| Jung | Joel | Orange Labs | France |
| Kaneko | Itaru | Tokyo Polytechnic University | Japan |
| Kang | DongNam | Nexstreaming | Korea |
| Kang | Jewon | Ewha W. University | Korea |
| KANG | JUNG WON | ETRI | Korea |
| Karczewicz | Marta | Qualcomm | United States |
| Kawamura | Kei | KDDI Corp. (KDDI R&D Labs.) | Japan |
| Keinert | Joachim | Fraunhofer IIS | Germany |
| Kerofsky | Louis | Interdigital | United States |
| Kervadec | Sylvain | Orange Labs | France |
| Kim | DaeYeon | Chips&Media Inc. | Korea |
| Kim | Duckhwan | ETRI | Korea |
| Kim | Hui Yong | ETRI | Korea |
| Kim | Ilseung | Hanyang Univ. | Korea |
| Kim | Jae Hoon | Apple | United States |
| Kim | Jae-Gon | Korea Aerospace University | Korea |
| Kim | Jungsun | MediaTek Inc | United States |
| Kim | Kyuheon | KyungHee Univ | Korea |
| Kim | Moo-Young | Qualcomm | United States |
| Kim | Namuk | Sungkyunkwan Univ. | Korea |
| Kim | Sang-Kyun | Myongji Unversity | Korea |
| Kim | Seung-Hwan | Sharp Labs of America | United States |
| Kim | Youngseop | Dankook University | Korea |
| Kimura | Takuto | NTT | Japan |
| Klenner | Peter | Panasonic | Germany |
| Ko | Hyunsuk | ETRI | Korea |
| Koenen | Rob | TNO | Netherlands |
| KOLAROV | Krasimir | APPLE | United States |
| Konstantinides | Konstantinos | Dolby Labs | United States |
| koo | bontae | etri | Korea |
| Kratschmer | Michael | Fraunhofer IIS | Germany |
| Krauss | Kurt | Dolby Laboratories Inc. | Germany |
| Kudumakis | Panos | Queen Mary University of London | United Kingdom |
| Kui | Fan | Pecking University， Shenzhen Graduated School | China |
| Kuntz | Achim | Fraunhofer IIS | Germany |
| Kwak | Youngshin | Ulsan National Institute of Science and Technology | Korea |
| Kwon | Oh-Jin | Sejong University | Korea |
| Ladd | Patrick | Comcast | United States |
| Lafruit | Gauthier | Université Libre de Bruxelles | Belgium |
| LAI | PoLin | MediaTek USA | United States |
| Lainema | Jani | Nokia | Finland |
| Laverty | Edward | DTS Inc. | United Kingdom |
| Lavric | Traian | Institut Mines-Télécom | France |
| Le Léannec | Fabrice | Technicolor | France |
| Lee | Bumshik | LG Electronics | Korea |
| Lee | Chang-kyu | ETRI | Korea |
| Lee | Dongkyu | Kwangwoon University | Korea |
| Lee | Hae | ETRI | Korea |
| Lee | Jae Yung | Sejong University | Korea |
| Lee | Jangwon | LG Electronics | Korea |
| Lee | Jin Young | ETRI | Korea |
| Lee | Jinho | ETRI | Korea |
| LEE | JUNGHYUN | Hanyang University | Korea |
| Lee | MyeongChun | Korea Electronics Technology Institute | Korea |
| Lee | Seungwook | ETRI | Korea |
| Lee | Sungwon | Qualcomm | United States |
| Lee | Taegyu | Yonsei University | Korea |
| LEE | Taejin | ETRI | Korea |
| Lee | Yong-Hwan | Far East University | Korea |
| Lee | Yung Lyul | Sejong University | Korea |
| Lei | Shawmin | MediaTek, Inc. | China |
| Levantovsky | Vladimir | Monotype | United States |
| Li | Ge | Peking University, Shenzhen Graduate School | China |
| LI | HAITING | Huawei Technologies Co., Ltd. | China |
| Li | Jisheng | Tsinghua University | United States |
| Li | Min | Qualcomm Inc. | United States |
| Li | Ming | ZTE Corporation | China |
| Li | Xiang | Qualcomm | United States |
| Li | Zhu | University of Missouri, Kansas City | United States |
| Lim | ChongSoon | Panasonic R&D Center Singapore | Singapore |
| Lim | Jaehyun | LG Electronics | Korea |
| Lim | Sung-Chang | ETRI | Korea |
| Lim | Sungwon | Sejong Univ. | Korea |
| Lim | Youngkwon | Samsung | United States |
| Lin | Ching-Chieh | ITRI | China |
| Lin | Chun-Lung | ITRI international | China |
| LIN | HUI-TING | ITRI/National Chiao Tung University | China |
| lin | tao | Tongji University | China |
| LIU | LI | Peking University | China |
| Liu | Shan | MediaTek | United States |
| liu | wenjun | huawei USA | United States |
| Lohmar | Thorsten | Ericsson | Germany |
| Lu | Ang | Zhejiang University | China |
| Lu | Taoran | Dolby Laboratories | United States |
| Luthra | Ajay | Arris | United States |
| ma | xiang | Huawei Technologies Co. Ltd | China |
| Macq | Benoit | UCL | Belgium |
| Malamal Vadakital | Vinod Kumar | Nokia | Finland |
| Mandel | Bill | Universal Pictures [Comcast] | United States |
| Maness | Phillip | DTS, Inc. | United States |
| Margarit | Dimitrie | Sigma Designs | United States |
| Marpe | Detlev | Fraunhofer HHI | Germany |
| Mattavelli | Marco | EPFL | Switzerland |
| MAZE | Frederic | Canon Research France | France |
| McCann | Ken | Zetacast/Dolby | United Kingdom |
| Minezawa | Akira | Mitsubishi Electric Corporation | Japan |
| Minoo | Koohyar | Arris Group Inc. | United States |
| Misra | Kiran | Sharp | United States |
| Mitrea | Mihai | Institut Mines Telecom | France |
| Morrell | Martin | Qualcomm | United States |
| Murtaza | Adrian | Fraunhofer IIS | Germany |
| Naccari | Matteo | BBC | United Kingdom |
| Nakachi | Takayuki | NTT | Japan |
| Nakagami | Ohji | Sony corporation | Japan |
| NAM | HYEONWOO | DONGDUK WOMEN'S UNIVERSITY | Korea |
| Narasimhan | Sam | Arris Inc | United States |
| Nasiopoulos | Panos | UBC | Canada |
| Natu | Ambarish | Australian Government | Australia |
| Navali | Prabhu | Ericsson | United States |
| Neuendorf | Max | Fraunhofer IIS | Germany |
| Neukam | Christian | Fraunhofer IIS | Germany |
| Nguyen | Tung | Fraunhofer HHI | Germany |
| NICHOLSON | Didier | VITEC | France |
| Norkin | Andrey | Netflix | United States |
| Numanagic | Ibrahim | Simon Fraser University | Canada |
| Ochoa | Idoia | Stanford University | United States |
| Oh | ByungTae | Korea Aerospace University | Korea |
| Oh | Hyun Mook | LG Electronics | Korea |
| OH | HYUN OH | WILUS Inc. | Korea |
| Oh | Kwan-Jung | ETRI | Korea |
| Oh | Sejin | LG Electronics | Korea |
| Ohm | Jens-Rainer | RWTH Aachen | Germany |
| Onders | Timothy | Dolby Laboratories | United States |
| Ostermann | Joern | Leibniz University Hannover | Germany |
| Oyman | Ozgur | Intel Corporation | United States |
| Pahalawatta | Peshala | AT&T Entertainment Group | United States |
| PALLONE | Gregory | Orange | France |
| Pan | Hao | Apple Inc. | United States |
| PANAHPOUR TEHRANI | Mehrdad | NAGOYA UNIVERSITY | Japan |
| Panusopone | Krit | ARRIS | United States |
| parhy | manindra | Nvidia | United States |
| Paridaens | Tom | Ghent University - iMinds - Multimedia Lab | Belgium |
| parikh | nidhish | Nokia Ltd | Finland |
| Park | Kyungmo | Samsung Electronics Co., Ltd. | Korea |
| Park | Min Woo | Samsung Electronics | Korea |
| Park | Sang-hyo | HanyangUniversity | Korea |
| PARK | YOUNGO | SAMSUNG | Korea |
| PENG | WEN-HSIAO | ITRI International/NCTU | United States |
| Pereira | Fernando | Instituto Superior Técnico | Portugal |
| Peters | Nils | Qualcomm | United States |
| Philippe | Pierrick | Orange | France |
| Piron | Laurent | Nagravision | Switzerland |
| Poirier | Tangi | Technicolor | France |
| Preda | Marius | Institut MINES TELECOM | France |
| Pu | Fangjun | Dolby Laboratories | United States |
| Qiu | Wenyi | Hisilicon | China |
| Quackenbush | Schuyler | Audio Research Labs | United States |
| Ramasubramonian | Adarsh Krishnan | Qualcomm Technologies Inc. | United States |
| Rapaka | Krishnakanth | Qualcomm Inc | United States |
| Reznik | Yuriy | Brightcove, Inc. | United States |
| Ridge | Justin | Nokia | Finland |
| ROH | DONGWOOK | LG ELECTRONICS | Korea |
| Rosewarne | Chris | Canon | Australia |
| Rouvroy | Gaël | Intopix | Belgium |
| Rusanovskyy | Dmytro | Qualcomm Inc. | United States |
| Said | Amir | Qualcomm Technologies, Inc. | United States |
| Salehin | S M Akramus | Qualcomm Technolgies Inc | United States |
| Samuelsson | Jonatan | Ericsson | Sweden |
| Sanchez de la Fuente | Yago | Fraunhofer HHI | Germany |
| Schierl | Thomas | Fraunhofer HHI | Germany |
| Seeger | Chris | NBCUniversal/Comcast | United States |
| Segall | Andrew | Sharp | United States |
| Sen | Deep | Qualcomm | United States |
| Senoh | Takanori | NICT | Japan |
| Seregin | Vadim | Qualcomm | United States |
| Setiawan | Panji | Huawei Technologies Duesseldorf GmbH | Germany |
| Shima | Masato | Canon Inc. | Japan |
| Shivappa | Shankar | Qualcomm Technologies Inc. | United States |
| Singer | David | Apple | United States |
| Skupin | Robert | Fraunhofer Heinrich Hertz Institute for Telecommunication | Germany |
| So | Youngwan | Samsung Elec. | Korea |
| Sodagar | Iraj | Microsoft | United States |
| Sohn | Yejin | Seoul Women's University | Korea |
| Sole | Joel | Qualcomm | United States |
| Song | Jaeyeon | Samsung | Korea |
| Song | Jeongook | Qualcomm | United States |
| Srinivasan | Ranga Ramanujam | Nvidia | United States |
| Stankiewicz | Olgierd | Poznan University of Technology | Poland |
| Stein | Alan | Technicolor | United States |
| Stockhammer | Thomas | Qualcomm Incorporated | Germany |
| Stolitzka | Dale | Samsung Electronics | United States |
| Strom | Jacob | Ericsson | Sweden |
| Su | Yeping | Apple Inc. | United States |
| Suehring | Karsten | Fraunhofer HHI | Germany |
| Sugimoto | Takehiro | NHK | Japan |
| Suh | Jong-Yeul | LG Electronics | Korea |
| Sullivan | Gary | Microsoft | United States |
| Sun | Haiwei | Panasonic R&D Center Singapore | Singapore |
| sun | wendell | Arris International | United States |
| Suzuki | Teruhiko | Sony Corporation | Japan |
| Swaminathan | Viswanathan (Vishy) | Adobe Systems Inc. | United States |
| Sychev | Maksim | Huawei Technologies | Russian Federation |
| Syed | Yasser | Comcast | United States |
| T. Pourazad | Mahsa | TELUS & UBC | Canada |
| Takabayashi | Kazuhiko | Sony Corporation | Japan |
| Tanimoto | Masayuki | Nagoya Industrial Science Research Institute | Japan |
| Teo | Han Boon | Panasonic | Singapore |
| Tescher | Andrew | Microsoft | United States |
| Thoma | Herbert | Fraunhofer IIS | Germany |
| Thomas | Emmanuel | TNO | Netherlands |
| Tian | Dong | Mitsubishi Electric Research Labs | United States |
| Toma | Tadamasa | Panasonic Corp. | Japan |
| Topiwala | Pankaj | FastVDO LLC | United States |
| Tourapis | Alexandros | Apple Inc | United States |
| Tu | Jih-Sheng | ITRI international | China |
| Tulvan | Christian | Mines-Telecom, Telecom Sud-Paris | France |
| Tung | Yi-Shin | MStar Semiconductor, Inc. | China |
| van Deventer | Oskar | TNO | Netherlands |
| Van Wallendael | Glenn | Ghent University - iMinds - Multimedia Lab | Belgium |
| Vanam | Rahul | InterDigital Communications | United States |
| Vetro | Anthony | Mitsubishi Electric | United States |
| Voges | Jan | Leibniz Universitaet Hannover | Germany |
| Wan | Wade | Broadcom Corporation | United States |
| Wang | Jian | Polycom | Canada |
| Wang | Ronggang | Peking University Shenzhen Graduate School | China |
| Wang | Xiaquan | Hisilicon | China |
| Wang | Ye-Kui | Qualcomm Incorporated | United States |
| Watanabe | Shinji | ITSCJ | Japan |
| Welch | Jim | IneoQuest Technologies | United States |
| Wenger | Stephan | Vidyo | United States |
| Willème | Alexandre | Université Catholique de Louvain (UCL) | Belgium |
| Won | Dongjae | Sejong Univ. | Korea |
| Wu | Kai | Panasonic R&D Center Singapore | Singapore |
| Wu | Ping | ZTE UK Ltd | United Kingdom |
| Wuebbolt | Oliver | Technicolor | Germany |
| XIANGJIAN | WU | Kwangwoon University | Korea |
| Xie | Qingpeng | Huawei | China |
| Xiu | Xiaoyu | InterDigital Communications Inc. | United States |
| Xu | Haiyan | HanyangUniversity | Korea |
| Xu | Jizheng | Microsoft | China |
| Xu | Xiaozhong | MediaTek | United States |
| XU | YILING | Shanghai Jiaotong University | China |
| Yamamoto | Yuki | Sony Corporation | Japan |
| Yang | Anna | Korea Aerospace Universiy | Korea |
| Yang | Haitao | Huawei Technologies Co., Ltd. | China |
| Yang | Jar-Ferr | National Cheng Kung University | China |
| YANG | JEONG MIN | Korea Electronics Technology Institute | Korea |
| Ye | Yan | InterDigital Communications | United States |
| Yea | Sehoon | LG Electronics | Korea |
| Yin | Jiaxin | Huawei | China |
| Yin | Peng | Dolby | United States |
| Yoon | Kyoung-ro | Konkuk University | Korea |
| YU | Lu | Zhejiang University | China |
| Yu | Yue | Arris | United States |
| Yun | JaeKwan | ETRI | Korea |
| Yun | Jihyeok | Kyung Hee University | Korea |
| Yun | Jihyeok | Kyunghee University | Korea |
| Zernicki | Tomasz | Zylia | Poland |
| Zhang | Li | Qualcomm | United States |
| Zhang | Louis | AMD | Canada |
| Zhang | Wenhao | Intel Corp. | China |
| ZHANG | XINGGONG | Peking University | China |
| ZHAO | WILF | VIXS | Canada |
| Zhao | Xin | Qualcomm Technologies, Inc. | United States |
| Zhao | Zhijie | Huawei Technologies Duesseldorf GmbH | Germany |
| Zhou | Jiantong | Huawei Technologies Co., LTD. | China |
| Zhou | Minhua | Broadcom | United States |
| Zhu | Jianqing | Fujitsu R&D Center | China |
| Zoia | Giorgio | Independent Consultant | Switzerland |
| Zou | Feng | Qualcomm | United States |

– Agenda

– Input contributions

– Output documents

– Requirements report

Source: Jörn Ostermann (Leibniz Universität Hannover)

– Systems report

Source: Young-Kwon Lim, Chair

– Video report

Source: Jens Ohm and Gary Sullivan, Chairs

– JCT-VC report

Source: Jens Ohm and Gary Sullivan, Chairs

– JCT-3V report

Source: Jens Ohm and Gary Sullivan, Chairs

– Audio report

Source: Schuyler Quackenbush, Chair

Table of Contents

1	Record of AhG meetings	3

1.1	AhG on 3D Audio Phase II	3

2	Opening Audio Plenary	8

3	Administrative matters	8

3.1	Communications from the Chair	8

3.2	Approval of agenda and allocation of contributions	8

3.3	Creation of Task Groups	8

3.4	Approval of previous meeting report	8

3.5	Review of AHG reports	8

3.6	Ballots to process	8

3.7	Received National Body Comments and Liaison matters	8

3.8	Joint meetings	9

3.9	Plenary Discussions	9

4	Task group activities	9

4.1	Joint Meetings	9

4.1.1	With Systems on 3D Audio PDAM 4	9

4.1.2	With All on MPEG Vision	10

4.1.3	With 3DG on Interactive 360 degree Media, VR and AR	11

4.1.4	With Requirements on New Profile Proposal	11

4.1.5	With All on Joint work between JPEG and MPEG	12

4.2	Task Group discussions	13

4.2.1	3D Audio Phase 1	13

4.2.2	3D Audio AMD 3 (Phase 2)	13

4.2.3	Maintenance	24

4.3	Discussion of Remaining Open Issues	27

5	Closing Audio Plenary and meeting deliverables	32

5.1	Discussion of Open Issues	32

5.2	Recommendations for final plenary	32

5.3	Disposition of Comments on Ballot Items	32

5.4	Responses to Liaison and NB comments	32

5.5	Establishment of Ad-hoc Groups	32

5.6	Approval of output documents	32

5.7	Press statement	32

5.8	Agenda for next meeting	32

5.9	All other business	32

5.10	Closing of the meeting	32

Annex A	Participants	33

Annex B	Audio Contributions and Schedule	35

Annex C	Task Groups	39

Annex D	Output Documents	40

Annex E	Agenda for the 115th MPEG Audio Meeting	43

# Record of AhG meetings

## AhG on 3D Audio Phase II

A meeting of the AhG on 3D Audio was held the 1300 – 1800 hrs on the Sunday prior to the 114th meeting of WG11 at the MPEG meeting venue.

3D Audio Phase 2 CEs

Total Components Coding (TCC)

Lukasz Januszkiewicz, Zylia, presented

| m37930 | Zylia Poznan Listening Test Site Properties | Jakub Zamojski, Lukasz Januszkiewicz, Tomasz Zernicki |  |
| --- | --- | --- | --- |

The contribution presents details on the Zylia listening room. This room meets BS.1116 requirements in terms of

- Aspect ratio

- Reverberation time as a function of frequency

Speakers are on the surface of a cylinder with radius of approximately 3 meters.

Lukasz Januszkiewicz, Zylia, presented

| m37932 | Corrections and clarifications on Tonal Component Coding | Lukasz Januszkiewicz, Tomasz Zernicki |  |
| --- | --- | --- | --- |

The contribution proposes syntax changes

- Add one bit and define a 2-bit field tccMode in the config()

This permits a one or alternatively two TCC “packets” of data per CPE.

Other corrections are proposed that that are either purely editorial or make specification text conform to reference software.

All experts present in the AhG meeting agreed to recommend to the Audio Subgroup to incorporate all changes in the contribution into a Study on MPEG-H 3D Audio DAM3 output document.

Christian Neukam, FhG-IIS, presented

| m37947 | Listening Test Results for TCC from FhG IIS | Sascha Dick, Christian Neukam |  |
| --- | --- | --- | --- |

The contribution reports on a cross-check listening test on the proposed Zylia TCC Core Experiment. In the test

- Sys1	RM

- Sys2	CE technology using OFDT-based synthesis

In absolute MUSHRA scores, no items different, mean not different

In differential MUSHRA scores, 1 item better for Sys2, mean not different, but mean value better by 1 MUSHRA point.

Lukasz Januszkiewicz, Zylia, presented

| m37933 | Low Complexity Tonal Component Coding | Tomasz Zernicki, Lukasz Januszkiewicz, Andrzej Rumiaski, Marzena Malczewska |  |
| --- | --- | --- | --- |

The contribution, along with the previous cross-checks, consists of a complete CE proposal.

The contribution explores whether a Low Compexity TCC might be appropriate for the Low Complexity Profile. The “RM” baseline was

- MPEG-H 3DA LC RQE with IGF active

The point of the experiment is that the TCC is able to work with the IGF tool. The contribution reports on a listening test on the proposed Zylia TCC Core Experiment. In the test

- Sys1	RM

- Sys2	CE technology using ODFT-based synthesis

In absolute MUSHRA scores, no items different, mean not different

In differential MUSHRA scores, 3 items better for Sys2, mean better, mean value better by 1.5 MUSHRA point.

The presenter noted that the number of Tonal Components is typically small (e.g. less than 3 per core channel), in which case the Time Domain tone synthesis technique would fit with a Low Complexity use case. The presenter noted that low complexity could be guaranteed via restrictions

The Chair clarified that the following issues and questions are on the table:

- TCC works with IGF (as demonstrated in the listening test)

- We might assume that TD synthesis is higher quality that ODFT synthesis

- We need to investigate the maxium number of TC per core audio channel

This will continue to be discussed and brought up later in the week.

High Resolution Envelope Processing (HREP)

Seungkwon Beack, ETRI, presented

| m37833 | ETRI's cross-check report for CE on High Resolution Envelope Processing | Seungkwon Beack, Taejin Lee |  |
| --- | --- | --- | --- |

The contribution presents a cross-check listening test or HREP. Tested were:

- 48 kb/s, 128 kb/s

- 8 items (stereo)

- 11 listeners

- Listening via headphones

- Sys1 – HREP

- Sys2: - 3D Audio RM

48 kb/s

- Absolute: 4 better, overall better

- Differential: 8 better (i.e. all better), overall better by 9 points (value is ~65)

128 kb/s

- Absolute: 1 better, overall better

- Differential: 2 better, overall better. Overall better by 2 points (value is ~92)

The Chair presented, on behalf of FhG-IDMT experts

| m37715 | Cross Check Report for CE on HREP (Test Site Fraunhofer IDMT) | Judith Liebetrau, Thomas Sporer, Alexander Stojanow |  |
| --- | --- | --- | --- |

The contribution presents a cross-check listening test or HREP

5.1 channel, 128 kb/s

- Absolute: no difference

- Differential: 3 better (only applause items), overall no difference

Stereo, 48 kb/s

- Absolute: overall better

- Differential: 5 better, overall better

Stereo 128 kb/s

- Absolute: no difference

- Differential: no difference

Christian Neukam, FhG-IIS, presented

| m37889 | 3DA CE on High Resolution Envelope Processing (HREP) | Sascha Disch, Florin Ghido, Franz Reutelhuber, Alexander Adami, Juergen Herre |  |
| --- | --- | --- | --- |

The contribution, along with the previous cross-checks, consists of a complete CE proposal.

The presenter motivated the need for the HREP tool – in short that applause-like signals are common in many scenarios, particularly broadcast of live performances.

The technology is an independent, single-channel pre- and post-processing tool whose side information rate is 1 to 4 kb/s for stereo (i.e. 2 channels).

Complexity is dominated by the 50% overlap real-valued DFT/IDFT, which is approximately 2.7 WMOPS. Worst case is 3.4 WMOPS when other processing is added.

For LC Profile, it is proposed to limit the number of HREP for channels/objects. Further, the presenter noted that if the gain is 1, then the DFT/IDFT does not need to be executed. For LC Profile, it is proposed that HREP

- No more than 8 core audio channels use HREP at any instant

- No more than 50% HREP frames (i.e. the 64-frame hop) are active with HREP.

The presenter showed activation plots (not included in the contribution) that indicated that HREP is active for almost 100% of the frames for the applause items, and almost none of the frames for one non-applause item.

The presenter noted that, to a large extent, the HREP coding is independent of core coder bitrate.

FhG-IIS conducted the same listening tests as reported in the previous cross-checks. The test items in these tests were:

5.1 channel, 128 kb/s

- 7 applause items

Stereo, 48 kb/s and 128 kb/s

- 11 MPEG Surround item, plus 2 additional applause items

Test results were:

5.1 channel, 128 kb/s

- differential: 4 better, overall better

48 kb/s stereo

- 2 better in absolute score

- 7 of 8 better in differential, overall better, mean improvement more than 10 mushra points

128 kb/s stereo

- 2 better, overall better in absolute by 5 mushra points

- 6 of 8 better in differential, mean better

The contribution presented in ANNEX B test outcomes when all listening test data is pooled .

5.1 channel, 128 kb/s

- 4 better, overall better

48 kb/s stereo

- 8 (all) better in differential, by as much as 15 mushra points, overall better, by 10 mushra points

128 kb/s stereo

- 6 better in differential, overall better. Overall improvement of 3 mushra points.

There was some discussion as to exactly where the HREP post-processor was in the 3D Audio decoder. The presenter noted that a figure in the contribution makes this very clear. It was concluded that HREP is applicable to channels and discrete objects (i.e. not SAOC objects). The contribution does not cover HOA content, and the Chair concluded that it may be too late in the Phase 2 timeline to contemplate application to HOA content.

In summary, the contribution requests

- That HREP technology be accepted into the MPEG-H 3D Audio standard

- That HREP be included in the LC Profile with the recommended constraints

All experts present in the AhG meeting agreed to recommend to the Audio Subgroup to incorporate the HREP technology into a Study on MPEG-H 3D Audio DAM3 output document and also into the High Profile.

Issues of acceptance into LC profile will continue to be discussed.

HOA Issues

Gregory Pallone, Orange, presented

| m37894 | Proposed modifications on MPEG-H 3D Audio | Gregory Pallone |  |
| --- | --- | --- | --- |

The contribution notes that when presenting via loudspeakers and listening in the near field, the perceived spatial cues, e.g. interaural level, may be incorrect. It gives use cases in which such near-field listening will occur, e.g. inside a car.

The results of an experiment are reported, in which far-field and near-field presentation are simulated using binaural rendering and presentation. Near Field Compensation (NFC) simulates moving the speakers further from the listener.

The contribution proposes to modify the 3D Audio specification in two places as follows:

Preprocessing block NFC processing (should be switched active if UseNfc is true and the speaker listener distance rmax is samller NfcReference Distance), pre-processing block DRC-1 for HOA and as an alternative to rendering to loud-speakers, a computational efficient binaural rendering directly using the HOA coefficients (H2B, see 13.3.1). Computational more efficient but mathematically equivalent ways to implement the processing chain may be found in Annex G.

with:

Preprocessing block NFC processing (should be switched active if rmax < NfcReferenceDistance in case UsesNfc flag is active, or if rmax < 1.5 meters in case UsesNfc flag is inactive, with rmax the maximum speaker distance of the listening setup), pre-processing block DRC-1 for HOA and as an alternative to rendering to loud-speakers, a computational efficient binaural rendering directly using the HOA coefficients (H2B, see 13.3.1). Computational more efficient but mathematically equivalent ways to implement the processing chain may be found in Annex G.

Nils Peters, Qualcomm, noted that the contribution uses a very regular set of loudspeaker positions, and wondered if the tested quality might be less with e.g. the MPEG-H 3D Audio 22.2 loudspeaker positions.

Oliver Weubolt, Technicolor, questioned how realistic or prevelant is the use case of the close-placed loudspeaker listening.

The Chair asked experts work together to draft the intent of the Orange proposal in more clear and concise language. This topic will continue to be discussed.

AhG Report

The Chair presented

| m37901 | Report of AHG on 3D Audio and Audio Maintenance | Schuyler Quackenbush |
| --- | --- | --- |

Experts agreed that the report represents the AhG activity. The Chair will upload it as a contribution document.

The AhG meeting was adjourned at 5:50pm

# Opening Audio Plenary

The MPEG Audio Subgroup meeting was held during the 114th meeting of WG11, February 22-26, San Diego, USA.  The list of participants is given in Annex A.

# Administrative matters

## Communications from the Chair

The Chair summarised the issues raised at the Sunday evening Chair’s meeting, proposed task groups for the week, and proposed agenda items for discussion in Audio plenary.

## Approval of agenda and allocation of contributions

The agenda and schedule for the meeting was discussed, edited and approved. It shows the documents contributed to this meeting and presented to the Audio Subgroup, either in the task groups or in Audio plenary. The Chair brought relevant documents from Requirements, Systems to the attention of the group. It was revised in the course of the week to reflect the progress of the meeting, and the final version is shown in Annex B.

## Creation of Task Groups

Task groups were convened for the duration of the MPEG meeting, as shown in Annex C. Results of task group activities are reported below.

## Approval of previous meeting report

The Chair asked for approval of the 113th Audio Subgroup meeting report, which was registered as a contribution. The report was approved.

| m37805 | 113th MPEG Audio Report | Schuyler Quackenbush |  |
| --- | --- | --- | --- |

## Review of AHG reports

There were no requests to review any of the AHG reports.

| m37902 | AHG on 3D Audio and Audio Maintenance | ISO secretariat |  |
| --- | --- | --- | --- |
| m37901 | AHG on Responding to Industry Needs on Adoption of MPEG Audio | ISO secretariat |  |

## Ballots to process

The following table indicates the ballots to be processed at this meeting.

| WG11 Doc | Title | Closes | Ballot |
| --- | --- | --- | --- |
| 15166 | ISO/IEC 13818-1:201x/DAM 5 | 2015-12-25 | 37555 |
| 15826 | ISO/IEC 14496-3:2009/Amd.3:2012/DCOR 1 | 2016-02-10 | 37573 |
| 15828 | ISO/IEC 14496-3:2009/PDAM 6, Profiles, Levels and Downmixing Method for 22.2 Channel Programs | 2015-12-26 | 37553 |
| 15838 | ISO/IEC 23003-3:2012/Amd.1:2014/DCOR 2 | 2016-01-26 | 37640 |
| 15392 | ISO/IEC 23003-3:2012/DAM 3 DRC and IPF |  | 37560 |
| 15842 | ISO/IEC 23003-4:2015 PDAM 1, Parametric DRC, Gain Mapping and Equalization Tools |  | 37643 |
| 15847 | ISO/IEC 23008-3:2015/DAM 2, MPEG-H 3D Audio File Format Support |  | 37559 |

## Received National Body Comments and Liaison matters

The Liaison statements were presented, discussed, and resources to draft responses were allocated.

| Number | Title | Topic |
| --- | --- | --- |
| m37580 | Liaison Statement from ITU-R SG 6 on ITU-R BS.1196-5 | ITU-R SG 6 via SC 29 Secretariat |
| m37655 | m37655: Liaison Statement from DVB on MPEG-H Audio | DVB |
| m37589 | IEC CD 61937-13 and 61937-14 | IEC TC 100 via SC 29 Secretariat |
| m37590 | IEC CD 61937-2 Ed. 2.0/Amd.2 | IEC TC 100 via SC 29 Secretariat |
| m37596 | IEC CDV MIDI (MUSICAL INSTRUMENT DIGITAL INTERFACE) SPECIFICATION 1.0 (ABRIDGED EDITION, 2015) | IEC TC 100 via SC 29 Secretariat |
| m37597 | IEC NP MIDI (MUSICAL INSTRUMENT DIGITAL INTERFACE) SPECIFICATION 1.0 (ABRIDGED EDITION, 2015) | IEC TC 100 via SC 29 Secretariat |
| m37651 | IEC NP Microspeakers | IEC TC 100 via SC 29 Secretariat |
| m37652 | IEC NP Multimedia Vibration Audio Systems - Method of measurement for audio characteristics of audio actuator by pinna-conduction | IEC TC 100 via SC 29 Secretariat |
| m37658 | IEC CD 60728-13-1 Ed. 2.0 | IEC TC 100 via SC 29 Secretariat |

## Joint meetings

| Groups | What | Where | Day | Time |
| --- | --- | --- | --- | --- |
| Audio, Systems | Carriage of MPEG-H Systems data in MPEG-H 3D Audio m37531 Study Of 23008-3 DAM4 (w15851) - Carriage Of Systems Metadata, Michael Dolan, Dave Singer, Schuyler Quackenbush m37896 Study on Base Media File Format 14496-12 PDAM1 | Audio | Tue | 0900-1000 |
| All | MPEG Vision | Audio | Wed | 1130-1300 |
| Audio, 3DV | MPEG-H 3D Audio and VR, AR | Audio | Thu | 1000-1100 |
| Audio, Req | Possible future MPEG-H 3D Audio profiles m37832 MPEG-H Part 3 Profile Definition | Audio | Thu | 1100-1200 |
| All | 360 Media | Audio | Thu | 1530-1600 |

## Plenary Discussions

Henney Oh, WILUS, presented

| m37987 | Information on Korean standard for terrestrial UHD broadcast services | Henney Oh |  |
| --- | --- | --- | --- |

The presenter reviewed the information from NGBF (m37104) that was submitted to the 113th MPEG meeting. At this meeting, this contribution notes that MPEG-H 3D Audio was selected and as the audio broadcast technology, and specifically the Low Complexity Profile. Schedule

- 2Q trial

- 4Q public roll-out

The NGBF envisions 16-channel input and 12-channel output.

The Chair was delighted to state that the Korean NGBF is the first customer of MPEG-H 3D Audio.

# Task group activities

In this report consensus positions of the Audio subgroup are highlighted in yellow. Other text captures the main points of presentations and subsequent discussion.

## Joint Meetings

### With Systems on 3D Audio PDAM 4

The Audio Chair presented

| m37531 | Study Of 23008-3 DAM4 (w15851) - Carriage Of Systems Metadata | Michael Dolan, Dave Singer, Schuyler Quackenbush |  |
| --- | --- | --- | --- |

The contribution proposes to replace the DAM4 text from the 113th meeting with new text that specifies a new signalling mechanism using UUID as opposed to a field value specified in the MPEG-H 3D Audio specification.

It was the consensus of the Audio and Systems experts to issue the contribution text as Study on ISO/IEC 23008-3 DAM4.

| m37896 | Study on Base Media File Format 14496-12 PDAM1 |  |  |
| --- | --- | --- | --- |

It was the consensus of the Audio and Systems experts to issue the contribution text as ISO/IEC 14496-14/DAM 1. The ballot comments were reviewed and an acceptable response was determined.

### With All on MPEG Vision

Rob Koenen, TNO, reviewed N15724, from the 113th meeting, which captured the status of MPEG Vision. Many experts contributed to the discussion.

The concept of MPEG Vision is

- A 5 year time horizon

- Stakeholders

  - Industry that uses MPEG specifications

  - Companies and institutions that participate in MPEG

  - The organizations in liaison with MPEG

- Establish dialog with industry, via WG11 output documents, to bring MPEG Vision to their attention for both participation and feedback

Vision topics are succinctly captured in an Annex of N15724

A next version of the MPEG Vision document could be in the following format:

- Introduction

- MPEG technology has enabled new markets

  - MP3 enabled Internet music delivery

  - Media compression that enabled wireless streaming media to SmartPhones

- Why MPEG is uniquely able to address the emerging needs of industry (high quality technology due to internal competitive phase, rigorous conformance and reference software testing).

- Emerging Trends

  - Increasing supply and demand of media

  - Social media

  - Mobile high-speed networking

    - That is always available

  - Broadband/Broadcast convergence

  - Internet of Things

  - Cloud computing and storage

  - Big Data, machine learning, search and discovery

  - Using above to improve customer experience (the “individual” end-user and the business application user).

  - Facilitating richer media authoring and presentation

  - Facilitating richer user to user communication

  - Facilitate seamless media processing chains, e.g. via Common Media Format

- Issues

  - Security

- Specific Topic Keywords (e.g. taken from aspects of Trends), followed by several sentences of exciting text. It may be desirable to also have a figure to communicate more effectively.

- Each specific topic could be associated with 30 seconds of evangelizing video, to be compiled into the “MPEG Vision Video”

- Specific ask to potential customers:

  - What are roadblocks?

  - What is level of interest?

  - When is it needed?

What will MPEG offer between now and 2020?

What can Audio experts contribute? At least a summary of emerging trends in audio and more specifically, audio compression.

### With 3DG on Interactive 360 degree Media, VR and AR

The Chair showed figure from 113th Audio report on the Interactive 360 degree Media joint meeting and noted that objects in the VR model have both (yaw, pitch, roll) and (x, y, z) parameters. The 3DV Chair noted that objects can be virtual sound sources, “users” or even rooms. In this respect, rooms can also have associated reverberation properties. The Audio Chair noted that if a higher level process (e.g. visual engine) in Augmented Reality use case assesses room properties such as dimension, acoustic reflectivity, reverberation, then Audio can react to Augmented Reality is the same way as Virtual Reality.

This need may trigger Audio to define interfaces to AR or VR engines and also create acoustic simulation (e.g. reverberation) technology.

### With Requirements on New Profile Proposal

Christof Fersch, Dolby, presented

| m37832 | MPEG-H Part 3 Profile Definition | Christof Fersch |  |
| --- | --- | --- | --- |

This is a joint input contribution from Dolby, DTS, Zylia, which proposes a new profile. The presenter noted that the proposed new profile has two main objectives:

- Efficient support of object-based immersive content

- Efficient integration into products supporting multiple formats

It is anticipated that a renderer would be out of scope for this profile, such that device manufacturers could add value or differentiate with their own renderer.

Relative to LC profile, it proposed tools

- Add: eSbr, MPS212, SAOC-3D, IC, TCC

- Remove: Format Converter, Object Renderer, HOA, Binaural, System metadata carriage

Jon Gibbs, Huawei, stated that Huawei supports the proposed profile since they desire to provide their own renderer.

Marek Domanski Polish National Body, stated support for a profile that does not include a renderer.

Max Neuendorf, FhG-IIS, noted that requested profile fails to address requirement of rendering.

Deep Sen, Qualcomm, asserted that the authors of the contribution are also the main competitors with MPEG-H 3D Audio in the marketplace. He further noted that a normative behaviour, including rendering, permits broadcasters to fulfil the regulatory requirements of e.g. the CALM act.

Juergen Herre, IAL/FhG-IIS, noted that SAOC-3D cannot provide high-quality individual objects as envisioned by the contribution.

Gregory Pallone, Orange, expressed the point of view of Orange as a broadcaster. Orange does not support non-normative rendering, and is concerned about using only some other renderer.

Matteo Naccari, BBC, stated that BBC wishes to have complete control of the complete broadcast chain, and hence does not support this proposal.

Jon Gibbs, Huawei, noted that this a fourth profile in MPEG-H 3D Audio. Huawei supports the possibility of providing its own renderer as a means to differentiate their products in the market. Further, he stated that Huawei, as a mobile handset device manufacturer, is very familiar with standards where end-to-end quality needs to be maintained and in those markets the network operators subsidise the handsets in order to justify this end-to-end control.

David Daniels, Sky Europe, stated support for the proposed profile.

Ken McCann, speaking as DVB liaison officer, noted that the Liaison to MPEG from DVB in m37655 includes DVB’s Commercial Requirements for Next Generation Audio which reflects opinions expressed in the room –that there is support for both normative and informative renders.

Yasser Syed, Comcast, stated that profiles should be responsive to market needs.

Matteo Naccari, BBC, stated that when broadcast consumers complain, they complain to BBC.

The Chair proposed that Audio experts draft a WG11 document that captures the proposal for careful study but on a timeline independent of DAM 3.

In addition, Audio could draft a resolution requesting that experts in the broadcast industry review the document and comment via contribution documents.

Furthermore, Audio could draft a Liaison template addressed to appropriate application standards organizations.

### With All on Joint work between JPEG and MPEG

The AhG Chair, Arienne Hines, CableLabs, gave a presentation on the plan for joint work. She presented a diagram on workflow, which Audio experts can find in the notes on the Joint Meeting on 360 degree Media as documented in the 113th MPEG Audio report.

Visual experts have proposed a Light Field representation. The Audio Chair stated that Audio experts could envision sound field analysis/synthesis as being applicable.

The work address end-to-end workflow, and the goal of the joint meeting was to fill in the headings for Audio. Candidate headings were:

- Audio Applications of Conceptual Workflow

- Technologies supporting Audio

- Attributes and Commonalities of Audio Technologies

Marius Preda, Univ Mines, noted that there can be sound fields and sound objects, and that both may be appropriate for this study.

Interested Audio experts will follow this work and progress document N16150 and N15971.

## Task Group discussions

### 3D Audio Phase 1

Phase I Corrections

Max Neuendorf, FhG-IIS, presented

| m37885 | Proposed DCOR to MPEG-H 3D Audio edition 2015 | Max Neuendorf, Achim Kuntz, Simone Fueg, Andreas Hoelzer, Michael Kratschmer, Christian Neukam, Sascha Dick, Elena Burdiel, Toru Chinen |  |
| --- | --- | --- | --- |

The contribution proposed numerous corrections and clarifications to the 3D Audio base text.

The Chair noted that, procedurally, it is proper to address Phase 1 corrections with a DCOR, and Phase 2 corrections with a Study on text, but at the 115th MPEG meeting is it expected that both texts are merged to create MPEG-H 3D Audio Second Edition.

The presenter reviewed the corrections proposed in the contribution.

Gregory Pallone, Orange, noted that in HOA binaural rendering there can be two BRIR filter sets: normal and H2B, and that this conflicts with the proposed change: signalling which BRIR to use. The presenter stated that he would consult with BRIR experts back at the office and bring back a recommendation for further discussion.

With the exception of one proposed correction discussed in the preceding paragraph, it was the consensus of the Audio subgroup to incorporate all changes proposed in the contribution into ISO/IEC 23008-3:2015/DCOR 1 Corrections, to issue from this meeting.

### 3D Audio AMD 3 (Phase 2)

Kai WU, Panasonic Singapore, presented

| m37827 | Proposed simplification of HOA parts in MPEG-H 3D Audio Phase 2 | Hiroyuki EHARA, Sua-Hong NEO, Kai WU |  |
| --- | --- | --- | --- |

The contribution raises concerns on Near Field Compensation (NFC) in LC Profile.

The contribution notes the following:

To avoid creating such a confusing and difficult standard, this alternative option between “lower HOA order with NFC” and “higher HOA order without NFC” should be removed, and the low complexity should be guaranteed for the HOA tools. There are four options of countermeasure as follows:

1)  Always enable NFC (no order restriction on the NFC usage)

2)  Always enable NFC (reduce the HOA order restriction in each level to the order where NFC can be applied)

3)  Always disable NFC (LCP does not support NFC)

4)  Disable HOA (LCP does not support HOA)

The contribution discusses how each option could be specified in the LC profile text.

In conclusion, the presenter stated support for option 3), which would require the following text:

If option-3 is chosen,

- remove NFC from LCP in Table P1 in [1] and the corresponding “Note 1”,

- change the “Note 6” in Table P1 in [1] to “Note 6: In order to meet target complexity for the profile/levels, implementers shall use the low-complexity HOA decoder and renderer”,

- remove NFC processing text after Table P4 in [1], and

- add the following text in the introduction part of Section 18 in [1]: “This section specifies the low-complexity HOA decoding and rendering algorithm. In the low-complexity profile, this section overrides the original sections of “HOA decoding” and “HOA rendering” for achieving a reduced complexity, otherwise this section is informative.”

The Chair noted that there are two components to the option 3 proposal:

- Remove NFC from LC Profile

- Mandate use of the low complexity HOA decoding found in Annex G

Max Neuendorf, FhG-IIS, stated that “option 3” proposal would lead to simpler, lower-complexity implementations.

The Chair recommended that experts continue to discuss the issues raised by the Orange

Oliver Wuebbolt, Technicolor, presented

| m37770 | Corrections and Clarifications on MPEG-H 3D Audio DAM3 | Oliver Wuebbolt, Johannes Boehm, Alexander Krueger, Sven Kordon, Florian Keiler |  |
| --- | --- | --- | --- |

The contribution proposed corrections and clarifications to the DAM3 text concerning HOA processing.

- Clarification of the order of DRC and NFC processing, with both text and a figure.

- Restrict application of NFC to only one HOA channel group

- Other corrections and clarifications

There was discussion on NFC and HOA channel groups between Gregory Pallone, Orange and the presenter. The Chair suggested that this one topic needs further discussion.

With the exception of NFC and HOA channel groups, it was the consensus of the Audio subgroup to incorporate all changes proposed in the contribution into the Study on ISO/IEC 23008-3:2015/DAM 3, to issue from this meeting.

Nils Peters,  Qualcomm, presented

| m37874 | Thoughts on MPEG-H 3D Audio | Nils Peters, Deep Sen, Jeongook Song, Moo Young Kim |  |
| --- | --- | --- | --- |

The contribution has two categories of proposals

- Extension of CICP tables

- HOA issues

Pre-binauralized Stereo

It proposes to signal “stereo that is binauralized” as a CICP index, specifically index 21. This must be added to a table in MPEG-H and a table in CICP . Further, such signals should be normatively specified to be processed with only certain outputs.

Achim Kuntz, FhG-IIS, noted that the WIRE output might facilitate processing of pre-binauralized stereo.

Gregory Pallone, Orange, reminded experts of their contribution to the previous MPEG meeting, in which an ambiance signal is provided as pre-binauralized stereo and an object it mixed onto that using a personal BRIR.

Coverage of ITU-R Speaker Configurations

The contribution proposes to add ITU-R speaker configurations to CICP and 3D Audio tables.

Support for Horizontal-Only HOA

Currently, the 3D Audio HOA tools to not have any directivity that lies directly on the horizontal plane.  This can be resolved via an additional 64-value codebook and without any changes to bitstream syntax.

Screen-related Adaptation for HOA

In the current specification, HOA audio sound stage adaptation can result is peaks in computational complexity. The presenter noted that an implementation-dependent solution is to pre-compute the adaptation matrix for each production and decoder screen size combination.

The contribution proposes an alternative signalling of production screen size.

HOA and Static Objects

If a program consists of an HOA scene and e.g. 3 static dialog objects, the contribution suggests that the HOA renderer be used for the static dialog objects.

Michael K, FhG-IIS, noted that switch group interactivity (e.g. dialog level) is not supported in HOA rendering. Gregory Pallone, Orange, noted that it should be possible.

The Chair suggested that both of the preceding issues needs more discussion, and will bring it up later in the week after all other contributions have been presented.

Achim Kuntz, FhG-II, presented

| m37892 | Review of MPEG-H 3DA Metadata | Simone Feug, Christian Ertel, Achim Kuntz |  |
| --- | --- | --- | --- |

The contribution was triggered by feedback from FhG-IIS implementers. The presenter noted that there are two disctinct categories of 3D Audio metadata:

- User interaction

- Decoding and rendering

Currently, most Audio Scene Interaction (ASI) metadata is provided in the MHAS layer, but this does not contain all ASI metadata.

The contribution proposes to

- Move rendering metadata from ASI to config and extension elements. In this way the decoder can be set up after parsing the config() element.

- Add other user interaction metadata to ASI. In this way, decoder user interface can be set up after parsing ASI.

The presenter noted that no metadata is added, and none is removed in the proposed changes.

It was the consensus of the Audio subgroup to adopt the proposed changes into the Study on MPEG-H 3D Audio DAM3.

Max Neuendorf, FhG-IIS, presented

| m37897 | Review of MPEG-H 3DA Signaling | Max Neuendorf, Sascha Dick, Nikolaus Rettelbach |  |
| --- | --- | --- | --- |

The contribution proposes several minor changes to signalling methods in MPEG-H 3D Audio.

It proposed to change:

- Signaling of start and stop indices in IGF such that they better match the acuity of human auditory system. This would be by increasing granularity by a factor of 2. This would require adding two bits, one for start and one for stop.

- Signaling of Stereo Filling in Multichannel Coding Tool (MCT). This would permit stereo filling to be used in MCT. The contribution includes results of a listening test that shows the improvement in performance when using Stereo Filling in MCT.

  - With differential scores, 3 items better, one by nearly 20 MUSHRA points. These are exactly the items with the worst performance when using the current 3D Audio technology.

- Signal crossfade (or not), such that crossfades are not mandated when they don’t make sense, e.g. when transitioning from one program to another. In addition, the contribution to removes the need for redundant config() information at the AudioPreRoll() level.

It was the consensus of the Audio subgroup to adopt the proposed changes into the Study on MPEG-H 3D Audio DAM 3.

Sang Bae Chon, Samsung, presented

| m37853 | Clarifications on MPEG-H PDAM3 | Sang Bae Chon, Sunmin Kim |  |
| --- | --- | --- | --- |

The contribution notes errors in the Internal Channel portion of the DAM 3 text and also Reference Software. It proposes the following corrections to the text, each of which were reviewed by the presenter.

| No | Change Type | Descriptions |
| --- | --- | --- |
| 1 | Syntax | Configuration bitstream correction. |
| 2 | Editorial | Typo |
| 3 | Editorial | Missing a group and clarifications |
| 4 | Editorial | Clarification on the “output” channel |
| 5 | Editorial | Clarification on the “output” channel |
| 6 | Editorial | Clarification on the figure |
| 7 | Editorial | Typo and clarification |
| 8 | Editorial | Detail description of signal and parameter flow in Figure |
| 9 | Editorial | Detail description of signal and parameter flow in Figure |
| 10 | Editorial | Clarification on the equation |
| 11 | Editorial | Typo |

In addition, it proposes two bug fixes in the RM6 Reference Software.

It was the consensus of the Audio subgroup to adopt the proposed changes into the Study on MPEG-H 3D Audio DAM 3.

Max Neuendorf, FhG-IIS, presented

| m37863 | Proposed Study on DAM3 for MPEG-H 3D Audio | Christian Neukam, Michael Kratschmer, Max Neuendorf, Nikolaus Rettelbach, Toru Chinen |  |
| --- | --- | --- | --- |

The contribution proposes numerous editorial or minor changes to the DAM 3 text from the 113th MPEG meeting, as shown in the following table.

| Issue | Changes Text? | Changes Ref Soft? | Changes Bitstr Config | Changes Bitstr Payload | due to signal processing | due to side effects |
| --- | --- | --- | --- | --- | --- | --- |
| Application of Peak Limiter | Y | Y | - | - | Y (only at high target loudness) | - |
| Default Parameters for DRC decoder | Y | Y | - | - | Y (only at high target loudness) | - |
| Corrections in Technical Overview | Y | - | - | - | - | - |
| Clarification on IGF Whitening | Y | - | - | - | - | - |
| Correction in TCX windowing | Y | - | - | - | - | - |
| Clarification on post-processing of the synthesis signal (bass post filtering) | Y | - | - | - | - | - |
| Update of description of Adaptive Low-Frequency De-emphasis | Y | - | - | - | - | - |
| Correction of wrap around in MCT | Y | - | - | - | - | - |
| Clarification on totalSfb | Y | - | - | - | - | - |
| Correction of inter-frame dependencies | Y | Y | - | Y | - | Y |
| Alignment of bitstream element names and semantics for screen-related remapping | Y | - | - | - | - | - |
| Removal of unnecessary semantics | Y | - | - | - | - | - |
| Correction of remapping formulas | Y | - | - | - | - | - |
| Replacement of Figure for screen-related remapping | Y | - | - | - | - | - |
| Correction of non-uniform spread | Y | - | - | - | - | - |
| Application of spread rendering | Y | Y | - | - | - | Y |
| Clarification of the relationship of scene-displacement processing and DRC | Y | - | - | - | - | - |
| Clarification on the processing of scene-displacement data | Y | - | - | - | - | - |
| Definition of ‘atan2()’ | Y | - | - | - | - | - |
| Correction of the HOA transform matrix | Y | - | - | - | - | - |
| Gain interaction as part of the metadata preprocessing | Y | - | - | - | - | - |
| Clarification of behavior after divergence processing | Y | - | - | - | - | - |
| Gain of original and duplicated objects (divergence) | Y | - | - | - | - | - |
| Exclusion of LFEs from diffuseness processing | Y | - | - | - | - | - |
| Gain adjustment of direct and diffuse paths | Y | - | - | - | - | - |
| Routing of diffuse path | Y | - | - | - | - | - |
| Correct reference distance in doubling factor formulas | Y | - | - | - | - | - |
| Fix of behavior for smaller radius values | Y | - | - | - | - | - |
| Minimum radius for depth spread rendering | Y | - | - | - | - | - |
| Correction in mae_Data() | Y | - | - | - | - | - |
| Correction of excluded sector signaling | Y | Y | - | - | - | - |
| Clarifications wrt. receiverDelayCompensation | Y | Y | - | - | - | - |
| Internal Channel signaling correction | Y | Y | Y | Y | - | Y |
| Editorial correction to Section 8 Updates to MHAS | Y | - | - | - | - | - |
| Typos | Y | - | - | - | - | - |

It was the consensus of the Audio subgroup to adopt the proposed changes into the Study on MPEG-H 3D Audio DAM 3.

3D Audio Profiles

Christof Fersch, Dolby, presented

| m37832 | MPEG-H Part 3 Profile Definition | Christof Fersch |  |
| --- | --- | --- | --- |

This a joint input contribution from Dolby, DTS, Zylia, which proposes a new profile, Broadcast Baseline. The presenter noted that Dolby Atmos and DTX DTS-X have cinema sound formats that are composed only of dynamic objects.

The presenter described a Common Receiver Broadcast Receiver architecture in which there might be multiple audio decoders that interface to a separate rendering engine.

In conclusion, the presenter requested that the new profile definition be included in the Study on DAM 3.

Discussion

Gregory Pallone, Orange, asked why the binaural rendering was removed from the profile proposal. The presenter responded that the profile does not include any rendering technology.

Juergen Herre, IAL/FhG-IIS, noted that some content providers wish to guarantee the user experience via a normative profile. The presenter observed that broadcasters are also free to use the MPEG-H LC Profile, with a normative renderer.

Jon Gibbs, Huawei, stated that as an implementer Huawei finds flexibility in rendering a desirable option.

The presenter stated that the proposed profile can decode every LC Profile bitstream. The Chair noted that the decoder can parse the LC Profile bitstream, but cannot be conformant since no rendered output is produced.

Henney Oh, WILUS, stated that Korean Broadcast Industry desires to have a codec coupled with renderer to guarantee a baseline user experience.

There will be further discussion in a joint meeting with Requirements.

Takehiro Sugimoto, NHK, presented

| m37816 | Proposed number of core channels for LC profile of MPEG-H 3D Audio | Takehiro Sugimoto, Tomoyasu Komori |  |
| --- | --- | --- | --- |

The contribution points out an ambiguity and also a limitation in the current LC Profile specification. The presenter stated that customers or even government mandate will be for

- 9 languages (beyond Japanese) in a multilingual service

- Audio description in every broadcast service (in both Japanese and English)

This leads to the following needs

- 10 languages for dialog

- 2 languages for audio description

- 22.2 immersive audio program

The Chair noted that there is

- Channels in a bitstream

- Channels that are decoded by 3D Audio Core Coder

- Channels that are ouput by Format Converter

It was the consensus of the Audio subgroup to support the needs expressed in the contribution, which will require clarification of the LC and High Profile specification.

Further Discussion

Max Neuendorf, FhG-IIS, presented a modified table for describing LC Profile in which new tables were added:

- Stream chn

- Decoded chn

- Output chn

After some discussion by experts, and small changes to the presented text, it was the consensus of the Audio subgroup to incorporate the table and text shown into the specification of  LC and Profile.

Max Neuendorf, FhG-IIS, presented

| m37883 | Complexity Constraints for MPEG-H | Max Neuendorf, Michael Kratschmer, Manuel Jander, Achim Kuntz, Simone Fueg, Christian Neukam, Sascha Dick, Florian Schuh |  |
| --- | --- | --- | --- |

The contribution proposed to change the LC Profile definition such that the maximum complexity is reduced. The presenter noted that the proposal for Binaural Rendering has already been discussed between experts with a lack of full agreement. Hence more discussion is needed on this one proposal.

- DRC

- Arithmetic Coding (Chair’s note – need more complete description)

- LTPF

- OAM

- M/S, Complex prediction

- IGF

- MCT

- Sampling Rate

- Object Rendering

- Binaural Rendering

- IPF

- Size of Audio Scene Information

Tim Onders, Dolby, asked if all LC profile listening test bitstreams satisfied the proposed constraints. The presenter believed that all did.

With the exception of the proposal for Binaural Rendering, and NFC in SignalGroupTypeHOA, it was the consensus of the Audio subgroup to adopt all proposed changes in the contribution into the Study on 3D Audio DAM 3 text.

The proposal for Binaural Rendering, and NFC in SignalGroupTypeHOA restrictions needs additional discussion.

Further Discussion

Concerning NFC in SignalGroupTypeHOA, it was the consensus of the Audio subgroup to adopt the proposed change in the contribution into the Study on 3D Audio DAM 3 text.

3D Audio Reference Software

Achim Kuntz, FhG-IIS, presented

| m37891 | Software for MPEG-H 3D Audio RM6 | Michael Fischer, Achim Kuntz, Sangbae Chon, Aeukasz Januszkiewicz, Sven Kordon, Nils Peters, Yuki Yamamoto |  |
| --- | --- | --- | --- |

This a joint contribution from many companies, and the presenter gave credit to all for their hard work. The code is in the contribution zip archive. The code implements:

- DAM3 from the 113th meeting, if #defines are set correctly

- Additional bugs that were identified and corrected, and delimited by #defines.

It was the consensus of the Audio subgroup to take the contribution and associated source code and make it RM6, Software for MPEG-H 3D Audio.

Taegyu Lee, Yonsei, presented

| m37986 | Bugfix on the software for MPEG-H 3D Audio | Taegyu Lee, Henney Oh |  |
| --- | --- | --- | --- |

The contribution noted that the current code for the FD binauralization tool supportes block size of 4096 but not 1024. The contribution also presents fix for this bug.

It was the consensus of the Audio subgroup to incorporate the proposed fix into RM7, which will be built according to a workplan from this meeting.

Invariants CE

The Chair asked Audio experts if they felt it was appropriate to review and discuss this meeting’s documents concerning the Swissaudec Invariants CE even though Clemens Par, Swissaudec, was not present to make the presentation and engage in the discussion. No Audio experts objected to this proposal.

The Chair made a presentation concerning the Swissaudec Invariants CE. First, he noted that the following document from the 113th meeting is the CE proposal containing the CE technical description.

| m37271 | MPEG-H "Phase 2" Core Experiment – Technical Description and Evidence of Merit | Clemens Par |  |
| --- | --- | --- | --- |

Second, he noted that a new version of the following contribution was uploaded to the contribution register during the afternoon of Tuesday of the MPEG week.

| m37529 | Resubmission of Swissaudec's MPEG-H "Phase 2" Core Experiment | Clemens Par |  |
| --- | --- | --- | --- |

From the many items in the m37529 zip archive, the Chair presented the following two documents:

- m37592-2/m37271_Delta_Final_Test_Report/m37271_l100825-01_Swissaudec_SenseLab042-15.pdf

and

- m37529/m37529_Computational_Complexity/m37529_m37271_ANNEX_Computational_complexity_clean.docx

The first is a final listening test report from DELTA SenseLab, the second a comparison of the complexity of the CE technology and the RM technology. In fact, the Chair created and presented his own complexity tables based on the Swissaudec contribution and the appropriate MPEG contribution documents (see text between the “====” delimiters below). The summary complexity table is shown here:

Comparison of the complexity of the Invariants CE to RM0 or Benchmark

|  | CO submission | RM0/Benchmark | CE | Ratio |
| --- | --- | --- | --- | --- |
| bitrate/items | CO_01 - CO_10 | PCU |  |  |
| 48 kbps | 3DA Phase 1 + MPS | 63+40 = 103 | 80.5 | 0.78 |
| 64 kbps | 3DA Phase 1 + MPS | 63+40 = 103 | 80.5 | 0.78 |
| 96 kbps | 3DA Phase 1 | 63 | 80.5 | 1.28 |
| 128 kbps | 3DA Phase 1 | 63 | 80.5 | 1.28 |
| bitrate/items | CO_11 - CO_12 |  |  |  |
| 48 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |
| 64 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |
| 96 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |
| 128 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |

Comments from Audio experts

The Chair understands that the CE proponent asserts performance equivalent to RM0 and complexity lower than RM0, however, the Chair notes that for some operating points the CE is less computationally complex than RM0, and for others it is more computationally complex.

Max Neuendorf, FhG-IIS, stated that subjective test results based on only three items do not prove the that subjective quality is preserved in all cases. Hence, there would be considerable risk in adopting the technology. The Chair noted that nine other experts expressed agreement with the previous statement. When asking the question: “how many experts agree to adopt the Swissauded CE technology into the Study on DAM 3?” no (zero) experts raised their hands.

Jon Gibbs, Huawei, noted that the Delta SenseLab test is statistically fairly weak in terms of proving that system quality is truly equivalent.

The Chair noted that other CEs have more than 3 items in their subjective listening tests, and that the risk in miss-judging the subjective performance based on the submitted test is a major issue that cannot be overcome by the associated computational complexity figures.

Chair’s presentation document:

M3721, MPEG-H “Phase 2” Core Experiment

113th MPEG meeting

Systems under test:

| Bitrate | Sys | Description |
| --- | --- | --- |
| 128 kb/s | Sys1 | Benchmark FhG 128 kb/s |
|  | Sys2 | CE 3DAC 128 (RM0+CE technology) |
|  | Sys3 | CPE 128 (Coded CE downmix) |
|  | Sys4 | CPE PCM (Uncoded (PCM) CE downmix) |
|  | Sys5 | High Anchor from CfP, 256 kb/s |
| 96 kb/s | Sys1 | Benchmark FhG 96 kb/s |
|  | Sys2 | CE 3DAC 96 (RM0+CE technology) |
|  | Sys3 | CPE 96 (Coded CE downmix) |
|  | Sys4 | CPE PCM (Uncoded (PCM) CE downmix) |
| 64 kb/s | Sys1 | RM0 64 kb/s |
|  | Sys2 | CE 3DAC 64 (RM0+CE technology) |
|  | Sys3 | CPE 64 (Coded CE downmix) |
|  | Sys4 | CPE PCM (Uncoded (PCM) CE downmix) |
| 48 kb/s | Sys1 | RM0 48 kb/s |
|  | Sys2 | CE 3DAC 48 (RM0+CE technology) |
|  | Sys3 | CPE 48 (Coded CE downmix) |
|  | Sys4 | CPE PCM (Uncoded (PCM) CE downmix) |

Signals used in the subjective test

| Signal | Channels |
| --- | --- |
| CO_01_Church | 22.2 |
| CO_02_Mensch | 22.2 |
| CO_03_SLNiseko | 22.2 |

[Chair presented DELTA SenseLab Report]

M34261, Description of the Fraunhofer IIS 3D-Audio Phase 2 Submission and Benchmark

109th MPEG meeting, July 2014, Sapporo, Japan

Overview

Table 1: Technology used for CO submission incl. number of coded channels (#ch)

|  | CO submission |  |
| --- | --- | --- |
| bitrate/items | CO_01 - CO_10 | #ch |
| 48 kbps | 3DA Phase 1 + MPS | 9.1 |
| 64 kbps | 3DA Phase 1 + MPS | 9.1 |
| 96 kbps | 3DA Phase 1 | 9.1 / 9.0 |
| 128 kbps | 3DA Phase 1 | 9.1 / 9.0 |
| bitrate/items | CO_11 - CO_12 |  |
| 48 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |
| 64 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |
| 96 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |
| 128 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |

Table 2: Technology used for CO benchmark incl. number of coded channels (#ch)
(Blue entries indicate that the waveforms are identical to the corresponding 
waveforms of the submission)

|  | CO benchmark |  |
| --- | --- | --- |
| bitrate/items | CO_01 - CO_10 | #ch |
| 48 kbps | 3DA Phase 1 + MPS | 5.1 |
| 64 kbps | 3DA Phase 1 + MPS | 7.1 |
| 96 kbps | 3DA Phase 1 | 9.1 / 9.0 |
| 128 kbps | 3DA Phase 1 | 9.1 / 9.0 |
| bitrate/items | CO_11 - CO_12 |  |
| 48 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |
| 64 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |
| 96 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |
| 128 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 |

PCU Complexity

As usually done within MPEG, the decoder and processing complexity is specified in terms of PCU. Memory requirements are given in RCU. The numbers given in Table 3 are worst-case estimates using the highest number out of the 4 bitrates (48, 64, 96 and 128 kbps).

Table 3: Complexity estimation

| Module | 3DA-Core Decoder | SAOC 3D | MPEG Surround |
| --- | --- | --- | --- |
| RCU | 152 (ROM) 50 (RAM) | 98 | 23 |
| PCU | 63 | 35 | 40 |

Given above, Phase 2 RM0 and Benchmark complexity is

|  | CO submission |  |  |
| --- | --- | --- | --- |
| bitrate/items | CO_01 - CO_10 | #ch | PCU |
| 48 kbps | 3DA Phase 1 + MPS | 9.1 | 63+40 = 103 |
| 64 kbps | 3DA Phase 1 + MPS | 9.1 | 63+40 = 103 |
| 96 kbps | 3DA Phase 1 | 9.1 / 9.0 | 63 |
| 128 kbps | 3DA Phase 1 | 9.1 / 9.0 | 63 |
| bitrate/items | CO_11 - CO_12 |  |  |
| 48 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 | 63 + 35 = 98 |
| 64 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 | 63 + 35 = 98 |
| 96 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 | 63 + 35 = 98 |
| 128 kbps | 3DA Phase 1 (incl. SAOC 3D) | 22.2 | 63 + 35 = 98 |

From m37271 v3

ECMA-407 Decoder					40.7 PCU

CICP-Downmix (9.1)				0.39 PCU

CICP-Downmix (11.1)				0.37 PCU

CICP-Downmix (14.0)				0.27 PCU

Complexity for the RM0 6-channel 3D Audio Core is ~ 3*13.2 = 39.6 PCU

Total PCU complexity for 22.2			80.3 PCU

Total PCU complexity for 9.1			80.69 PCU

Total PCU complexity for 11.1			80.67 PCU

Total PCU complexity for 14.0			80.57 PCU

Comparison of the complexity of the Invariants CE to RM0 or Benchmark

|  | CO submission | RM0/Benchmark | CE | Ratio |
| --- | --- | --- | --- | --- |
| bitrate/items | CO_01 - CO_10 | PCU |  |  |
| 48 kbps | 3DA Phase 1 + MPS | 63+40 = 103 | 80.5 | 0.78 |
| 64 kbps | 3DA Phase 1 + MPS | 63+40 = 103 | 80.5 | 0.78 |
| 96 kbps | 3DA Phase 1 | 63 | 80.5 | 1.28 |
| 128 kbps | 3DA Phase 1 | 63 | 80.5 | 1.28 |
| bitrate/items | CO_11 - CO_12 |  |  |  |
| 48 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |
| 64 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |
| 96 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |
| 128 kbps | 3DA Phase 1 (incl. SAOC 3D) | 63 + 35 = 98 | 80.5 | 0.82 |

### Maintenance

Seungkwon Beack, ETRI, presented

| m37834 | Maintenance report on MPEG Surround Extension tool for internal sampling-rate | Seungkwon Beack, Taejin Lee, Jeongil Seo, Adrian Murtaza | MPS |
| --- | --- | --- | --- |

The presenter reminded Audio experts that, at the 113th meeting, the MPEG Surround specification was revised to permit greater flexibility with respect to MPEG Surround internal sampling rate and number of QMF bands. Specifically, to support 64 QMF bands permits it to interface directly with MPEG-H 3D Audio in the QMF domain. It presents listening test results that document the performance of this operation point.

Systems under test

- Sys1 Revised system

- Sys2 Original system

Mushra test results showed

- No difference for average scores

- One better for differential scores, no difference overall

In conclusion, test results showed that current spec works.

Adrian Murtaza, FhG-IIS, presented

| m37877 | Proposed Study on DAM3 for MPEG-D MPEG Surround | Adrian Murtaza, Achim Kuntz | MPS |
| --- | --- | --- | --- |

The contribution relates to the internal sampling rate issue addressed by the previous contribution. Specifically, it mandates that MPEG-H 3D Audio shall only be used with MPEG Surround when MPEG Surround is in 64-band QMF mode.

It was the consensus of the Audio subgroup to incorporate the contribution into a Study on DAM3 for MPEG-D MPEG Surround.

Adrian Murtaza, FhG-IIS, presented

| m37879 | Thoughts on MPEG-D SAOC Second Edition | Adrian Murtaza, Jouni Paulus, Leon Terentiv | SAOC |
| --- | --- | --- | --- |

This contribution is a draft for what will become MPEG-D SAOC Second Edition. This Draft Second Edition contains:

- COR 1

- COR 2

- DCOR 3 (in the final text of the Second Edition)

- AMD 3 (Dialog Enhancement)

The Chair thanks Audio experts for undertaking the roll-up to make the SAOC Second Edition.

Adrian Murtaza, FhG-IIS, presented

| m37878 | Proposed Corrigendum to MPEG-D SAOC | Adrian Murtaza, Jouni Paulus, Leon Terentiv | SAOC |
| --- | --- | --- | --- |

The contribution proposes additional corrections to be added to the SAOC Defect Report from the 106th and 112th meeting to make the text of a DCOR 3 to issue from this meeting.

Corrections are:

- Better organization of text

- Clarifications of text

- Corrections to text

It was the consensus of the Audio subgroup to incorporate the text from the two defect reports (from the 106th and 112th meetings) and the corrections in this contribution into a DCOR 3 to issue from this meeting.

Adrian Murtaza, FhG-IIS, presented

| m37875 | Proposed Study on DAM4 for MPEG-D SAOC | Adrian Murtaza, Leon Terentiv, Jouni Paulus | SAOC |
| --- | --- | --- | --- |

The contribution related to Conformance, and proposes corrections to the

- The definition of “correct” decoding (i.e. maximum PCM output of 32 for 16-bit PCM output, and maximum RMS difference)

- Numerous other corrections to the text of the conformance document

- Definition of 23 new conformance sequences for SAOC-DE. The conformance streams are available now. In total, there are 71 SAOC conformance streams, 48 for SAOC and 23 for SAOC-DE.

It was the consensus of the Audio subgroup to make the contribution a Study on DAM4 for MPEG-D SAOC. The conformance streams are already on the MPEG SVN server, as indicated in the Study On text.

Adrian Murtaza, FhG-IIS, presented

| m37876 | Proposed Study on DAM5 for MPEG-D SAOC | Adrian Murtaza, Leon Terentiv, Jouni Paulus | SAOC |
| --- | --- | --- | --- |

The contribution related to Reference Software, and proposed several corrections and additional functionality to the Reference Software.

It was the consensus of the Audio subgroup to make the contribution a Study on DAM5 for MPEG-D SAOC. The reference software is already on the MPEG SVN server, as indicated in the Study On text.

Christof Fersch, Dolby, gave a verbal presentation of

| m37791 | Report on corrected USAC conformance bitstreams | Christof Fersch | USAC |
| --- | --- | --- | --- |

The one conformance stream previously identified as a problem, was re-defined and re-generated so as to resolve all issues.

Yuki Yamamoto, Sony, gave a verbal presentation of

| m37826 | Sony's crosscheck report on USAC conformance | Yuki Yamamoto, Toru Chinen | USAC |
| --- | --- | --- | --- |

Sony experts confirmed that the new conformance stream was able to be decoded successfully.

The Chair noted that the fully correct and cross-checked set of USAC conformance streams will be made available attached to ISO/IEC 23003-3:2012/AMD 1 COR 2, Corrections to Conformance. This will be re-visited when the DoC on DCOR 2 is reviewed.

Max Neuendorf,  FhG-IIS, presented

| m37886 | Constraints for USAC in adaptive streaming applications | Max Neuendorf, Matthias Felix, Bernd Herrmann, Bernd Czelhan, Michael Haertl | USAC |
| --- | --- | --- | --- |

The contribution describes and clarifies numerous situations that arise in streaming use cases involving USAC.  The contribution proposes to add text to

- The body of the USAC specification where appropriate

- Annex B Encoder Description

- Annex F Audio/Systems Interaction

It was the consensus of the Audio subgroup to incorporate the contribution text into ISO/IEC 23003-3:2012/FDAM 3, Support for MPEG-D DRC and IPF.

Michael Kratschmer, FhG-IIS, presented

| m37884 | Parametric Limiter for MPEG-D DRC | Michael Kratschmer, Frank Baumgarte | DRC |
| --- | --- | --- | --- |

The presenter gave a brief overview of how MPEG-D DRC works and what it can be used for. He further noted that peak limiting and clipping prevention is typically out of scope for most MPEG audio decoders. The contribution specifically addresses the prevention of peak limiting, via the specification of a new parametric DRC type for peak limiting. This new functionality does not require any new tools or architecture. What is required is a new playload that contains

- Limiting threshold

- Smoothing attack and release time constants

It was the consensus of the Audio subgroup to incorporate the contribution text into ISO/IEC 23003-4:2015 DAM 1, Parametric DRC, Gain Mapping and Equalization Tools, to be produced at this meeting.

Michael Kratschmer, FhG-IIS, presented

| m37882 | Proposed Corrigendum to MPEG-D DRC | Michael Kratschmer, Frank Baumgarte | DRC |
| --- | --- | --- | --- |

The contribution notes that each DRC configuration requires a separate metadata set. It proposes to adopt the downmixld mechanism for downmix configurations into a new drcSetId for DRC configurations. This does not require a syntax change, only a semantics change.

It was the consensus of the Audio subgroup to incorporate the contribution text into a Defect Report on MPEG-D DRC.

Frank Baumgarte, Apple, presented

| m37895 | Study on MPEG-D DRC 23003-4 PDAM1 | Frank Baumgarte, Michael Kratschmer | DRC |
| --- | --- | --- | --- |

The presenter reviewed that the PDAM 1 text specifies the following tools:

- Parametric DRC

- Gain mapping

- Loudness EQ

- Generic EQ

Since the 113th meeting, when the PDAM issued, the technology has been implemented which has identified issues in the specification. Many of those issues are captured in the proposed Study On text. Issues are:

- Complexity management. The Study text defines how to

  - Estimate complexity

  - Conditions under which EQs and other gains can be discarded so as to satisfy maxium decoder complexity limits

- Loudness measurement

  - Update to latest ITU recommendation

- EQ Phase alignment

  - Need further restrictions on filter phase

- Ordering of boxes in MP4 FF

  - To simplify decoder parser complexity

- Numerous other clarifications and editorial changes

It was the consensus of the Audio subgroup to make the contribution text ISO/IEC 23003-4:2015 DAM 1, Parametric DRC, Gain Mapping and Equalization Tools, to be produced at this meeting.

Michael Kratschmer, FhG-IIS, presented

| m37881 | Proposed RM7 of MPEG-D DRC software | Michael Kratschmer, Frank Baumgarte | DRC |
| --- | --- | --- | --- |

The contribution is a proposed RM7 for MPEG-D DRC Reference Software. It incorporates all tools in DRC including

- ISO/IEC 23003-4:2015, Dynamic Range Control

- 15842, Text of ISO/IEC 23003-4:2015 PDAM 1, Parametric DRC, Gain Mapping and Equalization Tools

- m37895, Study on MPEG-D DRC 23003-4 PDAM1

It was the consensus of the Audio subgroup to add to this the technology in

- m37884, Parametric Limiter for MPEG-D DRC

And issue this as

- ISO/IEC 23003-4:2015/PDAM 2, DRC Reference Software

from this meeting with a

- 3 week editing period and

- A resolution for a 2 month ballot

## Discussion of Remaining Open Issues

DAM 3 Open Issues

NFC Syntax

Gregory Pallone, Orange, presented syntax and supporting text pertaining to carriage of NFC information

Experts agreed that the current syntax will work and support the Orange use case if the NfcReferenceDistance is signalled in the bitstream.

Experts from Technicolor and Samsung stated that any change, even editorial, causes more work for implementers, and so would prefer that syntax remain as in the DAM 3 text.

It was the consensus of the Audio subgroup to keep syntax as in the DAM 3 text from the 113th meeting.

NFC Processing

Gregory Pallone, Orange, presented information pertaining to NFC processing.

The Chair asked the question: what are the use cases in LC Profile decoders that require NFC processing? The presenter noted that when listening in the car (and others) the speakers might be too close.

Revisions to LC Profile specification

Max Neuendorf, FhG-IIS, presented edited LC Profile specification text concerning:

- Bitstream channels

- 3D Audio core decoded channels

- Speaker output channels

The text is shown between the “====” delimiters, below.

It was the consensus of the Audio subgroup to keep adopt this text into Study on MPEG-H 3D Audio  DAM 3 text.

Table P2 — Levels and their corresponding restrictions for the Low Complexity Profile

| Level | Max. Sampling rate | Max. no. of core ch in compressed data stream | Max. no. of decoder processed core ch | Max. no. of loudspeaker output ch | Example of max. loudspeaker configuration | Max. no. of decoded objects | Example of a max. Config C+O | Max. HOA order | Example of max. HOA order + O |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 48000 | 10 | 5 | 2 | 2.0 | 5 | 2 ch + 3 static obj | 2 | 2nd order + 3 static obj |
| 2 | 48000 | 18 | 9 | 8 | 7.1 | 9 | 6 ch + 3 static obj | 4 | 4th order + 3 static obj |
| 3 | 48000 | 32 | 16 | 12 | 11.1 | 16 | 12 ch + 4 obj | 6 | 6th order + 4 obj |
| 4 | 48000 | 56 | 28 | 24 | 22.2 | 28 | 24 ch + 4 obj | 6 | 6th order + 4 obj |
| 5 | 96000 | 56 | 28 | 24 | 22.2 | 28 | 24 ch + 4 obj | 6 | 6th order + 4 obj |

—	The use of switch groups determines the subset of core channels out of the core channels in the bitstream that shall be decoded.

—	If the mae_AudioSceneInfo() contains switch groups (mae_numSwitchGroups>0), then the elementLengthPresent flag shall be 1

Further discussion on Zylia CE and LC Profile

Tomasz Żernicki and Lukasz Januszkiewicz from Zylia has presented listening test pooled results for TCC at 20 kbps (TCC+eSBR) and 64 kbps (TCC+IGF). There is a significant improvement for 7 items for 20 kbps and 2 items for 64 kbps. The quality of none item was degraded.

New results (64kbps) were related to application of TCC in higher bitrates with IGF tool activated. These new results demonstrate that TCC works efficiently for high bitrates use cases and still can introduce statistically significant improvement of the quality.

Tomasz Żernicki, Zylia, proposed to include TCC tool into MPEG-H 3D Audio Low Complexity profile. Additionally, relevant changes to DAM3 text were proposed.

The presenter proposed to restrict the tool for use in LC Profile according to the table below

Table PX — Restrictions applying to TCC tool according to the Levels of the Low Complexity Profile

| Mpegh3daProfile LevelIndication | 1 | 2 | 3 | 4 | 5 |
| --- | --- | --- | --- | --- | --- |
| Maximum number of TCC channels | 2 | 4 | 4 | 8 | 0 |
| MAX_NUM_TRJ | 4 | 4 | 4 | 4 | 0 |

Max Neuendorf, FhG-IIS, noted that the TCC processing presented to this meeting used the ODFT synthesis method.

Juergen Herre, IAL/FhG-IIS, asked why pitch pipe, which is a highly tonal tool, did not show improvement using the TCC tool. The presenter stated that the encoder signal classifier disable the tool for this class of signal.

Max Neuendorf, FhG-IIS, asked to clarify the description of complexity based on the synthesis method used. Presenters agreed, that a short update regarding the Taylor series cosine function calculation could be added to the technical description of the tool. Christof Fersch, Dolby, noted that this is a small change that can be added to DAM3 during present meeting.

Discussion on new tools LC Profile

The Audio Chair observed the TCC tool and the HREF tool have both requested adoption into LC profile, and furthermore, that the Chair has suggested the possibility of making all NFC processing informative in LC Profile. Furthermore, experts from Korea, the first customer of MPEG-H 3D Audio, have expressed a strong request that the set of tools in LC Profile should remain unchanged. The Chair suggested that a possible consensus position that resolves many open issues is to:

- Not admit TCC into LC Profile

- Not admit HREP into LC Profile

- Keep NFC signaling syntax and NFC processing in LC Profile as specified in the DAM 3 from the 113th MPEG meeting.

Henney Oh, WULUS, spoke for the Korean broadcast industry to say that Korea is implementing MPEG-H 3D Audio codec now, and it would be best if there is no change in the LC Profile toolbox. Sang Bae Chon, Samsung, speaking as a Consumer Electronics device manufacturer, stated that implementers are on a similarly aggressive timeline. A change to the LC Profile toolbox will jeopardize this timeline.

Concerning the set of tools in LC Profile and also NFC processing mandated in LCP profile, it was the consensus of the Audio subgroup to stay as is specified in the DAM 3 text from the 113th meeting.

HREP

Christain Neukam, FhG-IIS, gave a short presentation on HREP. The presentation asked to have HREP in all processing paths of the 3D Audio decoder: channels, objects, SAOC-3D, HOA.

Christof Freich, Dolby, stated some concern as to whether HREP will actually deliver a quality increase in the SAOC and HOA signal paths. Christian Neukam, FhG-IIS, stated that HREP is a core coder tool and as such will work on all signal types just at the 3D Audio core provides efficient compression for all signal types. Nils Peters, Qualcomm, noted that HOA works well with the core coder, and as such it his expectation that it will work with HREP. Oliver Weubbolt, Technicolor, noted that “channel-based” coding tools work equally well for HOA signals. Adrian Murtaza, FhG-IIS, noted HREP gives more bits to core coder and hence can be expected to make signals sound better. Christian Neukam, FhG-IIS, noted that HREP is an identity system absent any coding. Tim Onders, Doby, noted that HREP “shifts a more objectionable artifact to a less objectionable artifact,” and questioned whether subsequent SOAC and HOA processing could “color” the artifacts resulting in a worse result. Oliver Weubbolt, Technicolor, reminded experts that this tool supplies more than 15 MUSHRA points performance gain for some signals (e.g. selected applause signals). The Chair attempted to sum up, and noted that a 15 point performance gain is greater than almost any CE, and hence expects that HREP will deliver good performance when put in the SAOC and HOA signal paths.

It was the consensus of the Audio subgroup to accept the HREP tool into the SAOC and HOA signal paths (so that it is now present in all signal paths), and to document this in Study on MPEG-H 3D Audio DAM 3.

Qualcomm, multiple items

Nils Peters, Qualcomm, gave a presentation that re-iterated the points raised in his contribution m37874. The resolution for each item is recorded below.

CICP Extensions – Study as AhG mandate.

Screen adaptation and Signaling of screen size – pre-compute information ahead of content switch. The Chair noted that there was no need to change the existing syntax, but only recommend a small number (e.g. 8 of the 9x9x9 possibilities) preferred screen sizes and to describe how the adaptation information could be pre-compued. It was the consensus of the Audio subgroup to capture the proposal, with the modifications of the Chair, into an informative Annex.

Rendering of HOA and static objects –

Deep Sen, Qualcomm, noted that the content provider might be mixing using only an HOA panner and so it may be advantageous to place dialog objects using the HOA panner.

Achim Kuntz questioned if HOA panning is desirable, in that some objects would tend to become more diffuse. Presenter confirmed that a HOA panner would tend to excite more speakers.

This proposal was not accepted

Support for horizontal only HOA content – the proposal is to add one new codebook so that truly horizontal-only HOA content can be rendered as such.

It was the consensus of the Audio subgroup to adopt the proposal in to Study on MPEG-H 3D Audio DAM 3.

Panasonic presentation

The presenter observed that both “straightforward” and “informative Annex G” HOA renderer will be used in LC Profile decoders.

The presenter recommended adding one sentence. This was discussed, with some experts supporting the new text and some wishing it to be further edited. The Chair noted that, for this matter, the DAM text from the 113th meeting is correct and proposed that there be no changes.

Proposed changes were not accepted.

Further Discussion on Panasonic proposals

Concerning Section 18 “Low Complexity HOA Spatial Decoding and Rendering,” Panasonic experts presented new text, as shown below within the “#####” delimiters, where the red text is the proposed new text.

It was the consensus of the Audio subgroup to adopt the newly proposed text in to Study on MPEG-H 3D Audio DAM 3.

(The following text is extracted from Section 18 of DAM3 for your reference.) 
######################################################################

18        Low Complexity HOA Spatial Decoding and Rendering

Replace the following sentence at the beginning of subclause 12.4.2.1 "General Architecture" 

The architecture of the spatial HOA decoder is depicted in Figure 40. 

With

The Spatial HOA decoding process describes how to reconstruct the HOA coefficient sequences from the HOA transport channels and the HOA side information (HOA extension payload). Subsequently the HOA rendering matrix is applied to the HOA coefficient sequences to get the final loudspeaker signals. The HOA renderer is described in section 12.4.3. Both processing steps can be very efficiently combined resulting in an implementation with much lower computational complexity. Since the HOA synthesis in the decoding process can be expressed as a synthesizing matrix operation, the rendering matrix can be applied to the synthesizing matrix for such combination. This realizes “decoding and rendering” in one-step rendering without having to reconstruct full HOA coefficient sequences when they are not necessary. A detailed description how t o integrate the spatial HOA decoding and rendering can be found in Annex G. However, for didactical reasons the processing steps are described separately in the followi’ng subclauses. 

The architecture of the spatial HOA decoder is depicted in Figure 40. 


Replace ANNEX G (informative) "Low Complexity HOA Rendering" with the following text:

Annex G 
(informative)

######################################################################

Binaural Rendering and selection of impulse responses

Max Neuendorf, FhG-IIS, made a presentation on new text. This text was discussed, and edited.

It was the consensus of the Audio subgroup to adopt the newly proposed text in to Study on MPEG-H 3D Audio DAM 3.

# Closing Audio Plenary and meeting deliverables

## Discussion of Open Issues

Remaining open issues were discussed and resolved. These pertained to 3D Audio and are documented at the end of the 3D Audio Task Group section.

## Recommendations for final plenary

The Audio recommendations were presented and approved.

## Disposition of Comments on Ballot Items

DoC on Audio-related balloted items were presented and approved.

## Responses to Liaison and NB comments

Liaison statement and NB comment responses generated by Audio were presented and approved.

## Establishment of Ad-hoc Groups

The ad-hoc groups shown in the following table were established by the Audio subgroup.

| No. | Title | Mtg |
| --- | --- | --- |
|  | AHG on 3D Audio and Audio Maintenance | No |
|  | AHG on Responding to Industry Needs on Adoption of MPEG Audio | No |

## Approval of output documents

All output documents, shown in Annex D, were presented in Audio plenary and were approved.

## Press statement

The was no Audio contribution to the press statement.

## Agenda for next meeting

The agenda for the next MPEG meeting is shown in Annex F.

## All other business

There was none.

## Closing of the meeting

The 114th Audio Subgroup meeting was adjourned Friday at 13:30 hrs.

Participants

There were 43 participants in the Audio subgroup meeting, as shown in the following table.

| First | Last | Country | Affiliation | Email |
| --- | --- | --- | --- | --- |
| Seungkwon | Beack | KR | ETRI | skbeack@etri.re.kr |
| Toru | Chinen | JP | Sony | Toru.Chinen@jp.sony.com |
| Sang | Chon | KR | Samsung Electronics | sb.chon@samsung.com |
| Jürgen | Herre | DE | Int'l Audio Labs Erlangen / Fraunhofer | hrr@iis.fraunhofer.de |
| Taejin | Lee | KR | ETRI | tjlee@etri.re.kr |
| Max | Neuendorf | DE | Fraunhofer IIS | max.neuendorf@iis.fraunhofer.de |
| Henney | Oh | KR | WILUS | henney.oh@wilusgroup.com |
| Gregory | Pallone | FR | Orange | gregory.pallone@orange.com |
| Schuyler | Quackenbush | USA | ARL | srq@audioresearchlabs.com |
| Takehiro | Sugimoto | Japan | NHK | sugimoto.t-fg@nhk.or.jp |
| Jeongook | Song | US | Qualcomm | jeongook@qti.qualcomm.com |
| Oliver | Wuebbolt | DE | Technicolor | oliver.wuebbolt@technicolor.com |
| Tomasz | Zernicki | PL | Zylia | tomasz.zernicki@zylia.pl |
| Yuki | Yamamoto | Japan | Sony Corporation | Yuki.Yamamoto@jp.sony.com |
| Christof | Fersch | Germany | Dolby | christof.fersch@dolby.com |
| Taegyu | Lee | KR | Yonsei University | tglee@dsp.yonsei.ac.kr |
| Hiroyuki | Ehara | Japan | Panasonic Corporation | ehara.hiroyuki@jp.panasonic.com |
| Frank | Baumgarte | USA | Apple Inc. | fb@apple.com |
| Werner | De Bruijn | NL | Philips | werner.de.bruijn@philips.com |
| Panji | Setiawan | Germany | Huawei Technologies | panji.setiawan@huawei.com |
| Nils | Peters | US | Qualcomm | npeters@qti.qualcomm.com |
| Harald | Fuchs | Germany | Fraunhofer IIS | harald.fuchs@iis.fraunhofer.de |
| Michael | Kratschmer | Germany | Fraunhofer IIS | michael.kratschmer@iis.fraunhofer.de |
| Achim | Kuntz | Germany | Fraunhofer IIS | achim.kuntz@iis.fraunhofer.de |
| Martin | Morrell | USA | Qualcomm | mmorrell@qti.qualcomm.com |
| &#321;ukasz | Januszkiewicz | Poland | Zylia Sp. z o.o. | lukasz.januszkiewicz@zylia.pl |
| Adrian | Murtaza | DE | Fraunhofer IIS | adrian.murtaza@iis.fraunhofer.de |
| Moo Young | Kim | USA | Qualcomm | kimyoung@qti.qualcomm.com |
| Christian | Neukam | Germany | Fraunhofer | christian.neukam@iis.fraunhofer.de |
| Kai | Wu | Singapore | Panasonic R&D Center | kai.wu@sg.panasonic.com |
| Timothy | Onders | US | Dolby Laboratories, Inc. | timothy.onders@dolby.com |
| Deep | Sen | USA | Qualcomm | dsen@qti.qualcomm.com |
| Peisong | Chen | USA | Broadcom | peisong.chen@broadcom.com |
| Haiting | Li | CN | Huawei Technologies Co., Ltd. | lihaiting@huawei.com |
| Jon | Gibbs | UK | Huawei Technologies Co Ltd | jon.gibbs@oblisco.com |
| Ken | McCann | UK | Zetacast/Dolby | ken@zetacast.com |
| Jason | Filos | USA | Qualcomm | jfilos@qti.qualcomm.com |
| S M Akramus | Salehin | USA | QUALCOMM | ssalehin@qti.qualcomm.com |
| Ingo | Hofmann | Germany | Fraunhofer IIS | ingo.hofmann@iis.fraunhofer.de |
| Phillip | Maness | USA | DTS. Inc. | phillip.maness@dts.com |
| Shankar | Shivappa | USA | Qualcomm technologies Inc | sshivapp@qti.qualcomm.com |
| Hyunho | Ju | KR | Korea Electronics Technology Institute | hyunho@keti.re.kr |
| Ted | Laverty | USA | DTS, Inc. | ted.laverty@dts.com |

Audio Contributions and Schedule

3D Audio Phase 2 AhG Meeting

| Sunday | Topic | Authors | Presented |
| --- | --- | --- | --- |
| 1300-1800 | 3D Audio Phase 2 CEs |  |  |
|  | TCC |  |  |
| m37930 | Zylia Poznan Listening Test Site Properties | Jakub Zamojski, Lukasz Januszkiewicz, Tomasz Zernicki | x |
| m37932 | Corrections and clarifications on Tonal Component Coding | Lukasz Januszkiewicz, Tomasz Zernicki | x |
| m37947 | Listening Test Results for TCC from FhG IIS | Sascha Dick, Christian Neukam | x |
| m37933 | Low Complexity Tonal Component Coding | Tomasz Zernicki, Lukasz Januszkiewicz, Andrzej Rumiaski, Marzena Malczewska | x |
|  | HREP |  |  |
| m37833 | ETRI's cross-check report for CE on High Resolution Envelope Processing | Seungkwon Beack, Taejin Lee | x |
| m37715 | Cross Check Report for CE on HREP (Test Site Fraunhofer IDMT) | Judith Liebetrau, Thomas Sporer, Alexander Stojanow | x |
| m37889 | 3DA CE on High Resolution Envelope Processing (HREP) | Sascha Disch, Florin Ghido, Franz Reutelhuber, Alexander Adami, Juergen Herre | x |
|  | HOA Issues |  |  |
| m37894 | Proposed modifications on MPEG-H 3D Audio | Gregory Pallone | x |
|  | Review of AhG Report |  |  |

114th MPEG Audio subgroup meeting

| Monday | Topic | Authors | Presented |
| --- | --- | --- | --- |
| 0900-1300 | MPEG Plenary |  |  |
| 1300-1400 | Lunch |  |  |
| 1400-1430 | Audio Plenary |  |  |
|  | Welcome and Remarks Report on Sunday Chairs meeting Review main tasks for the week |  |  |
| m37805 | 113th MPEG Audio Report | Schuyler Quackenbush | x |
| m37902 | AHG on 3D Audio and Audio Maintenance | Schuyler Quackenbush | x |
| m37901 | AHG on Responding to Industry Needs on Adoption of MPEG Audio | Juliane Borsum | x |
|  | Review of Liaison Documents |  |  |
| m37987 | Information on Korean standard for terrestrial UHD broadcast services | Henney Oh | x |
| 1430-1800 | Maintenance |  |  |
|  | MPEG-D |  |  |
| m37834 | Maintenance report on MPEG Surround Extension tool for internal sampling-rate | Seungkwon Beack, Taejin Lee, Jeongil Seo, Adrian Murtaza | x |
| m37877 | Proposed Study on DAM3 for MPEG-D MPEG Surround | Adrian Murtaza, Achim Kuntz | x |
| m37875 | Proposed Study on DAM4 for MPEG-D SAOC | Adrian Murtaza, Leon Terentiv, Jouni Paulus | x |
| m37876 | Proposed Study on DAM5 for MPEG-D SAOC | Adrian Murtaza, Leon Terentiv, Jouni Paulus | x |
| m37878 | Proposed Corrigendum to MPEG-D SAOC | Adrian Murtaza, Jouni Paulus, Leon Terentiv | x |
| m37879 | Thoughts on MPEG-D SAOC Second Edition | Adrian Murtaza, Jouni Paulus, Leon Terentiv | x |
| m37791 | Report on corrected USAC conformance bitstreams | Christof Fersch | x |
| m37826 | Sony's crosscheck report on USAC conformance | Yuki Yamamoto, Toru Chinen | x |
| m37886 | Constraints for USAC in adaptive streaming applications | Max Neuendorf, Matthias Felix, Bernd Herrmann, Bernd Czelhan, Michael Haertl | x |
| m37884 | Parametric Limiter for MPEG-D DRC | Michael Kratschmer, Frank Baumgarte | x |
| m37895 | Study on MPEG-D DRC 23003-4 PDAM1 | Frank Baumgarte, Michael Kratschmer | x |
| m37882 | Proposed Corrigendum to MPEG-D DRC | Michael Kratschmer, Frank Baumgarte | x |
| m37881 | Proposed RM7 of MPEG-D DRC software | Michael Kratschmer, Frank Baumgarte | x |
| Tuesday |  |  |  |
| 0900-1000 | Joint with Systems 3D Audio DAM 4 |  |  |
| m37531 | Study Of 23008-3 DAM4 (w15851) - Carriage Of Systems Metadata | Michael Dolan, Dave Singer, Schuyler Quackenbush | x |
| m37896 | Study on Base Media File Format 14496-12 PDAM1 |  | x |
|  | Final AhG document presentations |  |  |
| m37827 | Proposed simplification of HOA parts in MPEG-H 3D Audio Phase 2 | Hiroyuki EHARA, Sua-Hong NEO, Kai WU | x |
|  | Phase I Corrections |  |  |
| m37885 | Proposed DCOR to MPEG-H 3D Audio edition 2015 | Max Neuendorf, Achim Kuntz, Simone Fueg, Andreas Hoelzer, Michael Kratschmer, Christian Neukam, Sascha Dick, Elena Burdiel, Toru Chinen | x |
|  | Phase II Corrections and Clarifications |  |  |
| m37770 | Corrections and Clarifications on MPEG-H 3D Audio DAM3 | Oliver Wuebbolt, Johannes Boehm, Alexander Krueger, Sven Kordon, Florian Keiler | x |
| m37874 | Thoughts on MPEG-H 3D Audio | Nils Peters, Deep Sen, Jeongook Song, Moo Young Kim | x |
| 1300-1400 | Lunch |  |  |
|  | Phase II Corrections and Clarifications |  |  |
| m37892 | Review of MPEG-H 3DA Metadata | Simone Feug, Christian Ertel, Achim Kuntz | x |
| m37897 | Review of MPEG-H 3DA Signaling | Max Neuendorf, Sascha Dick, Nikolaus Rettelbach | x |
| m37853 | Clarifications on MPEG-H PDAM3 | Sang Bae Chon, Sunmin Kim | x |
| m37863 | Proposed Study on DAM3 for MPEG-H 3D Audio | Christian Neukam, Michael Kratschmer, Max Neuendorf, Nikolaus Rettelbach, Toru Chinen | x |
|  | Proposed 3D Audio Profile |  |  |
| m37832 | MPEG-H Part 3 Profile Definition | Christof Fersch | x |
|  | 3D Audio Reference Software |  |  |
| m37891 | Software for MPEG-H 3D Audio RM6 | Michael Fischer, Achim Kuntz, Sangbae Chon, Aeukasz Januszkiewicz, Sven Kordon, Nils Peters, Yuki Yamamoto | x |
| m37986 | Bugfix on the software for MPEG-H 3D Audio | Taegyu Lee, Henney Oh | x |
| 1800- | Chairs meeting |  |  |
| Wednesday |  |  |  |
| 0900-1100 | MPEG Plenary |  |  |
| 1130-1300 | Joint with All at Audio |  |  |
|  | MPEG Vision |  | x |
| 1300-1400 | Lunch |  |  |
| 1400-1500 | Document Preparation |  |  |
| 1500-1600 | 3D Audio LC Profile |  |  |
| m37816 | Proposed number of core channels for LC profile of MPEG-H 3D Audio | Takehiro Sugimoto, Tomoyasu Komori | x |
| m37883 | Complexity Constraints for MPEG-H | Max Neuendorf, Michael Kratschmer, Manuel Jander, Achim Kuntz, Simone Fueg, Christian Neukam, Sascha Dick, Florian Schuh | x |
| 1600-1700 | Phase II CE |  |  |
| m37529 | Resubmission of Swissaudec's MPEG-H "Phase 2" Core Experiment | Clemens Par | x |
| 1700-1730 | Open Issues |  |  |
|  | Zylia presentation |  | x |
| 1730- | Social: Buses leave at 6:15pm |  |  |
| Thursday |  |  |  |
| 0900-1000 | Open Issues |  |  |
| 1000-1100 | Joint with 3DV at Audio |  |  |
|  | MPEG-H 3D Audio in a Virtural/Augmented Reality Use Case |  | x |
| 1100-1200 | Joint with Requirements at Audio |  |  |
|  | Possible future MPEG-H 3D Audio profiles m37832 MPEG-H Part 3 Profile Definition Christof Fersch Possible LCX profile for Cable Industry |  | x |
| 1200-1300 | Document Preparation |  |  |
| 1300-1400 | Lunch |  |  |
| 1400-1500 | DoC Review |  |  |
| 1530-1600 | 3D Everything joint meeting |  | x |
| 1600-1800 | Open Issues |  |  |
| 1800- | Chairs meeting |  |  |
| Friday |  |  |  |
| 0800-0900 | Discussion of Open Issues |  |  |
| 0800-1300 | Audio Plenary |  |  |
|  | Report on Thursday Chairs meeting |  |  |
|  | Recommendations for final plenary |  |  |
|  | Establishment Ad-hoc groups and review AhG Mandates |  |  |
| 1000 | Get document numbers |  |  |
| 1030 | Submit AhG Mandates and Resolutions |  |  |
|  | Approve and send Press Release |  |  |
|  | Approve Responses to NB comments and Liaison |  |  |
|  | Approval of output documents: Nxxxx in document header wxxxx (short title).docx -- document filename wxxxx.zip – zip archive name |  |  |
|  | Agenda for next meeting |  |  |
|  | Review of Audio presentation to MPEG plenary |  |  |
|  | A.O.B. |  |  |
|  | Closing of the Audio meeting |  |  |
| 1300-1400 | Lunch |  |  |
| 1400- | MPEG Plenary |  |  |

Task Groups

- MPEG-H 3D Audio Phase 1

- MPEG-H 3D Audio Phase 2

- Maintenance of MPEG-2, MPEG-4 and MPEG-D

Output Documents

Documents approved by Audio and jointly by Audio and other subgroups are shown below. Note that document numbers shown in RED are listed in another subgroups resolutions, and shown here for reference.

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 13818-1– Systems |  |  |  |
| 15912 | DoC on ISO/IEC 13818-1:2015/DAM 5 | Harald Fuchs | N | 16/02/26 |
| 15913 | ISO/IEC 13818-1:2015/FDAM 5 | Harald Fuchs | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 14496-3 – Audio |  |  |  |
| 15998 | Text of ISO/IEC 14496-3:2009/AMD 3:2012/COR 1, Downscaled (E)LD | Adrian Murtaza | N | 16/02/26 |
| 15999 | ISO/IEC 14496-3:2009/DAM 6, Profiles, Levels and Downmixing Method for 22.2 Channel Programs | Takehiro Sugimoto | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 14496-5 – Reference software |  |  |  |
| 15924 | Text of ISO/IEC 14496-5:2001/AMD 24:2009/DCOR 3, Downscaled (E)LD | Adrian Murtaza | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 14496-12 – ISO base media file format |  |  |  |
| 15922 | DoC on ISO/IEC 14496-12:2015 PDAM 1 DRC Extensions | David Singer | N | 16/02/26 |
| 15923 | Text of ISO/IEC 14496-12:2015 DAM 1 DRC Extensions | David Singer | N | 16/04/01 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 23003-1 – MPEG Surround |  |  |  |
| 15934 | Study on ISO/IEC 23003-1:2007/DAM 3 MPEG Surround Extensions for 3D Audio | Adrian Murtaza | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 23003-2 – Spatial Audio Object Coding (SAOC) |  |  |  |
| 16076 | ISO/IEC 23003-2:2010/DCOR 3 SAOC, SAOC Corrections | Adrian Murtaza | N | 16/02/26 |
| 16077 | Study on ISO/IEC 23003-2:2010/DAM 4, SAOC Conformance | Adrian Murtaza | N | 16/02/26 |
| 16078 | Study on ISO/IEC 23003-2:2010/DAM 5, SAOC Reference Software | Adrian Murtaza | N | 16/02/26 |
| 16079 | Draft of ISO/IEC 23003-2:2010 SAOC, Second Edition | Adrian Murtaza | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 23003-3 – Unified speech and audio coding |  |  |  |
| 16080 | DoC on ISO/IEC 23003-3:2012/Amd.1:2014/DCOR 2 | Michael Kratschmer | N | 16/02/26 |
| 16081 | Text of ISO/IEC 23003-3:2012/Amd.1:2014/COR 2 | Michael Kratschmer | N | 16/02/26 |
| 16082 | DoC on ISO/IEC 23003-3:2012/DAM 3 Support of MPEG-D DRC, Audio Pre-Roll and IPF | Michael Kratschmer | N | 16/02/26 |
| 16083 | Text of ISO/IEC 23003-3:2012/FDAM 3 Support of MPEG-D DRC, Audio Pre-Roll and IPF | Michael Kratschmer | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 23003-4 – Dynamic Range Control |  |  |  |
| 16084 | Defect Report on MPEG-D DRC | Michael Kratschmer | N | 16/02/26 |
| 16085 | DoC on ISO/IEC 23003-4:2015 PDAM 1, Parametric DRC, Gain Mapping and Equalization Tools | Michael Kratschmer | N | 16/02/26 |
| 16086 | Text of ISO/IEC 23003-4:2015 DAM 1, Parametric DRC, Gain Mapping and Equalization Tools | Michael Kratschmer | N | 16/04/01 |
| 16087 | Request for Amendment ISO/IEC 23003-4:2015/AMD 2, DRC Reference Software | Michael Kratschmer | N | 16/02/26 |
| 16088 | ISO/IEC 23003-4:2015/PDAM 2, DRC Reference Software | Michael Kratschmer | N | 16/03/18 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 23008-3 – 3D Audio |  |  |  |
| 16089 | ISO/IEC 23008-3:2015/DCOR 1 Corrections, | Christian Neukam | N | 16/02/26 |
| 16090 | DoC on ISO/IEC 23008-3:2015/DAM 2, MPEG-H 3D Audio File Format Support | Ingo Hofmann | N | 16/02/26 |
| 16091 | Text of ISO/IEC 23008-3:2015/FDAM 2, MPEG-H 3D Audio File Format Support | Ingo Hofmann | N | 16/02/26 |
| 16092 | Study on ISO/IEC 23008-3:2015/DAM 3, MPEG-H 3D Audio Phase 2 | Max Neuendorf | N | 16/03/18 |
| 16093 | Study on ISO/IEC 23008-3:2015/DAM 4, Carriage of Systems Metadata | Schuyler Quackenbush | N | 16/02/26 |
| 16094 | WD on New Profiles for 3D Audio | Christof Fersch | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | ISO/IEC 23008-6 – 3D Audio Reference Software |  |  |  |
| 16095 | 3D Audio Reference Software RM6 | Achim Kuntz | N | 16/02/26 |
| 16096 | Workplan on 3D Audio Reference Software RM7 | Achim Kuntz | N | 16/02/26 |
| No. | Title | In charge | TBP | Available |
|  | Liaisons |  |  |  |
| 16097 | Liaison Statement to DVB on MPEG-H 3D Audio | Ken McCann | N | 16/02/26 |
| 16098 | Liaison Statement Template on MPEG-H 3D Audio | Ken McCann | N | 16/02/26 |
| 16099 | Liaison Statement to ITU-R Study Group 6 on BS.1196-5 | Schuyler Quackenbush | N | 16/02/26 |
| 16100 | Liaison Statement to IEC TC 100 | Schuyler Quackenbush | N | 16/02/26 |
| 16101 | Liaison Statement to IEC TC 100 TA 4 | Schuyler Quackenbush | N | 16/02/26 |
| 16102 | Liaison Statement to IEC TC 100 TA 5 | Schuyler Quackenbush | N | 16/02/26 |

Agenda for the 115th MPEG Audio Meeting

Agenda Item

- Opening of the meeting

- Administrative matters

  - Communications from the Chair

  - Approval of agenda and allocation of contributions

  - Review of task groups and mandates

  - Approval of previous meeting report

  - Review of AhG reports

  - Joint meetings

  - Received national body comments and liaison matters

- Plenary issues

- Task group activities

  - MPEG-H 3D Audio

  - Maintenance: MPEG-2, MPEG-4, and MPEG-D

  - Audio Exploration

- Discussion of unallocated contributions

- Meeting deliverables

  - Responses to Liaison

  - Recommendations for final plenary

  - Establishment of new Ad-hoc groups

  - Approval of output documents

  - Press statement

- Future activities

- Agenda for next meeting

- A.O.B

- Closing of the meeting

– 3DG report

Source: Marius Preda, Chair

Summary

3DGC meeting report San Diego, February 2016	1

1.	Opening of the meeting	2

1.1	Roll call	2

1.2	Approval of the agenda	2

1.3	Goals for the week	3

1.4	Standards from 3DGC	3

1.5	Room allocation	3

1.6	Joint meetings	4

1.7	Schedule at a glance	4

2.	AhG reports	5

2.1	MPEG-V	5

2.2	Augmented Reality	5

2.3	3D Graphics compression	5

2.4	MIoT and Wearables	6

http://wg11.sc29.org/doc_end_user/documents/114_San%20Diego/ahg_presentations/MIoT-MPEGWearables-AHGR-SanDiego114.pptx-1456203700-MIoT-MPEGWearables-AHGR-SanDiego114.pptx	6

2.5	3D 3DG Activities are reported in the Wednesday and Friday plenary	6

3.	Analysis of contributions	6

3.1	Joint meeting with Systems on MSE AF	14

3.2	Joint meeting with Requirements on IoT and Wearable	14

3.3	Joint meeting with 3DA	14

3.4	Joint Session with JPEG on JPEGAR	14

3.5	Session 3DG Plenary	14

4.	General issues	15

4.1	General discussion	15

4.1.1	Reference Software	15

4.1.2	Web site	15

5.	General 3DG related activities	15

5.1	Promotions	15

5.2	Press Release	15

5.3	Liaison	16

6.	Resolutions from 3DG	16

6.1	Resolutions related to MPEG-4	16

6.1.1	Part 5 – Reference software	16

6.2	Part 16 – Animation Framework eXtension (AFX)	16

6.2.1	The 3DG subgroup recommends approval of the following documents	16

6.3	Part 27 – 3D Graphics conformance	16

6.3.1	The 3DG subgroup recommends approval of the following documents	16

6.4	Resolutions related to MPEG-A	17

6.5	Part 13 – Augmented reality application format	17

6.5.1	The 3DG subgroup recommends approval of the following documents	17

6.6	Part 17 – Multisensorial Media Application Format	17

6.6.1	The 3DG subgroup recommends approval of the following documents	17

6.6.2	The 3DG subgroup thanks US National Body for their comments on ISO/IEC 23000-17:20xx CD	17

6.7	Resolutions related to MPEG-V (ISO/IEC 23005 – Media context and control)	17

6.7.1	General	17

6.7.2	Part 1 – Architecture	17

6.7.3	Part 2 – Control Information	18

6.7.4	Part 3 – Sensory Information	18

6.7.5	Part 4 – Virtual World Object Characteristics	18

6.7.6	Part 5 – Data Formats for Interaction Devices	18

6.7.7	Part 6 – Common types and tools	19

6.8	Resolutions related to MAR Reference Model (ISO/IEC 18039 Mixed and Augmented Reality Reference Model)	19

6.8.1	General	19

6.9	Resolutions related to Explorations	19

6.9.1	Media-centric IoT and Wearable	19

6.9.2	Point Cloud Compression	19

6.10	Management	20

6.10.1	Liaisons	20

7.	Establishment of 3DG Ad-Hoc Groups	20

8.	Closing of the Meeting	21

# Opening of the meeting

## Roll call

## Approval of the agenda

The agenda is approved.

## Goals for the week

The goals of this week are:

- Review contributions related to MPEG-V

- Review contributions related to Augmented Reality

- Status of ref soft and conformance for Web3D Coding

- Review contributions related to MIoT and Wearable

- Edit output documents related to Context, objectives and requirements for MIoT/W

- Contribute to Big Media output documents

- Edit DoCs

- Investigate future developments for MPEG 3D Graphics Compression

- Point cloud compression

- Review and issue liaison statements

- JPEG on AR

- MIoT and Wearable with WG10, ITU-T, IEC SG10, Syc AAL

- Review the votes

- Web-site

- MPEG database

## Standards from 3DGC

| Std | Pt | Edit. | A/E | Description | CfP | WD | CD | DIS | FDIS | Gr. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4 | 5 | 2001 | A40 | 3DG for browsers RS |  |  | 15/06 | 15/10 | 16/06 | 3 |
| 4 | 16 | 2011 | A3 | Web3DG coding |  | 12/10 | 15/02 | 15/10 | 16/06 | 3 |
| 4 | 27 | 2009 | A7 | Web3DC Conformance |  |  | 15/06 | 15/10 | 16/06 | 3 |
| AR |  | 201x | E1 | ARRM |  |  | 14/07 | 16/02 | 16/10 | 3 |
| A | 13 | 201x | E2 | ARAF |  |  | 14/10 | 15/06 | 16/02 | 3 |
| A | 13 | 201x | A1 | ARAF RS & C |  | 15/06 | 15/10 | 16/06 | 17/01 | 3 |
| A | 17 | 201x | E1 | MSMAF |  |  | 15/10 | 16/02 | 16/10 | 3 |
| V | 1 | 201x | E4 | Architecture |  | 15/10 | 16/02 | 16/06 | 17/01 | 3 |
| V | 2 | 201x | E4 | Control information |  | 15/10 | 16/02 | 16/06 | 17/01 | 3 |
| V | 3 | 201x | E4 | Sensory information |  | 15/10 | 16/02 | 16/06 | 17/01 | 3 |
| V | 4 | 201x | E4 | Virtual world object characteristics |  | 15/10 | 16/02 | 16/06 | 17/01 | 3 |
| V | 5 | 201x | E4 | Data formats for interaction devices |  | 15/10 | 16/02 | 16/06 | 17/01 | 3 |
| V | 6 | 201x | E4 | Common types and tools |  | 15/10 | 16/02 | 16/06 | 17/01 | 3 |
| V | 7 | 201x | E3 | RS & C |  |  | 14/07 | 15/10 | 16/06 | 3 |

## Room allocation

3DGC:	Santa Clara

## Joint meetings

During the week, 3DG had several joint meetings with Requirements, Video, Audio and Systems.

| Groups | What | Day | Time1 | Time2 | Where |
| --- | --- | --- | --- | --- | --- |
| R, V, 3 | Everything 3D | Tue | 10:00 | 11:00 | R |
| All | MPEG Vision | Wed | 11:30 | 13:00 | A |
| JPEG-MPEG | Joint standards | Thu | 09:00 | 10:00 | JPEG |
| A, 3 | 3D Audio in VR/AR | Thu | 10:00 | 11:00 | A |
| R, 3 | MIoTW | Thu | 14:00 | 15:00 | 3 |
| All | Communication | Thu | 16:00 | 17:00 | Ocean Beach |
| All | MPEG Vision | Thu | 16:00 | 18:00 |  |

## Schedule at a glance

| Monday |
| --- |
|  | MPEG Plenary | 09h00 to 13h00 |
|  | Lunch | 13h00 to 14h00 |
| Session | Agenda/Status/Preparation of the week | 14h00 to 14h30 |
|  | MIoT and Wearable (xxx) | 14h30 to 17h00 |
| Session | 3DG Plenary, review of 3DG contributions ( xxx ) | 17h00 to 18h00 |
| Tuesday |
|  | ARAF contributions | 09h00 to 10h00 |
| JSession | Everything 3D | 10h00 to 11h00 |
|  | MioT and Wearable (review of contributions) | 11h00 to 13h00 |
|  | Lunch | 13h00 to 14h00 |
|  | MPEG-V (review of contributions) | 14h00 to 16h00 |
|  | MioT and Wearable (review of contributions) | 16h00 to 18h00 |
| Wed |
|  | MPEG Plenary | 09h00 to 11h30 |
| J Session (with all) | MPEG Vision | 11h30 to 13h00 |
|  | Lunch | 13h00 to 14h00 |
|  | MIoT and Wearable (liaisons) | 14h00 to 16h30 |
| Session | ARAF White paper | 16h30 to 17h00 |
| Thu |
| JSession MPEG-JPEG | Joint standards | 09h00 to 10h00 |
| Session | 3D Audio in VR/AR | 10h00 to 11h00 |
| Session | MIoT and Wearable (review draft requirements and DCfP) | 11h00 to 13h00 |
|  | Lunch | 13h00 to 14h00 |
| Requirements | MIoTW | 14h00 to 15h00 |
| Session | MIoT and Wearable output documents | 15h00 to 18h00 |
| JSession | Everything 3D | 15h30 to 16h30 |
| BO Session | Point Cloud compression planning | 16h30 to 18h00 |
| Joint meeting Communication (only for a BO group) | ARAF White Paper | 16h00 to 17h00 |
| Joint meeting with all (only for a BO group) | MPEG Vision | 16h00 to 18h00 |
| Friday |
| Session | Liaisons review, press release, AR and MPEG-V, MIoTW output documents | 09h00 to 10h00 |
| Session | 3DG Plenary, 3DG Output Documents Review, resolutions | 10h00 to 13h00 |
|  | MPEG Plenary | 14h00 to xxh00 |

# AhG reports

## MPEG-V

No AhG was established at the last meeting.

## Augmented Reality

http://wg11.sc29.org/doc_end_user/documents/114_San%20Diego/ahg_presentations/ARAF_AhG_Report.ppt-1456190378-ARAF_AhG_Report.ppt

## 3D Graphics compression

http://wg11.sc29.org/doc_end_user/documents/114_San%20Diego/ahg_presentations/AhG_3DG_monday_san_diego_february.v.1.pptx-1456171057-AhG_3DG_monday_san_diego_february.v.1.pptx

## MIoT and Wearables

## http://wg11.sc29.org/doc_end_user/documents/114_San%20Diego/ahg_presentations/MIoT-MPEGWearables-AHGR-SanDiego114.pptx-1456203700-MIoT-MPEGWearables-AHGR-SanDiego114.pptx

## 3D 3DG Activities are reported in the Wednesday and Friday plenary

Wednesday:

http://wg11.sc29.org/doc_end_user/documents/114_San%20Diego/presentations/MPEG3DGraphicsMercredi.pptx-1456339383-MPEG3DGraphicsMercredi.pptx

Friday:

http://wg11.sc29.org/doc_end_user/documents/114_San%20Diego/presentations/MPEG3DGraphicsVendredi.ppt-1456529824-MPEG3DGraphicsVendredi.ppt

# Analysis of contributions

Wearable & IoT

| m37763 | Root Elements for Media-centric IoT and Wearable (M-IoTW) The root element is considered as a collection of several elements : Data, PUnit, Cmmd, User. | Anna Yang, Jae-Gon Kim, Sungmoon Chun, Hyunchul Ko |
| --- | --- | --- |
| m37764 | Common and Gesture-Based Wearable Description for M-IoTW A draft and initial schema is proposed for each of the following types : Data, PUnit, Cmmd. The technical description is in a very early stage but it be considered as a good starting point | Sungmoon Chun, Hyunchul Ko, Anna Yang, Jae-Gon Kim |
| m37993 | Towards a reference architecture for Media-centric IoT and Wearable (M-IoTW) Summary : A draft architecture inspired by WSO2.org is proposed | Mihai Mitrea, Bojan Joveski |
| m38057 | MIoT Use-case (Vibration subtitle for movie by using wearable device) Resolution: consider this MIoT as an Individual MIoT for part 3 | Da Young Jung, Hyo-Chul Bae, Kyoungro Yoon, |
| m38113 | Speech-Related Wearable Element Description for M-IoTW Summary : Add Smartheadphone that has one or several microphones (regularMic and InearMic) AP : to check the micrphone from MPEG-V and update AP : investigate on considering the generic « audioResource » in PData instead of « speech » | Miran Choi, Hyun-ki Kim |
| m37903 | Use Case of MIoT Summary :We need to embed the global positioning in the metadata of the IoT. AP : add the requierement in the Req Document | Jin Young Lee |
| m37911 | Image analysis description for M-IoTW Summary: A hybrid architecture including some local processing (on the wearable) and some remote processing (more complex) Various image analysis are proposed (face detection and recognition, object detection and recognition, …) Resolution: consider this simple example for identifying MPEG-U and MPEG-UD types that can be reused | duckhwan kim, bontae koo |
| m37975 | MIoT API instances A set of APIs are proposed for MIoT covering basic functionalities. Camera and Tracker MIoT are also proposed | Sang-Kyun Kim, Min Hyuk Jeong, Hyun Young Park |
| m37976 | Introduction to IoTivity APIs (MIoT) Summary: IoTivity is a project proposed by Samsung and Intel for discovery and communication for IoTs. AP: use such a framework for Part 2 of MIoTW | Sang-Kyun Kim, Min Hyuk Jeong, Hyun Young Park, |
| m38041 | Liaison Statement from JTC 1/WG 10 on Revised WD of ISO/IEC 30141 | JTC 1/WG 10 via SC 29 Secretariat |
| m38042 | Liaison Statement from JTC 1/WG 10 on Request contributions on IoT use cases | JTC 1/WG 10 via SC 29 Secretariat |
| m37800 | Wearables and IoT&AAL use case standardisation IEC 62559-2 is specifyig a template for use cases. WG xxx and SyC AAL developped use cases related to IoTs IEC formed a strategy group on Smart Wearable Devices AP : put all the deocuments in a single place to facilitate the access for MPEG members m38041 Liaison Statement from JTC 1/WG 10 on Revised WD of ISO/IEC 30141 JTC 1/WG 10 via SC 29 Secretariat m38042 Liaison Statement from JTC 1/WG 10 on Request contributions on IoT use cases JTC 1/WG 10 via SC 29 Secretariat - Send a liaison to IEC SG 10 (strategic group on Wearable Smart Devices) - CTA standardisation for BCI products (Consumer technology Association) Details are in the documents below : | Kate Grant |
| m37697 | 2016-02-09 11:42:16 | 2016-02-17 18:48:03 | MPEG-V General/All | MIoT Use-case Summary: this contribution was not presented | M. Jalil Piran |

- Part 1. Global architecture, use cases and common requirements

- Part 2. System aspects: discovery, communication

  - to interwork with available platforms, e.g UPnP or SmartBAN or IoTivity or xxx

  - to set up a NEW light layer of presence and capabilities signaling

  - AP: issue a CfP for Part 2 (Sang)

(Note: implementation guidelines for MIoT to be used on other platforms)

- Part 3. Individual M-IoTs, data formats and APIs

  - Sensors and actuators

    - Data format defined in MPEG-V (some may need to be extended), the MIoTW standard deals only with the APIs for Sensors and actuators

    - See MIoT Camera Example

  - Media processing & storage units

    - Data formats and/or API

    - See MotionTracker Example, Face Recognition example

    - AP: issue a CfP for Media processing unit interfaces (Mihai)

- Part 4. Wearable M-IoTs, data formats and APIs

  - Smart Glasses

    - Camera, gesture recognizer, microphone, display, etc.,

  - Smart Watch

  - Fitness tracker, Smart Textile (D-Shirt), Sleep monitoring

- Part 5. M-IoT Aggregates (combining individual MIoTs, eventually with other IoTs)

  - Video Surveillance Systems

  - Car Sensing and Communication System

  - Smart Cities, Smart Factory, Smart Offices

MPEG-V

| m37808 | Proposal of metadata description for light display in MPEG-V Summary: A lightDisplay type is proposed that can be used to activate low resolution displays. These displays can have various forms (not only rectangular) AP: add the color matrix and the mask matrix. The second if used to create an arbitrary form of the LightDevice AP: design a VisualDisplayType (and AuralDisplayType) and an AdvancedLightEffect | Jae-Kwan Yun, Yoonmee Doh, Hyun-woo Oh, Jong-Hyun Jang |
| --- | --- | --- |
| m37831 | A proposal of instantiation to olfactory information for MPEG-V 4th edition part 1 Summary: use cases for enose and olfactory AP: accepted for Part 1 of 4th Edition | Hae-Ryong Lee, Jun-Seok Park, Hyung-Gi Byun, Jang-Sik Choi, Jeong-Do Kim |
| m37860 | Enhancement of Enose CapabilityType for MPEG-V 4th edition part 2 Summary: a full set of enose capabilities is provided. AP: accepted | Sungjune Chang, Hae-Ryong Lee, Hyung-Gi Byun, Jang-Sik Choi, Jeong-Do Kim |
| m37861 | A modification of syntax and examples for EnoseSensorType for MPEG-V 4th edition part 5 Summary: EnoseSensorType AP: add also the MonoChemical type (and change the Scent into MixtureChemical). Boths have CSs. | Jong-Woo Choi, Hae-Ryong Lee, Hyung-Gi Byun, Jang-Sik Choi, Jeong-Do Kim |
| m37977 | Modification of 3DPrintingLUT Summary: add the ThreeDPrintingSpectrumLUT (in addition to ThreeDPrintingXYZLUT) AP: accepted | In-Su Jang, Yoon-Seok Cho, Jin-Seo Kim, Min Hyuk Jeong, Sang-Kyun Kim |
| m37981 | 3D Printing Color Reproduction command and preference Summary: a command for activating or disactivating the color reproduction. AP: accepted | In-Su Jang, Yoon-Seok Cho, Jin-Seo Kim, Min Hyuk Jeong, Sang-Kyun Kim |
| m37999 | Proposal of metadata descriptions for handling sound effect in MPEG-V Summary: Sound Device AP: add the user preference at semantic level (a CS including "theatre, cinema, concert hall, …) | Saim Shin, Jong-Seol James Lee, Dalwon Jang, Sei-Jin Jang, Hyun-Ho Joo, Kyoungro Yoon |
| m38054 | Editor’s input for the WD of MPEG-V Part 1 Version 4 | Seung Wook Lee, JinSung Choi, Kyoungro Yoon |
| m38055 | Editor’s input for the WD of MPEG-V Part 2 Version 4 | Seung Wook Lee, JinSung Choi, Kyoungro Yoon |
| m38056 | Editor’s input for the CD of MPEG-V Part 5 Version 4 | Seung Wook Lee, JinSung Choi, Kyoungro Yoon, Hyo-Chul Bae |

AR

| m37909 | White Paper on ARAF 2nd Edition | Traian Lavric, Marius Preda |
| --- | --- | --- |
| m37910 | Big Data for personalized user experience in AR | Traian Lavric, Marius Preda, Veronica Scurtu |
| m38114 | ARAF Expansion for Transformation System between the outdoor GPS and Indoor Navigation Summary: it is supposed that the indoor location system is able to calculate the latitude, longitude and altitude corresponding to the user position. However, the designer would like to specify indoor POIs by using local coordinates (e.g. 10 meters x 30 meters x 3rd floor) and not the global coordinates (long, lat, altitude). There is a need to calibrate the transformation between the indoor and global positioning systems (this can be communicated to the browser as a instantiation proto). Another possibility is to consider the MapIndoor proto as a child of the MapMarker (this needs a corrigenda for MapMarker because there is no support for children) | JinHo Jeong, HyeonWoo Nam |

Liaison:

| # | Title | Source | Disposition |  |
| --- | --- | --- | --- | --- |
| 37576 | Liaison statement | JTC 1/ WG 10 | IoT | 3 |
| 37581 | JTC 1/WG 10 on Invitation to the 4th JTC 1/WG 10 Meeting | JTC 1/ WG 10 | Invitation to the 4th JTC 1/WG 10 Meeting, 18th-22nd Jan. 2016 | 3 |
| 37582 | JTC 1/WG 10 on Logistical information for the 4th JTC 1/WG 10 Meeting | JTC 1/ WG 10 |  | 3 |
| 37583 | Liaison statement | ITU-T SG 20 | a new Study Group, IoT and its applications including smart cities and communities (SC&C) | 3 |
| 37584 | Liaison statement | JTC 1/ WG 10 | collection of Data related to the Internet of Things | 3 |
| 38041 | Revised WD of ISO/IEC 30141 | JTC 1/ WG 10 | Internet of Things Reference Architecture (IoT RA) | 3 |
| 38042 | Request contributions on IoT use cases | JTC 1/ WG 10 |  | 3 |

3DG

| m37828 | Efficient color data compression methods for PCC | Li Cui, Haiyan Xu, Seung-ho Lee, Marius Preda, Christian Tulvan, Euee S. Jang |
| --- | --- | --- |
| m38136 | Point Cloud Codec for Tele-immersive Video | Rufael Mekuria (CWI), Kees Blom (CWI), Pablo Cesar (CWI) |
| m37528 | [FTV AHG] Further results on scene reconstruction with hybrid SPLASH 3D models Improvements on the SPLASH reconstruction from image + depth. Point cloud can be the base representation. | Sergio García Lobo, Pablo Carballeira López, Francisco Morán Burgos |
| m37934 | Web3D Coding for large objects with attributes and texture Summary: update for the Web3D ref software (support for high resolution textures, better navigation) | Christian Tulvan, Euee S. Jang, Marius Preda |

Text copied from the last version of the report in order to guideline the work on Wearable

Glasses (see-through and see-closed) Gesture recognition (performed by image analysis) Add new gestures (update the classification schema) MPEG-U could be the starting point Consider an intermediate representation format for arbitrary hand(s) gestures MPEG-7 ShapeDescriptor (Contour and Region) can be the starting point Adaptation of the recognition process with respect to the user MPEG-UD could be the starting point Voice recognition (check with Audio) Recognizing "some" voice commands Pre-encoded keywords: play, pause, left, right, User configured set of "words" Able to transmit the captured audio to a processing unit Probably encoded Probably sound features Interpret ambient sounds Image analysis (other than gesture) Recognizing "some" objects (e.g. Traffic signaling) CDVS and probably CDVA Face recognition MPEG-7 (FaceRecognition Desc, AdvancedFaceRecognition Desc and InfraredFaceRecognition Desc) Text recognition Image to string – not too much to standardize however the in/out API should be defined Able to transmit the captured image/video to a processing unit Probably encoded : MPEG-4 video and JPEG Probably image or video features (CDVS and CDVA) Able to convert in real time the captured image into another image (that will be eventually displayed) Input: image, output: image– not too much to standardize however the in/out API should be defined User interface Sensors MPEG-V could be the starting point Gyro, Accelerometer, Camera (color, stereoscopic, infrared, …), microphone, touch sensitive device, gaze tracker (?!) Display capabilities (Single, double screen, Stereoscopic) MPEG-V has the possibility to define actuator capabilities but is not dealing yet with displays Rendering Rendering is controlled by the application The glass should expose rendering capabilities (HW acceleration, speed, extensions…) Consider the user profile for adapting glass features MPEG-UD Control and management Define level of quality for individual components in the glass system Example: voice recognition may have level 100 and object recognition only 30: in case of lack of resources, voice recognition will have priority Exposing the hardware capabilities (CPU, GPU, memory, storage, battery level, …) Define level of quality for individual applications (to be moved outside the glass section) Informative Part Typical overall architecture for smart glasses Use cases examples Communication and interconnection between glasses and external devices Messages, commands Eg. http, udp Media (image, video, audio) Eg. DASH

Wearable we want to deal with in MPEG

- Glasses

- Watches (Miran Choi). AP: to do the same exercise that was done for glasses.

- Earphone (Miran Choi). AP: to do the same exercise that was done for glasses.

- Artificial heart (Mihai Mitrea). AP: to do the same exercise that was done for glasses.

- D-Shirt (Mihai Mitrea). AP: to do the same exercise that was done for glasses.

Text copied from the last version of the report in order to guideline the work on MIoT:

MIoT should expose timing information MIoT should expose location information (from the use case of fire surveillance system) MIoT should be able to implement specific image processing algorithms and provides codes with respect to a detected situation Defined some classes for image processing IoTs that we care about video camera microphone display (visual, auditory, olfactory, haptic) media storage media analyzers MIoT camera Sensing MPEG-V camera sensor (5 types already defined: color, depth, stereoscopic, thermo, spectrum) Some local Processing and support from a processing unit Compression (MPEG-4 video) Feature extraction and their transmission Face feature extraction (MPEG-7) Gesture recognition (MPEG-U ++) Feature extraction for arbitrary textures (CDVS) Color, shape, contour, texture pattern, motion trajectory, … (MPEG-7) Fire Full processing Send compact commands to outside, depending on the application; some commands can be standardized Sensors & Actuators may become Engines (Active components, xxx) (we should add APIs on top of MPEG-V s&a), therefore, they become IoTs. Some of them are MIoTs. We can add some processing capabilities for some of them, from low processing (sampling, compression, ..) to high processing (interpretation, analysis, …). We can also build aggregates of MIoTs and IoTs and wearable are an example of these aggregates. Alternatives MIoT as a new part in MPEG-V containing the APIs Not so appropriate for MIoTs that don't have sensing or actuating (like media analyzers or media storage) MIoT like MPEG-M engines Not so appropriate because the MPEG-M engines are usually complex A new project One layer contains individual MIoTs A second layer aggregates individual MIoTs, eventually with other IoTs A particular class of this layer is the wearable Another class is the large scale systems (e.g. multi-cam surveillance systems)

- Output documents:

  - Overview, context and objectives of Media-centric IoTs and Wearables (Marius) 3w

  - Conceptual model, architecture and use cases for Media-centric IoTs and Wearables (Mihai and Sang) 3w

  - Draft requirements for Media-centric IoTs and Wearables (Sang and Mihai) 3w

    - E.g. Category MIoT Camera

    - E.g. Category glasses

    - …

- M-IoTW Ahg Mandate

  - Improve and clarify the area of M-IoTW

  - Identify and document additional use cases for M-IoTW

  - Refine requirements for M-IoTW

  - Prepare material for CfP (e.g. scope, evaluation criteria, data set)

  - Investigate IoT Architectures for specific domains and how MIoTW will interwork with them

  - Identify the list of MPEG technologies related to M-IoTW

  - Identify key organizations in IoT and Wearables and the status of their work

  - Analyse the Working Draft of Information technology— Internet of Things Reference Architecture (IoT RA) and submit initial comments for their next meeting

## Joint meeting with Systems on MSE AF

No joint meeting was organized this meeting, MSE AF was handled by 3DG alone.

## Joint meeting with Requirements on IoT and Wearable

Definitions of IoT and Wearables terms:

| Entity | any physical or virtual object that is sensed by and / or acted on by Things. |
| --- | --- |
| Thing | any thing that can communicate with other Things, in addition it may sense and / or act on Entities. |
| Media Thing | is a Thing with at least one of audio / visual sensing and actuating capabilities |
| Wearer | any living organism that is sensed by a Wearable. |
| Wearable | any thing that senses the Wearer, may have control, communication, storage and actuation capabilities, and may sense the Wearer environment. |
| Mwearable | a Wearable having at least one of media communication or storage capabilities |

Three types of Wearables were illustrated by using the MPEG-V Architecture.

## Joint meeting with 3DA

No joint meeting was organized this meeting.

## Joint Session with JPEG on JPEGAR

No joint meeting was organized this meeting.

## Session 3DG Plenary

Review of all the output documents. Details are provided in the documents listed in section 6.

# General issues

## General discussion

### Reference Software

It is recalled that the source code of both decoder AND encoder should be provided as part of the Reference Software for all technologies to be adopted in MPEG standards. Moreover, not providing the complete software for a published technology shall conduct to the removal of the corresponding technical specification from the standard.

Currently all the AFX tools published in the third edition are supported by both encoder and decoder implementation.

### Web site

The new web site is available at http://wg11.sc29.org/3dgraphics/. It is a blog-based web site and all members are allowed to post.

# General 3DG related activities

## Promotions

## Press Release

Augmented Reality Application Format reaches FDIS status

At the 114th MPEG meeting, MPEG's Application Format for Augmented Reality (ISO/IEC 23000-13) has reached FDIS status and will be soon published as an International Standard. The MPEG ARAF enables augmentation of the real world with synthetic media objects by combining multiple, existing MPEG standards within a single specific application format addressing certain industry needs. In particular, ARAF comprises three components referred to as scene, sensor/actuator, and media. The scene component is represented using a subset of MPEG-4 Part 11 (BIFS), the sensor/actuator component is defined within MPEG-V, and the media component may comprise various types of compressed (multi)media assets using different modalities and codecs. The target applications include geo-location based services, image based object detection and tracking, audio recognition and synchronization, mixed and augmented reality games and real-virtual interactive scenarios.

MPEG issues the 4th Edition of MPEG-V CD for communication between actors in virtual and physical worlds

At 114th meeting, MPEG have released the 4th edition of MPEG-V CD (from part 1 to 6) that supports new sensors and actuator such as 3DPrinter, ArrayCamera, E-nose, Radar, Microphone, SoundDisplay and sensory effects such as AdvancedLight. In general, MPEG-V specifies the architecture and associated representations to enable interaction between digital content and virtual worlds with the physical one, as well as information exchange between virtual worlds. Features of MPEG-V enable the specification of multi-sensorial content associated with audio/video data, and control of multimedia applications via advanced interaction devices.

## Liaison

Answer to ITU-T SG20 liaison on IoT. An output document was produced.

Answer to JTC1 WG10 liaison on IoT. An output document was produced.

# Resolutions from 3DG

## Resolutions related to MPEG-4

### Part 5 – Reference software

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 14496-5 – Reference software |  |  |  |

## Part 16 – Animation Framework eXtension (AFX)

### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 14496-16 – Animation Framework eXtension (AFX) |  |  |  |
| 16037 | Core Experiments Description for 3DG | Christian Tulvan | N | 16/02/26 |

## Part 27 – 3D Graphics conformance

### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 14496-27 – 3D Graphics conformance |  |  |  |

## Resolutions related to MPEG-A

## Part 13 – Augmented reality application format

### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23000-13 – Augmented reality application format |  |  |  |
| 16103 | Text of ISO/IEC FDIS 23000-13 2nd Edition Augmented Reality Application Format | Traian Lavric | N | 16/03/03 |

## Part 17 – Multisensorial Media Application Format

### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23000-17 – Multisensorial Media Application Format |  |  |  |
| 16104 | DoC for ISO/IEC 23000-17:20xx CD Multiple Sensorial Media Application Format | Sang Kyun Kim | N | 16/02/26 |
| 16105 | Text of ISO/IEC 23000-17:20xx DIS Multiple Sensorial Media Application Format | Sang Kyun Kim | N | 16/02/26 |

### The 3DG subgroup thanks US National Body for their comments on ISO/IEC 23000-17:20xx CD

## Resolutions related to MPEG-V (ISO/IEC 23005 – Media context and control)

### General

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005 – Media context and control |  |  |  |
| 16106 | Technology under consideration | Seung Wook Lee | N | 16/02/26 |

### Part 1 – Architecture

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005-1 – Architecture |  |  |  |
| 16107 | Request for ISO/IEC 23005-1 4th Edition Architecture | Marius Preda |  | 16/02/26 |
| 16108 | Text of ISO/IEC CD 23005-1 4th Edition Architecture | Marius Preda |  | 16/02/26 |

#### The 3DG recommends to appoint Marius Preda and Seung Wook Lee as editors of ISO/IEC 23005-1 4th Edition Architecture

### Part 2 – Control Information

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005-2 – Control information |  |  |  |
| 16109 | Request for ISO/IEC 23005-2 4th Edition Control Information | Seung Wook Lee |  | 16/02/26 |
| 16110 | Text of ISO/IEC CD 23005-2 4th Edition Control Information | Seung Wook Lee |  | 16/03/11 |

#### The 3DG recommends to appoint Seung Wook Lee and Sang Kyun Kim as editors of ISO/IEC DIS 23005-2 4th Edition Control Information

### Part 3 – Sensory Information

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005-3 – Sensory information |  |  |  |
| 16111 | Request for ISO/IEC 23005-3 4th Edition Sensory Information | Sang Kyun Kim |  | 16/02/26 |
| 16112 | Text of ISO/IEC CD 23005-3 4th Edition Sensory Information | Sang Kyun Kim |  | 16/03/11 |

#### The 3DG recommends to appoint Sang Kyun Kim as editor of ISO/IEC DIS 23005-3 4th Edition Sensory Information

### Part 4 – Virtual World Object Characteristics

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005-4 – Virtual world object characteristics |  |  |  |
| 16113 | Request for ISO/IEC 23005-4 4th Edition Virtual world object characteristics | In-Su Jang |  | 16/02/26 |
| 16114 | Text of ISO/IEC CD 23005-4 4th Edition Virtual world object characteristics | In-Su Jang |  | 16/03/11 |

#### The 3DG recommends to appoint In-Su Jang and Sang Kyun Kim as editors of ISO/IEC DIS 23005-4 4th Edition Virtual world object characteristics

### Part 5 – Data Formats for Interaction Devices

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005-5 – Data formats for interaction devices |  |  |  |
| 16115 | Request for ISO/IEC 23005-5 4th Edition Data Formats for Interaction Devices | Seung Woo Kum |  | 16/02/26 |
| 16116 | Text of ISO/IEC CD 23005-5 4th Edition Data Formats for Interaction Devices | Seung Woo Kum |  | 16/03/11 |

#### The 3DG recommends to appoint Seung Woo Kum, Sang Kyun Kim and Kyoungro Yoon as editors of ISO/IEC DIS 23005-5 4th Edition Data Formats for Interaction Devices

### Part 6 – Common types and tools

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 23005-6 – Common types and tools |  |  |  |
| 16117 | Request for ISO/IEC 23005-6 4th Edition Common types and tools | Kyoungro Yoon |  | 16/02/26 |
| 16118 | Text of ISO/IEC CD 23005-6 4th Edition Common types and tools | Kyoungro Yoon |  | 16/03/11 |

#### The 3DG recommends to appoint Kyoungro Yoon as editor of ISO/IEC DIS 23005-6 4th Edition Common types and tools

## Resolutions related to MAR Reference Model (ISO/IEC 18039 Mixed and Augmented Reality Reference Model)

### General

#### The 3DG subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | ISO/IEC 18039 Mixed and Augmented Reality Reference Model |  |  |  |
| 16119 | Text of ISO/IEC 2nd CD 18039 Mixed and Augmented Reality Reference Model | Marius Preda | Y | 16/02/26 |

#### The 3DG subgroup recommends, at the request of SC24 WG9 concerning minor editorial and formatting aspects, to withdraw the ISO/IEC DIS 18039 Mixed and Augmented Reality Reference Model issued at 112th MPEG meeting, and transform it into a 2nd CD. In order to minimize further delays in processing this standard we request two months CD ballot to be implemented by both SCs so that the ballot results become available before the next meetings of the working groups.

## Resolutions related to Explorations

### Media-centric IoT and Wearable

#### The 3 subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | Explorations – Media-centric Internet of Things and Wearable |  |  |  |
| 16120 | State of discussions related to MIoTW technologies | Marius | N | 16/02/26 |

### Point Cloud Compression

#### The 3 subgroup recommends approval of the following documents

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | Explorations – Point Cloud Compression |  |  |  |
| 16121 | Current status on Point Cloud Compression (PCC) | Lazar Bivolarsky | N | 16/03/11 |
| 16122 | Description of PCC Software implementation | Lazar Bivolarsky | N | 16/03/11 |

## Management

### Liaisons

#### 3DG recommends approval of the following document

| No. | Title | In charge | TBP | Available |
| --- | --- | --- | --- | --- |
|  | Liaisons |  |  |  |
| 16123 | Liaison Statement to JTC1 WG10 related to MIoT | Marius | N | 16/02/26 |
| 16124 | Liaison Statement to ITU-T SG20 related to MIoT | Marius | N | 16/02/26 |

# Establishment of 3DG Ad-Hoc Groups

|  | AHG on AR |
| --- | --- |
| Mandates | Edit MAR RM documents Continue the implementation of ARAF Reference Software Identify additional needs for ARAF Investigate technologies for representing Points of Interests Identify the MPEG technologies that shall be part of ARAF Continue actions to implement the collaborative work-plan for MAR RM with SC24 |
| Chairmen | Traian Lavric (Institut Mines Telecom), Marius Preda (Institut Mines Telecom) |
| Duration | Until 115th MPEG Meeting |
| Reflector | mpeg-3dgc AT gti. ssr. upm. es |
| Subscribe | To subscribe, send email to https://mx.gti.ssr.upm.es/mailman/listinfo/mpeg-3dgc |
| Meeting | During weekend prior to MPEG | Room size | 20 |
|  | Before weekend prior to MPEG | Place /Date/Logistics May 29th, 17h00-18h00 |

|  | AHG on MPEG-V |
| --- | --- |
| Mandates | Edit the MPEG-V documents To further develop tools for MPEG-V 4th Edition and discuss related contributions. Collect material for reference software and conformance of MPEG-V 3rd Edition |
| Chairmen | Marius Preda (Institut Mines Telecom), Seung Wook Lee (ETRI) |
| Duration | Until 115th MPEG Meeting |
| Reflector | metaverse@lists.aau.at |
| Subscribe | http://lists.aau.at/mailman/listinfo/metaverse |
| Meeting | During weekend prior to MPEG | Room size | 20 |
|  | Before weekend prior to MPEG | Place /Date/Logistics May 29th, 15h00-17h00 |

|  | AHG on Graphics compression |
| --- | --- |
| Mandates | Refine requirements for PCC Solicit and compile additional test data for point clouds, including point clouds with multiple attributes per point Solicit contribution related to evaluation metrics Propose a raw representation for point clouds geometry and appearance Further develop compression technologies for point clouds geometry and appearance Collect contributions and maintain the utility software Logistic preparation for a potential workshop |
| Chairmen | Lazar Bivolarski (LZ), Rufael Mekuria (CWI), Christian Tulvan (Institut Mines Telecom), |
| Duration | Until 115th MPEG Meeting |
| Reflector | mpeg-3dgc AT gti. ssr. upm. es |
| Subscribe | To subscribe, send email to https://mx.gti.ssr.upm.es/mailman/listinfo/mpeg-3dgc |
| Meeting | During weekend prior to MPEG | Room size | 20 |
|  | Before weekend prior to MPEG | Place /Date/Logistics Sunday May 29th 2016, 09h00-18h00 |

# Closing of the Meeting

See you in Geneva.