INTERNATIONAL ORGANISATION FOR STANDARDISATION

ORGANISATION INTERNATIONALE DE NORMALISATION

ISO/IEC JTC 1/SC 29/WG 11

CODING OF MOVING PICTURES AND AUDIO

ISO/IEC JTC 1/SC 29/WG 11 N14003

Geneva, CH – November 2013

| Source: | Leonardo Chiariglione |
| --- | --- |
| Title: | MPEG work plan and time line |
| Purpose: | Work plan management |

MPEG work plan and time line

Contents

1	Media coding	4

1.1	Signalling and Transport of SAOC-DE in AAC	4

1.2	MVC extension for inclusion of depth maps	4

1.3	AVC compatible video with depth information	4

1.4	Additional Colour Space and Tone Mapping Descriptors	4

1.5	Multi-resolution Frame Compatible (MFC)	4

1.6	Pattern Based 3D Mesh Compression	5

1.7	Metadata for Realistic Material Representation	5

1.8	Font compression and streaming	5

1.9	Composite Font Representation	5

1.10	Open Font Format	5

1.11	Web Video Coding	6

1.12	Media Tool Library	6

1.13	SAOC Dialog enhancement	6

1.14	Media Context and Control – Control Information	6

1.15	Media Context and Control – Sensory Information	6

1.16	Media Context and Control – Virtual World Object Characteristics	6

1.17	Media Context and Control – Data Formats for Interaction Devices	6

1.18	Media Context and Control – Common Types and Tools	7

1.19	HEVC Range Extensions	7

1.20	HEVC Multiview Extensions	7

1.21	HEVC scalable extensions	7

1.22	HEVC Interlace	7

1.23	HEVC Image Sequences	7

1.24	HEVC Frame Packing Arrangement Types	7

1.25	Coding of non camera captured content	8

1.26	3D HEVC	8

1.27	3D Audio	8

1.28	Audio Dynamic Range Control	8

1.29	Internet Video Coding	8

1.30	Web 3D Graphics Coding	8

1.31	Video Coding for browsers	9

1.32	Full Gamut Content Distribution	9

2	Composition coding	9

2.1	Scene Description Based Collaborative Applications	9

2.2	Advanced User Interaction	9

2.3	MMT Composition Information	9

3	Description coding	10

3.1	Compact Descriptors for Visual Search	10

3.2	Compact Descriptors for Video Search	10

3.3	Social Metadata	10

3.4	User Description	10

3.5	Coding modes description	10

4	Systems support	10

4.1	Signalling of Transport profiles, signalling MVC stereo view association and MIME type registration	10

4.2	Support of DASH event signalling in MPEG-2 TS	11

4.3	Support for raw audio-visual data	11

4.4	Coding-independent codepoints	11

4.5	MMT Forward Error Correction Codes	11

4.6	MMT Cross Layer Interface	11

4.7	Uniform signalling for timeline alignment	12

5	IPMP	12

5.1	Common Encryption Format for MPEG-2 Transport Stream	12

5.2	Common Encryption Format for ISO Base Media File Format	12

5.3	AES-CBC-128 and key rotation	12

6	Digital Item	12

7	Transport and File formats	12

7.1	MPEG-2 Systems DASH support	12

7.2	Simplified carriage of MPEG-4 over MPEG-2 TS	13

7.3	Enhanced audio support and other improvements	13

7.4	Delivery of Timeline for External Data	13

7.5	Signalling of Transport profiles and MVC stereo view association, and MIME type registration	13

7.6	Transport of MVC depth video and HEVC low delay	14

7.7	Carriage of quality information in ISOBMFF	14

7.8	Carriage of MVC+D in ISO Base Media File Format	14

7.9	Ordered combination of separate tracks	14

7.10	Carriage of HEVC in ISO Base Media File Format	14

7.11	Sample group and sub-track definitions for HEVC tiles	15

7.12	Timed Text and Other Visual Overlays in ISO Base Media File Format associated	15

7.13	DASH	15

7.14	MPEG-DASH Implementation Guidelines	15

7.15	Format independent segment encryption and authentication	15

7.16	MPEG Media Transport	16

7.17	Additional technologies for MPEG Media Transport	16

7.18	MMT Implementation Guidelines	16

8	Multimedia architecture	16

8.1	MPEG-M API	16

8.2	MPEG-V Architecture	16

9	Application formats	17

9.1	Surveillance Application Format	17

9.2	Support of movie fragment structure for SVAF	17

9.3	Augmented Reality AF	17

9.4	Augmented Reality Reference Model	17

9.5	Multimedia Preservation	17

9.6	Mixed and Augmented Reality Reference Model	18

10	Reference implementation	18

10.1	MVC plus depth extension of AVC Reference Software	18

10.2	Multi-resolution Frame Compatible Stereo Coding extension of AVC Reference Software	18

10.3	Efficient representation of 3D meshes with multiple attributes Reference Software	18

10.4	Reference software multi-resolution 3D mesh compression	18

10.5	CEL and MCO Reference Software	18

10.6	Surveillance Reference Software	18

10.7	SVAF Reference Software	19

10.8	IMAF Reference Software	19

10.9	ARAF reference software	19

10.10	Media Tool Library Reference Software	19

10.11	SAOC Reference Software	19

10.12	USAC Reference Software	19

10.13	MPEG-DASH Reference Software	20

10.14	MPEG-V – Reference Software	20

10.15	HEVC Reference Software	20

11	Conformance	20

11.1	Low Delay AAC v2 Profile Conformance	20

11.2	MVC plus Depth Conformance	20

11.3	Multi-resolution Frame Compatible Stereo Coding extension of AVC Conformance	20

11.4	3D-AVC Conformance	20

11.5	3D Efficient representation of 3D meshes with multiple attributes Conformance	21

11.6	Multiresolution 3D mesh coding Conformance	21

11.7	CEL and MCO Conformance	21

11.8	Surveillance Conformance	21

11.9	SVAF Conformance	21

11.10	IMAF Conformance	21

11.11	ARAF Conformance	21

11.12	Media Tool Library Conformance	21

11.13	MPEG Surround conformance for Low Delay AAC v2 profile	22

11.14	SAOC Conformance	22

11.15	USAC Conformance	22

11.16	MPEG-DASH Conformance	22

11.17	HEVC Conformance	22

11.18	MPEG-V – Conformance	22

12	Maintenance	23

12.1	Systems coding standards	23

12.2	Video coding standards	23

12.3	Audio coding standards	23

12.4	3DG coding standards	23

12.5	Systems description coding standards	23

12.6	Visual description coding standards	23

12.7	Audio description coding standards	23

12.8	MPEG-21 standards	24

12.9	MPEG-A standards	24

13	Work plan and time line	24

# Media coding

## Signalling and Transport of SAOC-DE in AAC

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 3 | 4 |  | Mechanism to signal and transport SAOC Dialog Enhancement (SAOC-DE) profile data in the context of MPEG-4 Audio. |

## MVC extension for inclusion of depth maps

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 10 | 2 |  | Enhancement of the adaptability of viewing perspectives for 3D video content by supplementing multiview video coding (MVC) coded content with depth map information. |

## AVC compatible video with depth information

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 10 |  |  | This work consists of encoding a rich representation of 3D video content by supplementing an AVC-compatible "base view" with additional views and depth map information in an efficiently-coded manner. |

## Additional Colour Space and Tone Mapping Descriptors

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 10 | 4 |  | The purpose of this amendment of AVC is to add new UHDTV colorimetry as specified in ITU-R BT.2020, and new mode in tone mapping SEI. This amendment adds the same functions in AVC which are already defined in HEVC to keep consistency between the two standards. |

## Multi-resolution Frame Compatible (MFC)

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 10 | 5 |  | The purpose of this amendment is enabling full resolution stereoscopic video coding with frame compatible AVC signals. The frame-compatible stereoscopic signal is coded as the base view. The non-base view contains the enhancement information coded by MVC to enable reconstruction of the full resolution stereoscopic signal. |

## Pattern Based 3D Mesh Compression

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 16 |  |  | The coding of 3D meshes utilizing a pre-processing algorithm for discovering repetitive geometry structures in the mesh. Such structures are transformed (various positions, orientations and scaling factors) and combined such as the 3D model is organized into “pattern-instance” representation. A pattern is the representative geometry of the corresponding repetitive structure. |

## Metadata for Realistic Material Representation

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 16 |  |  | This parts defines the realistic material representations to specify makeup information on a face. Combined with the spectrum light source and the spectrum textures of objects specified in the MPEG-4 Part 11, this information enables to reproduce a realistic avatar appearance |

## Font compression and streaming

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 18 | 1 |  | This amendment clarifies usage of font data streams decoder specific information, and provide tools to carry font data streams in ISO/IEC 14496-12 |

## Composite Font Representation

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 22 |  |  | The advances in developing the Unicode Standard and the addition of new characters that represent most of the world's languages and writing systems resulted in a significant increase of the Unicode character repertoire to more than 100,000 characters. However, due to the finite size of many bitfields, the existing ISO/IEC 14496-22:2009 specification only provides the capabilities for a single font to support up to 64K glyphs. The Composite Font Standard is intended to resolve the existing limitation by providing a solution that would allow linking of existing OFF fonts (and, possibly, fonts in other formats) into a single Composite Font to be used as a virtual font by any compliant implementation. |

## Open Font Format

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 22 | E3 |  | The third edition of the OFF standard consolidates all previously issued corrigendum and amendments and extends the existing technology providing support for a larger set of world's languages, adding new text layout features and introducing support for colour fonts and MATH expression layout |

## Web Video Coding

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 29 | E1 |  | WVC coding aims to deliver a video coding standard based on royalty-free technology with a performance similar to AVC Baseline Profile |

## Media Tool Library

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| C | 4 |  |  | The Media Tool Library (MTL) is a collection of video and graphics coding tools, called Functional Units (FUs). Each FU implements a specific processing block in the coding process and it is specified by both a textual specification, that provides its purpose, and a reference implementation expressed in RVC-CAL Actor Language (RVC-CAL). The textual description provides to each FU a name, a short description of its functionality, the standard and the Profile it comes from, and the properties of its input and output data. |

## SAOC Dialog enhancement

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 3 | 3 |  | Extension to be used as a supplementary audio codec in the broadcasting environment to efficiently control the dialogue level in a backwards-compatible way. |

## Media Context and Control – Control Information

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 2 |  |  | The scope of MPEG-V part2 is defined as the capability descriptions of actuators/sensors in the real world, the user's sensory preference information, which characterize devices and users, and the sensor adaptation preferences information, which characterize sensors and users, so that appropriate information to control devices (actuators and sensors) can be generated. |

## Media Context and Control – Sensory Information

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 3 |  |  |  |

## Media Context and Control – Virtual World Object Characteristics

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 4 |  |  | This part defines a base type of attributes and characteristics of the virtual world objects which is shared by both avatars and the generic virtual objects. The base type of the virtual world object characteristics is composed of data types describing an identity, sound resources, scent resources, controlling, input events, and a behavior model. The virtual world object base type is inherited to both avatar metadata and virtual object metadata to extend the specific aspects of each of metadata. |

## Media Context and Control – Data Formats for Interaction Devices

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 5 |  | 10990 |  |

## Media Context and Control – Common Types and Tools

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 6 |  |  |  |

## HEVC Range Extensions

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | 1 |  | The purpose of this amendment is to provide the capability to support high fidelity video signals in HEVC. In high end consumer and professional environment, greater sample accuracy and alternative chroma sampling structure are used. This amendment is to extend the capability of ISO/IEC 23008-2 for those applications. |

## HEVC Multiview Extensions

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | 2 |  | The purpose of this amendment of HEVC is to provide the simple capability to support stereoscopic and multiview video. Stereoscopic and multiview video are emerging to the market and this extension provides a simple and efficient video coding with no changes at lower decoder levels, such that re-purposing of existing devices would be possible. Monoscopic video can be extracted as base view. |

## HEVC scalable extensions

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | ? |  | The purpose of this amendment HEVC is to provide scalability at the bitstream level, such that a sub-bitstream would allow reconstruction of a video with lower resolution or lower quality. Hierarchies of sub-bitstreams can be supported, where the lowest level (base layer) would also be extractable and decodable by a legacy device (e.g. conforming to main profile of HEVC). |

## HEVC Interlace

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | ? |  | The first version of HEVC supports coding of interlaced video at rates significant lower than possible with AVC. Still, further improvements might become available by tuning HEVC |

## HEVC Image Sequences

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | ? |  | HEVC is very efficient in coding intra images. In order to support applications like camera recording a sequence of still images, MPEG will extend its file format to support the sequences of images along with the meta data that is typically associated with single images. |

## HEVC Frame Packing Arrangement Types

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | ? |  |  |

## Coding of non camera captured content

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | ? |  | For applications like screen shareing, wireless display and remote computing, efficient coding of the computer screen content is important. Since this content has statistical properties different to natural video, MPEG investigates technology focussing on this material. |

## 3D HEVC

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 2 | ? |  | This work consists of encoding a rich representation of 3D video content by supplementing HEVC to encode additional views and depth map information jointly in an efficiently-coded manner. |

## 3D Audio

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 3 | 1E |  | This is an exploration of the role that MPEG audio standardization can play in two emerging trends in multi-media. The first is "3-D Audio" in which there may be many loudspeakers used in the audio presentation. Issues being explored are how to automatically adapt audio program material to the target number of loudspeakers in a given consumer's listening venue. The second is "Audio for new video presentation" in which the video will very high resolution (as in MPEG HEVC). This would permit a closer viewing distance such that the user is within the audio near field. Issues being explored are how the audio presentation (i.e. number and position of loudspeakers) can enhance sound source localization and the sense of immersiveness. Both large "home theatre" and smaller portable audio-visual presenations are being considered. |

## Audio Dynamic Range Control

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 4 | ? |  | The Dynamic Range Control (DRC) standard specifies technology for coding and applying DRC and Program Level control to audio. It is designed to work with any MPEG audio codec, including MPEG-4 AAC, HE-AAC, MPEG-D USAC and MPEG-H 3D Audio. |

## Internet Video Coding

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ?? | ?? |  |  | Internet Video Coding (IVC) aims to develop a video coding standard based on royalty-free technology with a performance as good as possible under the given constraints. |

## Web 3D Graphics Coding

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? | 1st Ed |  | An exploratory activity aiming at implementing the 3DG decompression tools in javascript such as they can be executed by a web browser |

## Video Coding for browsers

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? | ? |  | Video Coding for Browsers (VCB) aims to develop a video coding standard based on royalty-free technology with a performance as good as possible under the given constraints. |

## Full Gamut Content Distribution

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? | ? |  | In the near future, we will have displays able to display many more colors that todays TV sets. MPEG investigates ways to enable transport of video with a wider color gammut and high dynamic range. |

# Composition coding

## Scene Description Based Collaborative Applications

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 11 | 4 |  | The Widgets Extensions amendment of 23007-1 contains a small set of extensions coming from early implementation experience. The protocol for widget migration has been defined to ensure the interoperability of widget managers sharing the same service protocol. The possibility to migrate a widget to multiple other widget managers has been added. A simple capabilities exchange mechanism has been added for a widget manager to be able to migrate the appropriate version of a widget to another widget manager. |

## Advanced User Interaction

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 20 | 4 |  | Specifies advanced user interaction interfaces to support various advanced user interaction devices such as a multi-point interaction device. A mapping mechanism needed to utilize ISO/IEC 23005-5 Data Formats for Interaction Devices in ISO/IEC 23007 is provided in this part. Additional interfaces accommodating Advanced User Interaction that can be utilized by ISO/IEC 23007-1 and ISO/IEC 14496-20 are provided. |

## MMT Composition Information

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 11 | ? |  | MMT defines a composition layer to enable the authoring and delivery of rich media services. The Composition Information (Cl) is authored using HTML5 and thus exhibits all the Capabilities and tools availablefor HTML5. In addition, MMT CI provides tools to support dynamic media scenes and their delivery over unicast channels, authoring of content for secondary screens, as well as separation of media dynamics from scene setup. This is achieved in a backward compatible manner using a dedicated CI file that is in XML format. |

# Description coding

## Compact Descriptors for Visual Search

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 7 | 13 | E1 |  | Relating contents of images with databases requires to describe the images and match the description of the image to the one available in the database. This activity strives to create compact descriptors that allow for efficient search of images in databases. |

## Compact Descriptors for Video Search

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? | ? |  |  |

## Social Metadata

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 7 | 5 | 4 |  | This Amendment provides means for describing a person beyond the context of the Person DS. The description especially targets the annotation of a person's interests in the context of social networking platforms as well as the collaborative review and rating of media entities. |

## User Description

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? | 1st Ed |  | The MPEG User Description (MPEG-UD) aims to provide interoperability among various personalized applications and services. A user can store all his information in the MPEG-UD. The MPEG-UD may be safely and securely managed by the users, e.g. by separating between public and private encrypted data. Some data is static in while other data is dynamic. |

## Coding modes description

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? | 1st Ed |  | Green MPEG |

# Systems support

## Signalling of Transport profiles, signalling MVC stereo view association and MIME type registration

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 |  |  |  |

## Support of DASH event signalling in MPEG-2 TS

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 |  |  | Amendment 1 to ISO/IEC 23009-1 (DASH) specifies event signaling data in both Mp4 file format and MPEG-2 TS. The event signaling data is uniquely carried in transport stream (ISO/IEC 13818-1). This amendment to ISO/IEC 13818-1, allocates the formerly reserved PID 4 for adaptive streaming information (event signaling data). |

## Support for raw audio-visual data

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 1 | 2 |  |  |

## Coding-independent codepoints

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| B | 8 | E1 |  | This part of ISO/IEC 23001 specifies defines various code-points and fields which document aspects, that are bit-rate and compression independent, of a video or audio stream. They describe the characteristics of the signal before the signal is actually compressed by any encoder that is suitable for compressing such an input signal, or after decompressing the signal. |

## MMT Forward Error Correction Codes

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 10 |  |  | MMT defines several tools for error correction Such as Forward Error Correction (FEC) and retransmissions. A set of FEC codes is defined in 23008-10 that is shares a Common FEC framework. Additional codes may also be added . Some of the Currently defined FEC codes have enhanced support for Layered media |

## MMT Cross Layer Interface

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 1 | ? |  | MMT introduces the formats and procedures for Cross Layer Interfaces; thus, enabling Communication between the different protocol layers of an MMT entity or between MMT entities to exchange feedback about an ongoing MMT delivery session in a standardized way. This feedback information maybe faster and more accurate than end-to-end feedback information. |

## Uniform signalling for timeline alignment

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? | ? |  |  |  |

# IPMP

## Common Encryption Format for MPEG-2 Transport Stream

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| B | 9 |  |  | This format defines a way to encrypt media (audio, video, etc.) in files of the ISO base media file format family. By using a common encryption format, a single media asset can be used by several services and devices using different digital rights management systems, and the implementation complexity that would be consequent on having duplicate files and formats for the same content can be reduced or eliminated. |

## Common Encryption Format for ISO Base Media File Format

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| B | 7 |  |  | This format defines a way to encrypt media (audio, video, etc.) in files of the ISO base media file format family. By using a common encryption format, a single media asset can be used by several services and devices using different digital rights management systems, and the implementation complexity that would be consequent on having duplicate files and formats for the same content can be reduced or eliminated. |

## AES-CBC-128 and key rotation

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| DASH | 4 | E1 |  |  |

# Digital Item

# Transport and File formats

## MPEG-2 Systems DASH support

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 | 9 | 12264 | MPEG transport did not specify a profile as all the capabilities were signaled using the relevant bits in the headers. The recent development of streaming standards required signaling of a transport profile where some capabilities were limited. Second, stereoscopic MVC specifications did not associate the views with left or right eye display. This amendment specifies signaling of 'transport profiles' and extends the MVC descriptor to signal view to eye association. The amendment also includes an Annex to list the current mime types being used in various applications. |

## Simplified carriage of MPEG-4 over MPEG-2 TS

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 | 8 |  | Currently multimedia services based on ISO/IEC-14496-1 and ISO/IEC 14496-11 technologies cannot be played by ISO/IEC-14496-1 unaware players, in a backward compatible manner, even if the service uses video or audio components formats playable. Additionally, the carriage of ISO/IEC-14496-1 services over ISO/IEC 13818-1 uses, in some cases, inefficient signalling. This amendment to ISO/IEC 13818- provides mechanisms to use media components in backward compatible manner and improves the delivery efficiency of ISO/IEC-14496-1 multimedia services. |

## Enhanced audio support and other improvements

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 12 | 2 |  |  |

## Delivery of Timeline for External Data

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 | 6 |  | This amendment defines tools to identify and synchronize external data associated with an MPEG program in MPEG-2 transport streams. The tools allow: - alignment of media timelines regardless of PCR discontinuities through a variety of possible time codes, - signaling of URLs of associated data and their types (mime types, ISOBMFF, MPEG-DASH, MMT), - announcement of upcoming associated data |

## Signalling of Transport profiles and MVC stereo view association, and MIME type registration

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 | 2 |  | This amendment to MPEG-2 systems specifies 3 functions: It extends the MVC_extension_descriptor to explicitly signal the association between the 2 views of ‘stereoscopic MVC video’ with left or right eye for display on 3DTV devices. This explicit signaling was not available in earlier versions of MVC video standard or transport of MVC in MPEG-2 systems. A ‘transport profile descriptor’ is defined to signal ‘adaptive profile’ such as one used by the DASH specification. The descriptor also defines the ‘complete profile’ which is the current default transport profile. The descriptor is used at a program level to indicate that the program contains a transport stream that may have constraints associated with adaptive streaming applications so that re-purposing systems can properly manage the re-multiplexing of this transport stream. A new annex T that defines the ‘Mime types’ which are registered and commonly used for various MPEG defined elements has also been added. |

## Transport of MVC depth video and HEVC low delay

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 2 | 1 |  |  | This amendment specifies transport of MVC depth video sub-bitstream as defined in Annex I of ISO/IEC 14496-10 including association with other MVC sub-bitstreams. The amendment also adds the signaling (using HEVC video descriptor) to indicate use of HEVC low-delay coding mode in each access unit where the STD buffer management is performed using the HEVC HRD parameters. |

## Carriage of quality information in ISOBMFF

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 12 |  |  |  |

## Carriage of MVC+D in ISO Base Media File Format

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 12 |  |  | This amendment specifies the storage of video bitstreams consisting of multiple views and the associated depth, encoded based on Annex I of ISO/IEC 14496-10. The design is based on the MVC file format, which is specified in Clause 7 of ISO/IEC 14496-15, in a backwards-compatible manner. In the design, storage of the texture and depth of a particular view in either separate tracks or the same track is supported. The design also includes the signalling of various indications, such as the presence of texture and/or depth for each view, as well as whether the texture or depth component or both of a view is required for the presentation of another view. |

## Ordered combination of separate tracks

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 12 | ? |  | Tools describing in which order media tracks may be combined for decoding purposes, using implicit aggregation rules |

## Carriage of HEVC in ISO Base Media File Format

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 15 | 2 |  | This amendment of ISO/IEC 14496-15 specifies the storage format for HEVC (ISO/IEC 23008-2) video streams. The storage of HEVC content uses the existing capabilities of the ISO base media file format but also defines extensions to support the following features of the HEVC codec. Adaptation Parameter sets: decoding parameters that are supposed to change more frequently than coding parameters in picture parameter sets. Temporal scalability sample grouping: a structuring and grouping mechanism to indicate the association of access units with different hierarchy levels of temporal scalability. Temporal layer access sample grouping: a structuring and grouping mechanism to indicate the identification of access units as temporal layer access (TLA) samples. |

## Sample group and sub-track definitions for HEVC tiles

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 15 | 2 |  |  |

## Timed Text and Other Visual Overlays in ISO Base Media File Format associated

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 30 |  |  | 14496-30 is a new part to the ISO Base Media File Format series. It specifies the implementation of two timed text formats using 14496-12 Amendment 2 support for timed text tracks. It specifically addresses W3C TTML derivatives (including SMPTE Timed Text), and WebVTT formats. This provides an important supplement to the 14496-12 Amendment 2 additions to enable further industry interoperability. |

## DASH

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| DA | 1 | ? |  |  |

## MPEG-DASH Implementation Guidelines

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| DASH | 3 | 1st Ed |  | This technical report contains a set of guidelines for design and deployment of streaming media delivery systems using ISO/IEC 23009 (MPEG-DASH) standard. This includes guidelines for content generation, guidelines for client implementation, and examples of deployment scenarios. |

## Format independent segment encryption and authentication

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| DASH | 4 | E1 |  | MPEG DASH Segment Encryption and Authentication is a toolkit exactly for content protection. Conceptually, the standard consists of two separate frameworks: Segment Encryption and Segment Authentication. The Segment Encryption framework is built upon the concept of cryptoperiod. The Segment Authentication provides a toolkit for solving an often neglected problem of verifying the authenticity of the content viewed by a user. |

## MPEG Media Transport

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 1 | 1E | ? | In order to overcome current limitations of available standards in the area of media streaming, the development of a media aware client is envisioned in line with the MPEG philosophy of concentrating the work on the media client. Possible topics of work are: Transport- and file format friendly stream format Cross layer optimization between video and transport layer Error resilience for MPEG streams, Conversion between transport mechanisms Content adaptation to different networks. |

## Additional technologies for MPEG Media Transport

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 1 | 1 |  | xxx |

## MMT Implementation Guidelines

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 12 |  |  | The MMT Implementation Guidelines describe the usage of MMT for different media delivery scenarios. It describes the different functions that MMT provides and shows using examples how they can deployed separately or together to realize a media delivery service. |

# Multimedia architecture

## MPEG-M API

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| M | 2 | E3 |  | xxx |

## MPEG-V Architecture

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 1 | E2 |  | MPEG-V (Media context and control) provides an architecture and specifies associated information representations to enable interoperability between virtual worlds, e.g., digital content provider of a virtual world, (serious) gaming, simulation, and real and virtual worlds e.g., sensors, actuators, vision and rendering, robotics. The MPEG-V Part 1 specifies the Architecture of MPEG-V by specifying the components, APIs and use cases. |

# Application formats

## Surveillance Application Format

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 10 | E2 |  | A packaging format designed for the storage of video and audio content originating from surveillance cameras and microphones. It packages the media content together with associated metadata by using the appropriate file format definitions e.g. AVC file format. |

## Support of movie fragment structure for SVAF

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 11 | 3 |  | Stereoscopic Video AF (SVAF) provides information about composition type and transition between 2D and 3D view. This amendment is to provide a further investigation of said information in terms of movie fragment structure in order to enable delivery of SVAF content that is incrementally encapsulated. |

## Augmented Reality AF

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 13 | E2 |  | Augmented Reality Application Format (ARAF) is a collection of a subset of the ISO/IEC 14496-11 (MPEG-4 part 11) Scene Description and Application Engine standard, combined with other relevant MPEG standards (e.g. ISO/IEC 23005 - MPEG-V), designed to enable the consumption of 2D/3D multimedia content. Consequently, ISO/IEC 23000-13 focuses not on client or server procedures but on the data formats used to provide an augmented reality presentation. |

## Augmented Reality Reference Model

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 14 | E1 |  | The purpose of the Augmented Reality Reference Model (AR RM) is to state a vision, framework and terminology and to include multiple points of view for AR, including but not limited to 3D graphics, video, geospatial and other constructs. The AR RM contains different views Enterprise, Information, Computation and Engineering. It also includes the dictionary and use cases. |

## Multimedia Preservation

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 15 | E1 |  | The objective of the Multimedia Preservation Description Information (MPDI) framework is to provide a standardized description to multimedia content to enable users to plan, execute, and evaluate preservation operations to achieve the objectives of digital preservation. |

## Mixed and Augmented Reality Reference Model

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| ? |  |  |  | MAR (Mixed and Augmented Reality) reference model aims at defining the domain of mixed/augmented reality, the main concepts, various terms and their definitions, and an overall system architecture analyzed from various viewpoints, principles on which the document will be built. MAR reference model specifies a set of minimum functions and performance levels that should be supported by an MAR system. The reference model contains a list of possible use cases and their validation with respect to the architecture proposed by the reference model |

# Reference implementation

## MVC plus depth extension of AVC Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 5 | 33 |  | Provides a reference implementation of the MVC-plus-depth extension of AVC |

## Multi-resolution Frame Compatible Stereo Coding extension of AVC Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 5 | 34 |  | Provides a reference implementation of the MFC extension of AVC |

## Efficient representation of 3D meshes with multiple attributes Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 5 | 31 |  | Provides a reference implementation of Efficient representation of 3D meshes as defined in ISO/IEC 14496-16 AMD1. |

## Reference software multi-resolution 3D mesh compression

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 5 | 32 | 12417 | The purpose of the Augmented Reality Reference Model (AR RM) is to state a vision, framework and terminology and to include multiple points of view for AR, including but not limited to 3D graphics, video, geospatial and other constructs. The AR RM contains different views Enterprise, Information, Computation and Engineering. It also includes the dictionary and use cases. |

## CEL and MCO Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 21 | 8 | 1 |  | xxx |

## Surveillance Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 10 |  |  | xxx |

## SVAF Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 11 |  |  | xxx |

## IMAF Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 12 | 2 |  | xxx |

## ARAF reference software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 14 | 1 |  | ARAF Reference Software provides an implementation of the ARAF PROTOs. |

## Media Tool Library Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| C | 4 | 1 |  | This work provides VTL conformance testing and RVC simulation model (RSM). VTL conformance testing comprises of input/output patterns that can be used for testing FU-level conformance. The FU conformance testing is compliant to the VTL standard (ISO/IEC 23002-4:2010). RSM is the reference implementation of RVC framework defined from ISO/IEC 23001-4:2010 and ISO/IEC 23002-4:2010 |

## SAOC Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 2 | 2 |  | This is reference software for ISO/IEC 23003-2:2010, Spatial Audio Object Coding (SAOC). |

## USAC Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 2 | 2 | 12808 | This is the reference software implementation of the Unified Speech and Audio Coding (USAC) specification. The software consists of a normative decoder implementation and an informative implementation. The encoder implementation further consists of two separate branches: a monophonic-capable encoder that has been tested to have high performance and a second branch that is fully functional but of with untested performance. |

## MPEG-DASH Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 2 | 2 |  |  |

## MPEG-V – Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 5 |  |  | Provides the reference implementation of the XML and binary version of MPEG-V types |

## HEVC Reference Software

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 5 | E1 |  | Reference software for HEVC version 1 (23008-2) |

# Conformance

## Low Delay AAC v2 Profile Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 26 | 3 |  | This is conformance streams for the MPEG-4 Low Delay AAC v2 Profile technology. This profile consists of the tools: Error Resilient AAC Low Delay (ER AAC LD), Error Resilient AAC Enhanced Low Delay (ER AAC ELD), and Low Delay MPEG Surround (LD MPEG Surround) |

## MVC plus Depth Conformanceㅈㄷ

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 4 | 41 |  | Conformance bitstreams for the MVC plus depth extension (14496-10:2012/Amd.2) |

## Multi-resolution Frame Compatible Stereo Coding extension of AVC Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 4 | 42 | 13744 | Conformance bitstreams for the MFC extension of AVC (14496-10:2012/Amd.5) |

## 3D-AVC Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 4 |  |  | Conformance bitstreams for 3D AVC |

## 3D Efficient representation of 3D meshes with multiple attributes Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 27 | 4 |  | Provides the conformance data set for Efficient representation of 3D meshes as defined in ISO/IEC 14496-16 AMD1. |

## Multiresolution 3D mesh coding Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 27 | 5 | 12420 | Provides the conformance data set for Efficient representation of. |

## CEL and MCO Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| 21 | 14 | 1 |  | xxx |

## Surveillance Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 10 |  |  | xxx |

## SVAF Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 11 |  |  | xxx |

## IMAF Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 12 | 2 |  | xxx |

## ARAF Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| A | 14 | 1 |  | ARAF Conformance provides examples validating the ARAF PROTOS. The examples are encapsulated in MPEG-4 files which can be played by an ARAF player. |

## Media Tool Library Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| C | 4 | 1 |  | This work provides VTL conformance testing and RVC simulation model (RSM). VTL conformance testing comprises of input/output patterns that can be used for testing FU-level conformance. The FU conformance testing is compliant to the VTL standard (ISO/IEC 23002-4:2010). RSM is the reference implementation of RVC framework defined from ISO/IEC 23001-4:2010 and ISO/IEC 23002-4:2010 |

## MPEG Surround conformance for Low Delay AAC v2 profile

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 1 | 3 |  | This part of MPEG-4 Audio Conformance specifies the conformance tests for Low Delay AAC v2 profile applications, devices, and components. Since this profile comprises AAC, SBR and MPEG Surround coding tools, this work supplies conformance data for the AAC, Low Delay SBR and Low Delay MPEG Surround combination. |

## SAOC Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 2 | 1 |  | This part of SAOC specifies the conformance tests for SAOC applications, devices, and components. |

## USAC Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 2 | 2 |  | This part of USAC specifies the conformance tests for USAC applications, devices, and components. |

## MPEG-DASH Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| D | 2 | 2 |  |  |

## HEVC Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| H | 8 | 1 |  | Conformance bitstreams for HEVC version 1 (23008-2) |

## MPEG-V – Conformance

| Std | Pt | Amd | Req | Short description |
| --- | --- | --- | --- | --- |
| V | 4 |  |  | Provides the conformance of the XML and binary version of MPEG-V types. |

# Maintenance

## Systems coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
|  |  |  |  | Collection of defect reports and development of corrigenda in the systems coding area |

## Video coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
|  |  |  |  | Collection of defect reports and development of corrigenda in the video coding area |

## Audio coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
|  |  |  |  | Collection of defect reports and development of corrigenda in the audio coding area |

## 3DG coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
| 4 | 16 |  |  | Collection of defect reports and development of corrigenda in the 3DG coding area |

## Systems description coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
| 7 | 1 |  |  | Collection of defect reports and development of corrigenda in the systems description coding area |

## Visual description coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
| 7 | 3 |  |  | Collection of defect reports and development of corrigenda in the visual description coding area |

## Audio description coding standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
| 7 | 4 |  |  | Collection of defect reports and development of corrigenda in the audio description coding area |

## MPEG-21 standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
| 21 |  |  |  | Collection of defect reports and development of corrigenda for MPEG-21 standards |

## MPEG-A standards

| Std | Pt | Cor | Req | Short description |
| --- | --- | --- | --- | --- |
| A |  |  |  | Collection of defect reports and development of corrigenda for multimedia application standards |

# Work plan and time line

| Std | Pt | Edit. | Status | Description | CfP | WD | CD | DIS | FDIS | Gr. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 1 | 201x | A3 | Transport of HEVC video over MPEG-2 systems |  |  |  | 12/10 | 13/08 | S |
| 2 | 1 | 201x | A4 | Support for event signalling in MPEG-2 TS |  |  |  | 13/01 | 13/08 | S |
| 2 | 1 | 201x | A5 | Transport of MVC depth video sub-bitstream and extensions to support HEVC low delay coding mode |  |  |  | 13/08 | 13/10 | S |
| 4 | 1 | 2010 | A2 | Support for raw audio-visual data |  |  | 12/05 | 12/10 | 13/08 | S |
| 4 | 2 | 2004 | C5 | Rounding operation |  |  |  |  | 13/08 | V |
| 4 | 3 | 2009 | A4 | New levels for AAC profiles |  |  |  |  | 13/08 | A |
| 4 | 4 | 2004 | A41 | Conformance testing of the MVC + depth extension of AVC |  |  | 13/01 | 13/04 | 13/11 | 3V |
| 4 | 4 | 2004 | A42 | Conformance testing of MFC |  |  | 13/08 | 13/11 | 14/04 | 3V |
| 4 | 5 | 2001 | A24/C2 | AAC RS Corr. |  |  | 13/04 |  | 13/08 | A |
| 4 | 5 | 2001 | A32 | RS multi-resolution 3D mesh compression |  | 11/12 | 13/01 | 13/04 | 13/11 | 3 |
| 4 | 5 | 2001 | A33 | RS for the MVC + depth extension of AVC |  |  | 13/04 | 13/11 | 14/04 | 3V |
| 4 | 5 | 2001 | A34 | RS for the MFC |  |  | 13/08 | 13/11 | 14/04 | 3V |
| 4 | 10 | 2012 | C1 | Substream extraction |  |  | 13/01 |  | 13/08 | V |
| 4 | 10 | 2012 | A3 | AVC compatible video-plus-depth extension |  |  | 12/10 | 13/04 | 13/11 | 3V |
| 4 | 10 | 2012 | A4 | Additional Colour Space and Tone Mapping Descriptors |  |  | 13/01 | 13/04 | 13/11 | V |
| 4 | 10 | 2012 | A5 | Multi-resolution Frame Compatible Stereo Coding |  |  | 13/01 | 13/04 | 13/11 | 3V |
| 4 | 11 | 201x | E2 | Scene description and application engine | 11/12 | 12/02 | 13/04 | 13/08 | 14/01 | S |
| 4 | 12 | 2012 | C1 | Minor corrections |  |  | 13/01 |  | 13/08 | S |
| 4 | 12 | 2012 | A2 | Carriage of timed text and other visual overlays |  |  | 12/07 | 13/01 | 13/08 | S |
| 4 | 12 | 2012 | A3 | Enhanced audio support and other improvements |  |  |  | 13/08 | 14/04 | S |
| 4 | 15 | 2010 | A2 | Carriage of high-efficiency video coding (HEVC) |  |  | 12/05 | 13/04 | 13/08 | S |
| 4 | 15 | 201X | E3 | Carriage of NAL unit structured video in the ISO Base Media File Format |  |  |  |  |  |  |
| 4 | 16 | 2011 | A2 | Multi-resolution 3D mesh compression |  | 11/01 | 11/07 | 13/01 | 13/08 | 3 |
| 4 | 16 | 2011 | A3 | Web3DG coding |  |  | 13/11 | 14/01 | 14/07 | 3 |
| 4 | 18 | 2004 | A1 | Font handler |  |  | 13/04 | 13/10 | 14/04 | S |
| 4 | 22 | 201x | E3 | Open font format | 13/08 | 13/11 | 14/01 | 14/04 | 14/10 | S |
| 4 | 26 | 2010 | C7 |  |  |  | 13/04 |  | 13/08 | A |
| 4 | 26 | 2010 | A3 | C for Low Delay AAC v2 profile |  |  | 12/07 | 13/01 | 13/08 | A |
| 4 | 27 | 2009 | A5 | C for multi-resolution 3D mesh compression |  |  | 13/01 | 13/04 | 13/11 | 3 |
| 4 | 28 | 2012 | C1 | Naming corrections |  |  | 13/01 |  | 13/08 | S |
| 4 | 29 | 201x | E1 | Web video coding |  | 11/12 | 12/05 | 13/04 | 13/11 | V |
| 4 | 30 | 201x | E1 | Timed text and other visual overlays in ISO base media file format |  |  | 12/10 | 13/01 | 13/08 | S |
| 7 | 13 | 201x | E1 | Compact descriptors for visual search |  | 12/07 | 13/11 | 14/01 | 14/07 | V |
| 21 | 8 | 2008 | A3 | CEL and MCO RS |  |  | 13/01 | 13/08 | 14/04 | S |
| A | 10 | 2012 | A1 | Conformance and reference software |  |  | 13/01 | 13/04 | 13/11 | S |
| A | 11 | 2009 | A3 | Support of movie fragment for SV AF |  |  | 13/01 | 13/04 | 13/11 | S |
| A | 13 | 201x | E1 | ARAF |  | 11/12 | 12/05 | 12/10 | 13/08 | 3 |
| A | 13 | 201x | A1 | ARAF RS & C |  |  | 13/01 | 13/04 | 13/11 | 3 |
| A | 14 | 201x | E1 | ARRM |  |  | 12/10 |  | 14/01 | 3 |
| A | 15 | 201x | E1 | MPAF |  | 13/04 | 13/11 | 14/04 | 14/10 | S |
| B | 7 | 2012 | E2 | Common Encryption for ISOBMFF Files |  |  | 13/04 | 13/08 | 14/01 | S |
| B | 9 | 201x | E1 | Common encryption for MPEG-2 TS |  |  | 12/10 | 13/04 | 13/11 | S |
| C | 4 | 2010 | A3 | GTL for RMC framework |  | 11/03 | 12/02 | 13/04 | 13/11 | 3 |
| C | 4 | 201x | A2 | FU and FN descriptions for HEVC |  |  | 13/04 | 13/11 | 14/04 | V |
| C | 5 | 201x | A1 | GTL RS & C |  | 12/02 | 12/10 | 13/08 | 14/01 | 3 |
| D | 1 | 2007 | A2/C4 | RS corrections |  |  | 13/01 |  | 13/08 | A |
| D | 3 | 2012 | C2 | USAC corrections |  |  | 13/01 |  | 13/08 | A |
| V | 1 | 201x | E3 | Architecture |  |  | 13/11 | 14/01 | 14/07 | 3 |
| V | 2 | 201x | E3 | Control information |  |  | 13/11 | 14/01 | 14/07 | 3 |
| V | 3 | 201x | C1 | Data type corrections |  |  | 13/01 |  | 13/08 | 3 |
| V | 3 | 201x | E3 | Sensory information |  |  | 13/11 | 14/01 | 14/07 | 3 |
| V | 4 | 201x | E3 | Virtual world object characteristics |  |  | 13/11 | 14/01 | 14/07 | 3 |
| V | 5 | 201x | E3 | Data formats for interaction devices |  |  | 13/11 | 14/01 | 14/07 | 3 |
| V | 6 | 201x | E3 | Common types and tools |  |  | 13/11 | 14/01 | 14/07 | 3 |
| V | 7 | 201x | E2 | C & RS |  | 11/12 | 12/02 | 12/07 | 13/08 | 3 |
| U | 1 | 2011 | C2 | Minor corrections |  |  | 13/04 |  | 13/11 | S |
| U | 3 | 2011 | A1 | C & RS for widget extention and AUI |  | 12/02 | 12/05 | 13/04 | 13/11 | S |
| H | 1 | 201x | E1 | MMT | 10/10 | 11/03 | 12/07 | 13/04 | 13/11 | S |
| H |  | 201x | A1 | Additional MMT technologies |  |  | 13/04 | 13/08 | 14/04 | S |
| H | 2 | 201x | A1 | HEVC Range ext. |  |  | 13/01 | 13/08 | 14/01 | VC |
| H | 2 | 201x | A2 | HEVC Multiview |  |  | 13/01 | 13/08 | 14/01 | 3V |
| H | 2 | 201x | A3 | HEVC Scalability |  |  | 13/08 | 14/01 | 14/07 | VC |
| H | 3 | 201x | E1 | 3D Audio | 13/01 | 13/11 | 14/04 | 14/07 | 15/01 | A |
| H | 4 | 201x | E1 | MMT RS |  | 13/11 | 14/04 | 14/07 | 15/01 | S |
| H | 5 | 201x | E1 | HEVC RS |  |  | 13/01 | 13/08 | 14/01 | VC |
| H | 6 | 201x | E1 | 3D Audio RS |  |  | 15/04 | 15/07 | 16/01 | A |
| H | 7 | 201x | E1 | MMT Conformance |  | 13/11 | 14/04 | 14/07 | 15/01 | S |
| H | 8 | 201x | E1 | HEVC Conformance |  |  |  | 13/08 | 14/01 | VC |
| H | 9 | 201x | E1 | 3D Audio Conf. |  |  | 15/04 | 15/07 | 16/01 | A |
| H | 10 | 201x | E1 | MMT FEC |  |  | 12/07 | 13/08 | 14/01 | S |
| H | 11 | 201x | E1 | MMT CI |  |  | 13/08 | 13/11 | 14/04 | S |
| H | 12 | 201x | E1 | MMT implementation guidelines |  | 13/01 | 13/11 | 14/01 | 14/07 | S |
| DA | 1 | 2012 | A1 | Support for Event Messages and ... |  |  |  |  | 13/08 | S |
| DA | 2 | 201x | E1 | C & RS |  |  | 12/05 | 12/10 | 13/08 | S |
| DA | 3 | 201x | E1 | Implementation guidelines |  |  | 12/07 |  | 13/08 | S |